| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC8.0 (WG4 at TP#9) |
| Title:* | SEC CSF Authorization Description Update for Security TS |
| Source:* | CATT |
| Contact: | Wei Zhou, zhouwei@catt.cn Hui Xu, xuhui@catt.cn |
| Date:* | 2014-02-17 |
| Abstract:* | This contribution aims to replace some text and figures related to authorization description. |
| Agenda Item:* | Security TS |
| Work item(s): | WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To add the proposed text into the TS document |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

This contribution aims to provide authorization architecture and authorization call flow. This content should be in a new section that does not currently exist.

2	Proposal

-----------------------Start of 1st   change-------------------------------

## 2.2	Informative references

[x.1]	eXtensible Access Control Markup Language (XACML) Version 3.0. 22 January 2013. OASIS Standard.

-----------------------End of 1st  change-------------------------------

-----------------------Start of 2nd   change-------------------------------

## 3.1	Definitions

Policy Access Point: The system entity that finds applicable policy or policy set.

Policy Decision Point [x.1]: The system entity that evaluates applicable policy and renders an authorization decision.

Policy Enforcement Point [x.1]: The system entity that performs access control, by making decision requests and enforcing authorization decisions.

Policy Information Point [x.1]: The system entity that acts as a source of attribute values.

-----------------------End of 2nd  change-------------------------------

-----------------------Start of 3rd   change-------------------------------

## 3.4	Acronyms

PAP	Policy Access Point

PDP	Policy Decision Point

PEP	Policy Enforcement Point

PIP	Policy Information Point

-----------------------End of 3rd  change-------------------------------

-----------------------Start of 4th   change-------------------------------

#### x.x.x	Authorization Architecture

The following figure provides a high level overview of the authorization architecture. This architecture comprises four subcomponents that are described as follows:

- Policy Enforcement Point (PEP)

PEP intercepts resource access requests, makes access control decision requests, and enforces access control decisions. The PEP coexists with the CSFs that need authorization services.

- Policy Decision Point (PDP)

PDP interacts with the PAP and PIP to get applicable authorization polices and attributes needed for evaluating authorization policies respectively, and then evaluates access request using authorization policies for rendering an access control decision. The PDP is located in the Authorization component of SEC CSF.

- Policy Access Point (PAP)

PAP obtains applicable authorization policies according to an access control decision request. These applicable policies should be combined in order to get a finial access control decision. These authorization policies may belong to different access control mechanisms, or written in different authorization languages. The PAP is located in the Authorization component of SEC CSF.

- Policy Information Point (PIP)

PIP provides attributes that are needed for evaluating authorization policies, for example IP address of the requester, creation time of the resource, current time or location information of the requester. The PIP is located in the Authorization component of SEC CSF.

The SEC CSF Authorization component may comprise any of the subcomponents: PDP, PAP and/or PIP. It means that the subcomponents PEP, PAP, PDP and PIP could be distributed across different nodes. For example the PEP is located in an ASN/MN and the PDP is located in the IN.

Note: Release 1 does not support separation of PAP and PIP on different CSE from PDP.

-----------------------End of 4th  change-------------------------------