| Doc# oneM2M-SEC-2014-0047R01-Key_hierarchy Input Contribution |  |
| --- | --- |

| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 (SEC) Meeting during TP#9 |
| Title:* | SEC CSF key hierarchy |
| Source:* | Morpho Cards GmbH, Gemalto |
| Contact: | Oleg Krainioukov (oleg.krainioukov@morpho.com) Mireille Pauliac (mireille.pauliac@gemalto.com) |
| Date:* | 2014-02-03 |
| Abstract:* | This contribution proposes to add Key Hierarchy for oneM2M SEC CSF (Chapter 5.3). It is based on Version 0.3.0 of TS-0003 as available on the portal. R01 describes a key management with no longer hierarchy aspects. The term “M2M Root Key” is replaced with “M2M Long Term Key” |
| Agenda Item:* | TBD |
| Work item(s): | WI 0007 - oneM2M Security Analysis |
| Document(s) Impacted* | oneM2M-TS-0003 Security Solutions TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to include the changes proposed in revision marks in this input contribution to the Security Solutions TS |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Addition of a new text to section 5.3:

### 5.3.x	Key management and realisation

#### 5.3.x.1	Description of oneM2M keys

The following keys are used for different levels of Authentication and Authorization within the Security CSF:

M2M Long Term Key

This key shall be used for mutual authentication and key agreement between CSEs, for example between IN-CSE and MN-CSE. The M2M Long Term Key shall be coupled with a unique CSE and CSE-ID identifier, and may be bootstrapped in the Security CSF of a CSE in various different ways, depending on the trust relationships between different stakeholders in the M2M ecosystem. One M2M Long Term Key exists for each set of provisioned CSE credentials. IN IN-CSE, M2M Long Term Key shall be stored within MAF.

In scenarios where the M2M Service Provider and the Access Network Provider have a trust relationship (including the case that they are actually the same entity), access network credentials may be used as M2M Long Term Key.

M2M Connection Key

.

The M2M Connection Key is used as symmetric shared secret for setting up secure data sessions between CSEs. The M2M Connection Key shall expire upon termination of the corresponding Service Connection. A different M2M Connection Key shall be generated for every new M2M Security association procedure of the CSE with the same or a different IN-CSE.

M2M Application Key

There shall be one M2M Application Key per AE. An M2M Application Key is shared between AE and respective CSE. The M2M Application Key should be used for authentication of an AE by the Security CSF in the CSE and for protection of application data traffic.

In Field Domain, all key material shall be stored within the secure storage service of the Security CSF.

#### 5.3.x.2	M2M Long Term Key Provisioning

The following scenarios are supported by the oneM2M architecture:

1)	Pre-provisioning

The M2M Long Term Key may be securely provisioned during manufacturing or deployment. The M2M Long Term Key should be securely stored inside the Security CSF of the M2M device or one of its components (e.g., in UICC independently from the Network Access Application). In these cases, the M2M Service Provider is responsible for ensuring that M2M Nodes are provided with necessary M2M Long Term Keys using mechanisms that are not specified in the present document.

2)	Access Network based Bootstrapping

The Security CSF may leverage key material that is derived from Access Network credentials, and use that key material to provision the M2M Long Term Key in the Security CSF of a CSE.

3)	Access Network independent Bootstrapping

M2M Long Term Key may be provisioned in the Security CSF in an access-network independent procedure. This scenario is applicable when the Access Network Operator and the M2M Service Provider do not share a business relationship and/or do not wish to use Access Network Credentials for bootstrapping of Service Layer credentials.

For options 1 and 3 there may be no need for Access Network Credentials, depending on the access network technology used.