| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 (SEC) at TP#9 |
| Title:* | Briefing Flows for Security TS |
| Source:* | Phil Hawkes, Qualcomm , phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Contact: | As above |
| Date:* | 2014-02-18 |
| Abstract:* | The purpose of the briefing resource is to allow deploying off-the-shelf Field Domain Nodes without directly configuring the Field Domain Nodes. This contribution provides some attachment flows incorporating briefing procedures |
| Agenda Item:* | Contributions impacting ARC TS-0001 |
| Work item(s): | ARC WI-0002, SEC WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) and Architecture TS (TS-0001) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG4 member should discuss on this topic, and determines final forms to be included as part of Security TS and/or Architecture TS. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

This contribution provides some attachment flows incorporating briefing procedures. This contribution follows on from the contribution titled “Attachment Flow Diagrams for Security TS” – the “Attachment Flow Diagrams…” contribution should be read first.

The authors have also submitted a contribution to the WG2 (ARC) titled “Briefing Resource and Procedures” which provides specification for the <briefing> resource and corresponding procedures.

==================<Start of Change 1 (New Text) >=================

x.y.9 Briefing

#### x.y.9.1	Motivation for Briefing

For a Registree (CSE/AE) in a Field Domain Node, it may not be possible to preconfigure (or manually reconfigure) Registree with the CSE_ID of the Registrar with which the Registree should register to obtain M2M Services. The <briefing> resource provides a mechanism for conveying such details. The details are provided to a Registrar whose identity is already known to the Registree, and with whom the Registree can perform mutual authentication (the means for providing such details is not described in these specifications). The Registree retrieves the <briefing> resource from this first Registrar, and subsequently authenticates and registers with the Registrar identified in the <briefing> resource. The <briefing> resource may also contain other parameters facilitating mutual authentication of the Registree with the Registrar identified in the <briefing> resource.

For the purposes of this discussion, the first Registrar is said to plays the role of a Briefing Registrar,  while the second Registrar (Identified in the <briefing> resource) plays the role of the Target Registrar.

There are two main scenarios motivating this feature:

- One purpose is remotely configuring a Registree in an (un-configured) off-the-shelf Field Domain Node to obtain M2M service from a target Registrar of the M2M Subscriber’s choosing. In this case, the Registree is pre-configured with a Briefing Registrar’s details, and the Registree will attach to Briefing Registrar for the express purpose of retrieving the <briefing> resource from the Briefing Registrar. The M2M Subscriber provides the details for the Target Registrar to the Briefing Registrar.  During start up, the Registree first attaches to the Briefing Registrar and retrieves the <briefing> resource. Then the CSE/AE authenticates and registers with the Target Registrar (identified in the <briefing> resource) using the information in the <briefing> resource.

The Briefing Registrar provides the “briefing” service to the M2M Subscriber associated with the Registree. There is no need for any arrangement between the Briefing Registrar and the target Registrar identified in the <briefing> resource.

Here are two examples of the off-the-shelf Field Domain Node scenario:

- Example A. A device manufacturer may provide a Briefing Registrar for the devices that it manufactures, or alternatively a third party could provide a Briefing Registrar on behalf of the device manufacturer. The manufacturer preconfigures the device with the Briefing Registrar’s CSE_ID and any authentication-mechanism-specific parameters needed for mutual authentication with the Briefing Registrar (e.g. root certificates). Device owners can provide the Briefing Registrar with the Target Registrar CSE_ID and any other authentication-mechanism-specific parameters. The Registree (CSE/AE) in the device are pre-configured to authenticate and register to the Briefing Registrar once the Registree is initiated. The Registree then retrieves (from the Briefing Registrar) the <briefing> resource containing the Target Registrar CSE_ID and any other authentication-mechanism-specific parameters. The Registree then authenticates and registers with the Target Registrar identified in the <briefing> resource.

- Example B:An Underlying Network Service Provider may provide a Briefing Registrar for the its Underlying Network Service Subscribers. The Underlying Network Service Provider ensures that their UICC/UIM are pre-configured with the Briefing Registrar’s CSE_ID and any authentication-mechanism-specific parameters needed for mutual authentication with the Briefing Registrar (e.g. root certificates). Device owners can provide the Briefing Registrar with the Target Registrar CSE_ID and any other authentication-mechanism-specific parameters. The Briefing Registrar CSE_ID is retrieved from the UICC/UIM during the device-start-up process.  The Registree (CSE/AE) in the device are pre-configured to authenticate and register to this Briefing Registrar once the Registree is initiated. The Registree then retrieves (from the Briefing Registrar) the <briefing> resource containing the Target Registrar CSE_ID and any other authentication-mechanism-specific parameters. The Registree then authenticates and registers with the Target Registrar identified in the <briefing> resource.

- Another purpose is allowing a first Registrar (to which the Registree is currently registered and obtaining M2M service) to provide the details of a second Registrar to which the Registree should authenticate and register for M2M Service.

- Here are two examples of this scenario:

- Example C: both Registrars may be operated by a single M2M Service Provider, and the M2M Service Provider wishes the Registree to migrate to a different Registrar for any number of reasons (e.g. the Registree may have moved location and Registree closer to the new location would be more appropriate). The Registree creates a subscription to the <briefing> resource after registration to the first Registrar. At a later time, the M2M SP determines that it wishes to migrate the Registree to another Registrar and (with permission of the M2M Service Subscriber) updates the <briefing> resource for the Registree (hosted on the first Registrar).. The Registree is notified that the <briefing> resource has been updated and the Registree retrieves the <briefing> resource to obtain the details for the second Registrar. The Registree then authenticates and registers to the second Registrar.

- Example D: The two Registrars may be operated by distinct M2M Service Providers, and the M2M Service Subscriber wishes to migrate the Registree to the second Registrar (for example, if the M2M Service Subscriber’s contract with the first M2M Service Provider of the first Registrar is ending, and the M2M Service Subscriber is starting a contract with the M2M Service Provider of the second Registrar). As in the above example, Registree creates a subscription to the <briefing> resource after registration to the first Registrar. At a later time, the M2M Service Subscriber updates the <briefing> resource for the Registree (hosted on the first Registrar). The Registree is notified that the <briefing> resource has been updated and the Registree retrieves the <briefing> resource to obtain the details for the second Registrar. The Registree then authenticates and registers to the second Registrar.

In the first case (remotely configuring CSE/AE of an off-the-shelf Field Domain Node), the Attachment of the Registree to the Registrar providing the M2M Service typically involves Attachment of the Registree to the Briefing Server followed, retrieving the <briefing> resource, and Attachment of the Registree to the target Registrar providing the M2M Service. That is, the Registree performs two Attachments. In the first case, the Briefing procedure would typically only be used once to direct the Registree to the correct Registrar, and after that the Briefing procedure would not be invoked again.

In an initial attachment, briefing would occur at step/phase 2 (see Clause x.y.1 “Generic Sequence of Events for Attachment Flows”). Note that the Briefing procedure requires authenticating to the “Briefing” Registrar, so the authentication and registration to the “Briefing” Registrar occurs in step/phase 2 of the Initial attachment for the Target Registrar.

The <briefing> resource and associated is specified in the oneM2M Architecture TS [TS-0001]. The following clauses show examples of how briefing procedures are incorporated with (a) PKI and Client Authentication, and (b) PKI and Token Authentication.

- Brown text highlights briefing-related details.

#### x.y.9.2	Briefing with PKI  and Client Certificate Authentication

The Briefing Registrar Root Certificate is a root certificate to which the Briefing Registrar’s Certificate will chain. This specification does not constrain who is the owner of the Briefing Root Certificate.

The Target Registrar Root Certificate is a root certificate to which the Target Registrar’s Certificate will chain. This specification does not constrain who is the owner of the Target Root Certificate.

#### x.y.9.3	Briefing with PKI and Token Authentication

The Briefing Registrar Root Certificate is a root certificate to which the Briefing Registrar’s Certificate will chain. This specification does not constrain who is the owner of the Briefing Root Certificate.

The Target Registrar Root Certificate is a root certificate to which the Target Registrar’s Certificate will chain. This specification does not constrain who is the owner of the Target Root Certificate.