| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 (SEC) |
| Title:* | MAS and MTF description |
| Source:* | Gemalto (ETSI), Oberthur Technologies (ETSI) |
| Contact: | Mireille Pauliac, Gemalto, mireille.pauliac@gemalto.com Dragan Vujcic, Oberthur Technologies, v.dragan@oberthur.com |
| Date:* | 2014-02-07 |
| Abstract:* | This contribution proposes a description of two specific functionalities required for oneM2M security. R01 distinguishes an additional M2M security function related to authorization aspects. |
| Agenda Item:* | Contributions impacting ARC TS-0001 |
| Work item(s): | ARC WI-0002, SEC WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) and Architecture TS (TS-0001) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG4 member should discuss on this topic, and determines final forms to be included as part of Security TS and/or Architecture TS. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

OneM2M security requires the presence of three specific security functionalities within the Service Domain: the M2M Authentication Function (MAF), the M2M Enrolment Function (MEF), and the M2M Authorization Function (MZF).

This contribution proposes below a description of those three functionalities within new sub-clause of SEC TS-0003. A description should also be available in ARC TS-0001.

6.3.x	 Sensitive Data Handling

x.x.1 Specific servers in Service Domain

OneM2M security requires the presence of three specific security functionalities within the Service Domain: the M2M Authentication Function (MAF), the M2M Enrolment Function (MEF) and the M2M Authorization Function (MZF). They can be either under M2M Service Provider control or delegated to a M2M Trust Enabler.

- M2M  Enrolment Function (MEF)

The MEF aims at enabling security procedures involving CSE or AE of Nodes. In case of M2M Security Remote Provisioning procedure, the MEF provides the M2M Root Key both to the MAF and the SEC CSF of ASN/MN-CSE.

- M2M Authentication Function (MAF)

M2M Root Keys used to authenticate M2M Nodes are long term secret keys that shall be securely stored. M2M Root Keys are securely stored in a specific infrastructure functionality named M2M Authentication Function (MAF).

The MAF securely contains the set of M2M Root keys that are used for authenticating CSEs/AEs that have been enrolled for M2M services. The MAF stores both the M2M Root keys and associated ASN/MN-CSE IDs and/or AE-IDs. The MAF is identified thanks to its MAF-ID.

When M2M Security Remote Provisioning procedure takes place to share a M2M Root Key between an ASN/MN CSE and the M2M Authentication Function, the M2M Enrolment Function (MEF) communicates with the MAF through an appropriate interface (e.g. DIAMETER if not co-located in same entity).

The MAF is also in charge of all security operations involving the usage of the M2M Root Keys. Consequently, the MAF derives from the M2M Root Keys the M2M Security Association Keys to be used in M2M Security Association Establishment procedure.

- M2M Authorization Function (MZF)

The MAZ is in charge of authorization aspects.