| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2 ARC at TP#9 |
| Title:* | Security alignments on M2M Identifiers |
| Source:* | WG4 |
| Contact: | francois.ennesser@gemalto.com |
| Date:* | 2014-02-18 |
| Abstract:* | This contribution proposes clarifications and security alignments on M2M identifiers. |
| Agenda Item:* | To be defined |
| Work item(s): | WI 0002 - oneM2M Architecture |
| Document(s) Impacted* | oneM2M-TS-0001 Technical Specification - M2M Architecture (v0.3.2) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to incorporate this text into the TS (oneM2M-TS-0001) |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

- Introduction

This contribution proposes to change:

- Assignment of App-Inst-ID: Since such an identifier is needed for Security Context Establishment which takes place before registration, it could be created

  - On a provisioned node, when a new application is instantiated into an AE

  - Or when a Node gets provisioned for M2M Services, if it already contained instantiated AE

  - Or as a result of service provisioning

- Assignment of CSE-ID for field nodes: This identifier is also needed for Security Context Establishment which takes place before registration, therefore we propose that it gets provisioned (which covers both pre-provisioning and remote provisioning (online bootstrapping) procedures.

- M2M Node Identifier: This is a pre-provisioned identifier which is used for provisioning (pre-provisioning or online bootstrapping) procedures. Since it is pre-provisioned, it cannot always be assigned by the M2M SP, it is typically assigned by a manufacturer, which can be summarized as an out of scope stakeholder.

Though no change is proposed by WG4 on the matter, the identifier App-ID is not included in the current table: Is there a reason?

- Proposed change

Inside the TS, Table 7.2.1:

## 7.2	M2M Identifiers lifecycle and characteristics

Table 7.2-1: M2M Identifiers lifecycle and characteristics

| Identifier | Assigned by | Assigned to | Assigned during | Lifetime | Uniqueness | Used during | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- |
| M2M Service Provider Identifier | Out of scope | AE, CSE | Out of scope | Out of scope | Global | FFS |  |
| Application Instance Identifier | FFS | AE | Security Provisioning or AE instantiation | Application Instance Registration | Global | - Application instance Registration - Security Context Establishment - Other operations FFS | Need to satisfy security requirements |
| CSE Identifier | M2M SP | CSE | Security Provisioning | Life of the CSE | Global | - Information flows (section 10) - Security Context Establishment | Need to satisfy security requirements |
| M2M Node Identifier | Out of scope | M2M Node hosting CSE | Pre-provisioned | Life of the M2M Node | Global | Security provisioning | Needs to be Read Only |
| M2M Subscription Identifier | M2M SP | Application Entities, and one or more CSEs belonging to the same M2M subscriber | At service signup | Life of the Subscription with the MM SP | Global | - Charging and Information Recorded - Other operations are FFS | Multiple CSEs can be allocated the same M2M Subscription Identifier |
| M2M-Request-ID | Mcc: CSE Mca: Application Instance | A request initiated by an AE or CSE | Mcc: When a request is initiated by a CSE, or handling of a request received by a CSE. Mca: When a request is initiated by an AE | Equal to the lifetime of the Request and its corresponding Response | Mcc: Global Mca: Local or global | Requests and corresponding responses |  |
| External Identifier | Manual mode: Jointly between the Underlying Network provider and M2M SP, where applicable. Plug-And- Play: FFS | M2M Node belonging to a CSE that wants to utilize services of the Underlying Network. | Manual Mode: Administrative Agreement. Plug-And- Play: FFS | Life time of the CSE. | FFS | Requests initiated by a CSE over the Interface, where applicable. |  |

================== End of 1st Change ======================