| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2(ARC)/WG4(SEC) |
| Title:* | serviceUse resource on m2mServiceSubscription resource. |
| Source:* | FUJITSU |
| Contact: | Shingo Fujimoto, FUJITSU, shingo_fujimoto@jp.fujitsu.com |
| Date:* | 2014-02-19 |
| Abstract:* | This contribution proposed to add new resource named ‘Authorization’. Authorization resource accepts the authorization requests from AE or CSE. |
| Agenda Item:* | Access Control |
| Work item(s): | WI-0002(arc)/WI-0007(sec) |
| Document(s) Impacted* | TS-0001 (Arch-TS) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG member should agree on proposal. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

‘Authorization’ should be requested by AE or CSE which is allowed to authorize another principal to access the resource with scope.

m2mServiceSubscription resource should be used to manage the such a authorization, but even serviceId, nodeId, and App-Inst-ID are provided, that cannot support the third party authorization (ex. OAuth).

Additionally, if the application is accessing the resource through Mcc’(e.g. AE is sitting in other administrative domain), the hosting CSE cannot authenticate such AE.

This contribution proposed to modify the m2mServiceSubscription to solve the issue..

---- Start of  proposed change ---

### 9.6.20	Resource Type m2mServiceSubscription

This resource represents status of M2M Service Subscription. It is used to configure node to accept requests from specific AE-Instance regarding use of M2M service.

Editor’s Note: The link between the M2M Service Subscription resource and RBAC will be added once RBAC is included in the specification.

Figure 9.6.20-1: Structure of <m2mServiceSubscription> resource 
(only resource specific attributes are shown)

Editor’s Note: The actual node resource shall include information such as, extID, profile, device specific ID if applicable and link to CSE and Applications running on the node.

Editor’s Note: the M2M-Sub-ID storage is FFS

This resource shall contain the child resources according to their multiplicitly in Table 9.6.19-1 (0 indicates the optionality of the child resource).

Table 9.6.20 -1: Child resources of <m2mServiceSubscription> resource

| Child Resource Name of <remoteCSE> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <ServiceUse> | 0..n | See section 9.6.x. |

The <m2mServiceSubscription> resource shall contain the attributes described in Table 9.6.20-2.

Table 9.6.20-2: Attributes of <m2mServiceSubscription> resource

| Attribute Name of <m2mServiceSubscription> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| parentID (pID) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID (aRI) | 0..1 | RW | See section 9.6.1 where this common attribute is described. If no accessRightID is given at the time of creation, the accessRightID of the parent resource is linked to this attribute |
| creationTime (cT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| creator (cr) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |

--- End of proposed change ---

--- Start of proposed adding ---

### 9.6.x	Resource Type serviceUse

This resource represents an use of M2M Service Subscription.

Figure 9.6.x-1: Structure of <serviceUse > resource 
(only resource specific attributes are shown)

The <serviceUse> resource shall contain the attributes described in Table 9.6.x-1.

Table 9.6.x-1: Attributes of <serviceUse> resource

| Attribute Name of <m2mServiceSubscription> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| parentID (pID) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID (aRI) | 0..1 | RW | See section 9.6.1 where this common attribute is described. If no accessRightID is given at the time of creation, the accessRightID of the parent resource is linked to this attribute |
| creationTime (cT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| creator (cr) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| nodeId | 1 | RW | Identifier of a node pertaining to the M2M Service Subscription. The node identifier is specified in section 7.1.5 . The nodeId attributes link to the actual node resource that provides information pertaining to the node such as the external identifier, etc. |
| serviceId | 1 | RW | This attribute indicates the unique ID of the service being subscribed to. A service provider can define its own services. |
| App-Inst-ID | 1 | RW | Identifier of an application instance identifier as defined in section 7.1.2. It shall link to an application resource. |
| accessCredential | 0..1 | WO | The credential data will be set if the credential data is required to be shared with AE and hosting CSE. |

---End of proposed adding