| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG2(ARC)/WG4(SEC) |
| Title:* | Service Access Credential |
| Source:* | FUJITSU |
| Contact: | Shingo Fujimoto, FUJITSU, shingo_fujimoto@jp.fujitsu.com |
| Date:* | 2014-02-19 |
| Abstract:* | Service Access Credential should be managed with M2M Service Subscriptions. This contribute propose to add new attribute on nodeInfo sub-resource at m2mServiceSubscription. |
| Agenda Item:* | Access Control |
| Work item(s): | WI-0002(arc)/WI-0007(sec) |
| Document(s) Impacted* | TS-0001 (Arch-TS) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG4 member should agree to present this proposal at WG2. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Service Access Credential should be managed with M2M Service Subscriptions.

This contribute propose to add new attribute on nodeInfo sub-resource at m2mServiceSubscription.

--- start of change ---

### 9.6.20	Resource Type nodeInfo

This resource represents M2M node information that is needed as part of the M2M Service Subscription resource. It shall contain information about the node as well as application identifiers running on that node.

Figure 9.6.20-1: Structure of <nodeInfo> resource 
(only resource specific attributes are shown)

The <nodeInfo> resource shall contain the attributes described in Table 9.6.20-1.

Table 9.6.20-1: Attributes of <nodeInfo> resource

| Attribute Name of <m2mServiceSubscription> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| parentID (pID) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| expirationTime (eT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| accessRightID (aRI) | 0..1 | RW | See section 9.6.1 where this common attribute is described. If no accessRightID is given at the time of creation, the accessRightID of the parent resource is linked to this attribute |
| creationTime (cT) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| creator (cr) | 1 | RW | See section 9.6.1 where this common attribute is described. |
| lastModifiedTime (lMT) | 1 | RO | See section 9.6.1 where this common attribute is described. |
| nodeID | 1 | RW | Node identifier indicating where the M2M Service Subscription applies. Wildcard may be used to allow all the Nodes within a M2M Service Provider. |
| AppID | 0..n | RW | See section 7.1.3. application ID pertaining to an application running on this node |
| CSEID | 0..1 | RW | cseID pertaining to this node (for nodes that have a CSE). The cseID becomes know once the pre CSE registration procedure is triggered. |
| serviceAccessCredential | 0..1 | NR | credential to be shared with targeted node for use the credential as proof of authorization of the access. Note: credential data should be stored in secure storage. |

---- end of change ---