| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC#9.2 |
| Title:* | Overview on Authentication Mechanisms for Security TS |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Phil Hawkes, Qualcomm , phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2014-03-07 |
| Abstract:* | This contribution provides an introduction to the authentication mechanisms for in the Security TS. |
| Agenda Item:* | TS-0003 |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate text into an appropriate section of the Security TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

==================<Start of Change 1 (New Text) >=================

### h.2	Overview on oneM2M Authentication Mechanisms

The oneM2M system supports the following authentication mechanisms:

- Pre-Established Symmetric Key. The Registree and Registrar previously established a symmetric key that is a secret known only to the Registree and Registrar. The Registree and Registrar authenticate each other by verifying message authentication codes in the Security Handshake which were generated using the symmetric key.  For more details see Clause h.4.

Note:  In the present specifications the terms Registree and  Registrar are used to reflect the different roles of  the two entities involved in the authentication procedure even when authentication is not part of a Registration procedure as defined in [TS-0001].  Typically, the entity denoted as Registree is owned by the M2M service Subscriber, while the entity denoted as Registrar is owned by the M2M Service Provider. The Registree initiates the Security Handshake with the Registrar.

- oneM2M supports two authentication mechanisms using centralized key distribution. In such schemes, the Registree and a Central Key Distribution Server authenticate each other and derive a symmetric key that the Central Key Distribution Server delivers to the Registrar. The Registree and Registrar then authenticate each other using the derived symmetric key. The oneM2M authentication mechanisms using centralized key distribution are:

  - GBA based Authentication. In this case, the Underlying Network Service Provider owns the Central Key Distribution Server. The details are specified by 3GPP and 3GPP2 [reference]. For more details see Clause h.5.

  - M2M Authentication Server (MAS)-based. In this case, the M2M Service Provider owns the Central Key Distribution Server. For more details see Clause h.6.

The Registree and Registrar authenticate each other by verifying that the message authentication codes in the Security Handshake were generated using the derived symmetric key. Following successful Security Handshake, the derived symmetric key is installed for use in subsequent Security Handshakes using the Pre-Established Symmetric Key mechanism above.

- Certificate-Based: The Registree and Registrar are issued with private signing keys and certificates containing the corresponding public verification keys. The Registree and Registrar must validate each other’s certificate before trusting the public verification keys in the certificate. The Security Handshake is then authenticated as described under “Asymmetric Authentication” in Clause h.1. Following the Security Handshake, symmetric keys may be exported from the session secrets and installed at the Registree and Registrar for use in subsequent Security Handshakes using the Pre-Established Symmetric Key mechanism above. For more details see Clause h.7.

For a more detailed description of the above authentication mechanisms, it is useful to differentiate between the following phases:

- Authentication Credentials: This includes the information that the Registree and Registrar will use to authenticate themselves to the other entity. For some authentication mechanisms, entity identifiers are assumed be present. There are various options for configuring this information in the entities, but this has no further influence on the subsequent phases.

- Identity Association: Configuration of the relevant information to the entities to enable

  - The Registree to verify the Registrar and associate the correct entity identifier.

  - The Registrar to verify the Registree and associate the correct entity identifier.

- Security Context Establishment:

  - Security Handshake: Mutual authentication of the Registree and Registrar.

  - (optional) Key Export: generating and installing a symmetric key (denoted Kx) intended for subsequent use in the Pre-Established Symmetric Key authentication mechanism (see Table h.2-1 for definition of Kx).

Editor’s note: The notation “Kx” is intended to be a placeholder only, until a better abbreviation is agreed upon.

Figure h.2-1 provides a summary of the above defined four authentication mechanisms

Figure h.2-1	Overview of the authentication mechanisms supported by oneM2M. See Table h.2-1 for details of the abbreviations used in this table.

Table h.2-1	Abbreviations used in Figure h.2-1.

| Abbreviation | Full Term |
| --- | --- |
| Authn | Authentication |
| AuthzToken | Authorization Token |
| BSF, B-TID, Ks, USS | GBA terms (see definitions) |
| Ks..NAF | GBA Ks_(int/ext)_NAF |
| Kx | Key to be used in Pre-Established Symmetric Key scheme. Editor’s note: The notation “Kx” is intended to be a placeholder only, until a better abbreviation is agreed upon. |
| (O) | Optional |
| (T)KxId | (Optional Temporary) Identifier for Key to be used in Pre-Established Symmetric Key scheme. Editor’s note: The notation “(T)KxID” is intended to be a placeholder only, until a better abbreviation is agreed upon. |
| Ree | Registree |
| Rar | Registrar |
| [Rar/Ree]Cert | [Registrar/Registree] Certificate |
| [Rar/Ree]CertName | Part of the credential identifier that matches a unique value in a name field of the [Registrar/Registree] Certificate |
| [Rar/Ree]Chain | [Registrar/Registree] Certificate chain: Certificate Chain from the [Registrar/Registree] Certificate to a [Registrar/Registree] Root Certificate |
| [Rar/Ree]CredInfo | [Registrar/Registree] Credential Information |
| [Rar/Ree]ID | Entity identifier (CSE_ID, AE_ID) for the [Registrar/Registree] |
| [Rar/Ree]PrivateKey | [Registrar/Registree] private signing key |
| [Rar/Ree]RootOfTrust | [Registrar/Registree] Root of Trust: The hash of the public key in the [Registrar/Registree] Certificate (if self-signed) or the [Registrar/Registree] Root Certificate |