| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC#9.2 |
| Title:* | Pre-Established Symmetric Key Authentication for Security TS |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Phil Hawkes, Qualcomm , phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2014-03-07 |
| Abstract:* | This contribution describes the Pre-Established Symmetric Key Authentication mechanism. |
| Agenda Item:* |  |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate text into an appropriate section of the Security TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

==================<Start of Change 1 (New Text) >=================

### h.4 The Pre-Established Symmetric Key Authentication Mechanism

This clause describes the Authentication Credentials, Identity Association and Security Handshake for Pre-Established Symmetric Key Authentication Mechanism. All remaining details for the Pre-Established Symmetric Key Authentication Mechanism are identical to the generic Authentication Flow shown in Clause h.3.

### h.4.1 Pre-Established Symmetric Key Authentication Flow

Figure h.3-1 illustrates the sequence of events for authentication and subsequent registration (when required) and resource access operations for the Pre-Established Symmetric Key Authentication Mechanism.

Figure h.6-1	Initial authentication and initial registration when using the Pre-Established Symmetric Key authentication mechanism.  See Table h.2-1 for details of the abbreviations used in this table. The following font colours differentiate the general topic that the text relates to:

- Black text contains authentication-mechanism-independent details

- Blue text highlights details specific to a particular authentication mechanism.

- Purple text highlights technical actions that are not specified in oneM2M.

- Red text highlights security-related properties.

### h.4.2	Pre-Established Symmetric Key Authentication Credentials

The Registree and Registrar authenticate each other by verifying message authentication codes in the Security Handshake which were generated using a symmetric key denoted Kx that has been previously established in both the Registree and Registrar. By “previously established”, it is meant that either

- The symmetric key Kx and associated identifier KxID were configured to the Registree and Registrar by out-of-band (out-of-scope) means, or

- The symmetric key and associated identifier KxID were installed at the Registree and Registrar following successful authentication between the Registree and Registrar using one of the other authentication mechanisms (GBA-based authentication, MAS-based authentication or Certificate-Based authentication).

The Authentication Credential for this authentication mechanism is the previously-established symmetric key, denoted Kx. The Credential Information identifying Kx is denoted KxID.

### h.4.3 Pre-Established Symmetric Key Identity Association

Note: The Registrar’s identity is assumed to have been configured prior to this phase.

Editor’s Note: The specification may need more details regarding configuring the Registrar’s identity.

Note: Prior to the “Identity Association Phase”, the following are business steps are assumed to occur. The details of these business steps are not specified by oneM2M.

    - The Pre-Established Symmetric Key Credential Identifier KxID  is made available to the M2M Service Subscriber.

    - The M2M Service Provider and M2M Service Subscriber agree on the identity to be used by the Registree (and which the Registrar will associate with the Pre-Established Symmetric Key Credential Identifier KxID  ).

    - The Registrar identity is made available to the M2M Service Provider.

    - The M2M Service Provider provides the M2M Service Subscriber with the Registrar identity (which the Registree will associate with Pre-Established Symmetric Key Credential Identifier KxID  ).

The M2M Service Provider and M2M Service Subscriber have the Registrar and Registree configured with the information needed for mutual authentication and identification:

  - The M2M Service Provider has the Registrar configured with the following arguments describing a Registree authorized to perform Security Context Establishment with the Registrar:

    - The Pre-Established Symmetric Key Credential Identifier KxID;

    - Registree identity (the Registrar is to use this identity for the Registree authenticating using the above arguments).

The mechanisms for achieving this are discussed in clause g.h.i.

Note: The Registrar will associate the configured Registree’s identity with messages secured within Security Contexts established using the Pre-Established Symmetric Key Kx associated with the Pre-Established Symmetric Key Credential Identifier KxID.

  - The M2M Service Subscriber has the Registree commanded to initiate Security Context Establishment, and includes the following arguments:

    - The Pre-Established Symmetric Key Credential Identifier KxID;

    - Registrar identity (this is used to route the (D)TLS exchange); and

    - Registree identity (the Registree is to use this identity with the Registrar.

The mechanisms for achieving this are discussed in clause g.h.i.

Note: The Registree will associate the Registrar’s identity with messages secured within Security Contexts established using the Pre-Established Symmetric Key Kx associated with the The Pre-Established Symmetric Key Credential Identifier KxID

Note: in many cases, the entity identities will be configured when the Pre-Established Symmetric Key Kx is established, so a separate configuration is not required.

### h.4.4 Pre-Established Symmetric Key Security Handshake

Registree and Registrar perform a (D)TLS-PSK handshake [TLS-PSK RFC 4279] to establish a secure session.

- The “psk_identity” parameter [TLS-PSK RFC 4279] is set to the value of the Pre-Established Symmetric Key identifier KxID.

- The “psk” parameter [TLS-PSK RFC 4279] is set to the value of the Pre-Established Symmetric Key identifier Kx.