| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC#9.2 |
| Title:* | Certificate-Based Authentication Flow for Security TS |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Phil Hawkes, Qualcomm , phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2014-03-07 |
| Abstract:* | This contribution describes the Certificate-Based authentication mechanism. |
| Agenda Item:* |  |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate text into an appropriate section of the Security TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

==================<Start of Change 1 (New Text) >=================

### h.7 The Certificate-Based Authentication Mechanism

This clause describes the Authentication Credentials, Identity Association and Security Handshake for Certificate-Based Authentication mechanism. All remaining details for the Certificate-Based Authentication mechanism are identical to the Generic Authentication Flow shown in Clause h.3.

Editor’s Note: Definitions will be required for the common terms used in this authentication mechanism. We should determine if definitions are most appropriate in the SEC TR or SEC TS. The terms to be defined are:

- Certificate Chain

- Private Signing Key

- Public Verification Key

- Public Key Certificate (often abbreviated to Certificate).

- Root Certificate

- Root of Trust

### h.7.1 Certificate-Based Authentication Flow

Figure h.7-1 illustrates the sequence of events for authentication and subsequent registration (when required) and resource access operations for the Certificate-Based Authentication Mechanism.

Figure h.7-1	Initial authentication and initial registration when using the Certificate-Based authentication mechanism.  See Table h.2-1 for details of the abbreviations used in this figure. The following font colours differentiate the general topic that the text relates to:

- Black text contains authentication-mechanism-independent details

- Blue text highlights details specific to a particular authentication mechanism.

- Purple text highlights technical actions that are not specified in oneM2M.

- Red text highlights security-related properties.

### h.7.2	Certificate-Based Authentication Credentials

For this authentication mechanism, the Registree authenticates itself to the Registrar using a Public Verification Key certificate.

  - To authenticate itself using this authentication mechanism, the Registree is configured with the following information.

    - The Registree Private Signing Key and corresponding Registree Public Verification Key.

Note: The Registree authenticates itself to other entities by proving that it knows the Private Signing Key.

Editor’s Note: In some cases the Private Signing Key is unique to a Registree. When the Registrar is a Field Domain Node, then the Private Signing Key might be used to authenticate all Registrees executing on a particular piece of hardware or used to authenticate all AEs executing a particular piece of software. This needs clarification text.

    - The Registree Certificate containing the Registree Public Verification Key. The Registree Certificate Name is a unique identity provided in a name field of the Certificate (e.g. in the X.509 “Subject” or “Subject Alternative Name” attribute). Two options are available:

      - The Registree is configured with a valid Certificate Chain from the Registree Certificate to a Registree Root Certificate. The Registree Root of Trust is the cryptographic hash of the Public Verification Key in the Registree Root Certificate.

      - The Registree Certificate is a self-signed certificate, for which the Registree Private Signing Key is used to generate the Certificate signature (so the certificate is verified using the Registree Public Verification Key).  In this case the cryptographic hash of the Registree Public Verification Key is both the Registree Root of Trust and the Registree Certificate Name. This implies that the cryptographic hash of the Registree Public Verification Key must be present in a name field of the Registree Certificate.

The mechanisms for configuring these parameters to the Registree are discussed in clause d.e.f.

The Registree Credential Information consists of

- The Registree Certificate Name, and

- The Registree Root of Trust.

Editor’s Note: The authentication credential details for a Registree and Registrar are identical. We should consider the best way to describe both cases while avoiding duplication.

Editor’s Note: Details for OCSP [RFC2560] and Certificate Revocation Lists (CRLs) are FFS.

### h.7.3 Certificate-Based Identity Association

Note: The Registrar’s entity identity is assumed to have been configured prior to this phase.

Editor’s Note: The specification may need more details regarding configuring the Regsitrar’s entity identity are needed.

Note: Prior to the “Identity Association Phase”, the following business steps are assumed to occur (the details of these business steps are not specified by oneM2M):

    - The Registree Certificate Name and Registree Root of Trust are made available to the M2M Service Subscriber.

    - The M2M Service Subscriber provides the M2M Service Provider with the Registree Certificate Name and the Registree Root of Trust.

    - The M2M Service Provider and M2M Service Subscriber agree on the entity identity to be used by the Registree.

    - The Registrar Certificate Name, Registrar Root of Trust and Registrar entity identity are made available to the M2M Service Provider.

    - The M2M Service Provider provides the M2M Service Subscriber with the Registrar Certificate Name, the Registrar Root of Trust and the Registrar entity identity.

The M2M Service Provider and M2M Service Subscriber have the Registrar and Registree configured with the information needed for the authentication and identification of the Registree and Registrar respectively:

  - The M2M Service Provider has the Registrar configured with the following arguments describing a Registree authorized to perform Security Context Establishment with the Registrar:

    - Registree Certificate Name (the Registree Certificate must include this value in a name field);

    - Registree Root of Trust (the Registree Certificate must be self-signed using this root of trust, or have a Certificate Chain to this root of trust) ;

    - Registree entity identity (the Registrar is to use this entity identity for the Registree authenticating using the above arguments).

The mechanisms for achieving this are discussed in clause g.h.i.

Note: The Registrar will associate the Registree’s identity with messages secured within Security Contexts established in accordance with the configured Registree Certificate Name and Registree Root of Trust.

  - The M2M Service Subscriber has the Registree commanded to initiate Security Context Establishment, and includes the following arguments:

    - Registrar Certificate Name (the Registrar Certificate must include this value in a name field);

    - Registrar Root of Trust (the Registrar Certificate must be self-signed using this root of trust, or have a Certificate Chain to this root of trust);

    - Registrar entity identity (this is used to route the (D)TLS exchange); and

    - Registree entity identity (the Registree is to use this entity identity with the Registrar).

The mechanisms for achieving this are discussed in clause g.h.i.

Note: The Registree will associate the Registrar’s identity with messages secured within Security Contexts established in accordance with the configured Registrar Certificate Name and Registrar Root of Trust.

### h.7.4 Certificate-Based Security Handshake

The Registrar provides the Registrar Certificate to the Registree during the Security Handshake.

The Registree verifies the Registrar Certificate as follows:

- If the Registrar Certificate is a self-signed certificate, then the Registree verifies that

  - The Registrar Certificate Name and Registrar Root of Trust (received during Identity Association) are identical.

  - The Registrar Certificate Name (received during Identity Association) is identical to a value in a name field (e.g. in the X.509 “Subject” or “Subject Alternative Name” attribute) of the Registrars Certificate.

  - The Registrar Root of Trust (received during Identity Association) is identical to the Registrar Certificate’s Public Verification Key (or hash thereof).

- If the Registrar Certificate is not a self-signed certificate, then the Registree verifies that

  - The Registrar Certificate Name (received during Identity Association) is identical to a value in a name field (e.g. in the X.509 “Subject” or “Subject Alternative Name” attribute) of the Registrars Certificate

  - The Registrar Certificate has a valid Certificate Chain to a certificate whose Public Verification Key (or hash thereof) is identical to the Registrar Root of Trust (received during Identity Association).

After the Registrar Certificate has been verified, the Registree uses the Registrar Public Verification Key (in the Registrar Certificate) to verifies that the digital signature on the session parameters that is provided as part of the Security Handshake.

Note: After a successful (D)TLS handshake in which the Registrar provides a Certificate Chain, the Registree can associate the Registrar’s identity (received during Identity Association) with additional information in the Certificate Chain (e.g. the Registrar Manufacturer, Registrar owner, or conformance criteria). These details are not described in these specifications.

Editor’s Note: Details of credentials for OCSP [RFC2560] may be required here.

Editor’s Note: The security handshake details for a Registree and Registrar are identical. We should consider the best way to describe both cases while avoiding duplication.