| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC#10 |
| Title:* | Pre-Provisioned Symmetric Key Security Association Establishment Framework |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Phil Hawkes, Qualcomm , phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2014-04-01 |
| Abstract:* | This contribution describes the Pre-Provisioned Symmetric Key Security Association Establishment Framework. |
| Agenda Item:* |  |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate text into an appropriate section of the Security TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Note on R01: See Note in SEC-2014-0224R01.

Note on R02:

- See Note in SEC-2014-0243 “Overview of Security Frameworks”. Revision marks show the changes from R02

- We felt that clause 8.2.2 was too small to partition into sub-clauses – this is why the sub-clause headings have been removed.

- We understand that the Pre-Provisioned Symmetric Key (denoted Kpp) in this framework might correspond to the Master Credential discussed in SEC-2014-0236. We are happy to revise the contribution to this agreed names.

.

==================<Start of Change 1 (New Text) >=================

### 8.2.2 The Pre-Provisioned Symmetric Key Security Association Establishment Framework

This clause describes the Cryptographic Secret Configuration, Entity Identity Configuration and Security Handshake for Pre-Provisioned Symmetric Key Security Association Establishment Framework.  This framework enables mutual authentication of two entities corresponding to either two CSEs or a CSE and an AE. The Master Credential for this framework is a long-term symmetric key that has been pre-provisioned into the entities to be authenticated; this key is called a Pre-Provisioned Symmetric Key and is denoted Kpp. The entities authenticate each other by verifying message authentication codes in the Security Handshake which were generated using the Pre-Provisioned Symmetric Key.

Note: Long term Pre-Provisioned Symmetric Keys can pose a security risk if not adequately secured, and for this reason Long term Pre-Provisioned Symmetric Keys are recommended to be stored in Secure Environments.

Figure 8.2.2-1 illustrates the sequence of events when using the Pre-Provisioned Symmetric Key Security Association Establishment Framework. In this description, “Entity A” and “Entity B” correspond to either two CSEs or a CSE and an AE or an AE and a CSE (respectively).

Figure 8.2.2-1	The sequence of events when using the Pre-Provisioned Symmetric Key Security Association Establishment Framework.  See Table 8.2.1-1 for details of the abbreviations used in this table. The following font colours differentiate the general topic that the text relates to:

- Blue italic text highlights details specific to this particular Security Association Establishment Framework.

- Purple italic text highlights technical actions that may include steps not specified by oneM2M.

- Red italic text highlights security-related properties.

- Master Credential Configuration: The Pre-Provisioned Symmetric Key and the corresponding Pre-Provisioned Symmetric Key Identifier, denoted KppId, are pre-provisioned to both entities.

- Note:  This pre-provisioning (by definition) uses mechanisms not specified by oneM2M.

Identity Mapping Configuration:  Each entity is configured with the information needed for mutual authentication and identification:

  - Entity A is commanded to initiate Security Context Establishment, and includes the following arguments:

    - The Pre-Provisioned Symmetric Key Identifier KppId.

    - Entity A identity (IdA). Entity A is to assume this identity when interacting with Entity B.

    - Entity B identity (IdB). Entity A is to use this identity for Entity B authenticating using the above arguments. This identity is also used to route the (D)TLS exchange.

The mechanisms for achieving this are discussed in clause g.h.i.

Note: EntityA will associate Entity B’s identity with messages secured within Security Contexts established using the Pre-Provisioned Symmetric Key Kpp associated with the Pre-Provisioned Symmetric Key Identifier KppId

  - Entity B is configured with the following arguments describing Entity A authorized to perform Security Context Establishment with the Registrar:

    - The Pre-Provisioned Symmetric Key Identifier KppId.

    - Entity A identity (IdA). Entity B is to use this identity for Entity A authenticating using the above arguments..

    - Entity B Identity (IdB), if not already configured to Entity B. Entity B is to assume this identity when interacting with Entity A.

The mechanisms for achieving this are discussed in clause g.h.i.

Note: Entity B will associate the configured Entity A identity with messages secured within Security Contexts established using the Pre-Provisioned Symmetric Key Kpp associated with the Pre-Provisioned Symmetric Key Credential Identifier KppId.

Note: in many scenarios, the entity identities will be configured when the Pre-Provisioned Symmetric Key Kpp is established, so a separate configuration is not required in those scenarios.

### Centralized Key Distribution Server Handshake: There is no Centralized Key Distribution Server Handshake applied in the Pre-Provisioned Symmetric Key Security Association Establishment Framework.

Security Handshake: The entities perform a (D)TLS-PSK handshake [TLS-PSK RFC 4279] to establish a secure session.

- The “psk_identity” parameter [TLS-PSK RFC 4279] is set to the value of the Pre-Provisioned Symmetric Key Identifier KppId.

- The “psk” parameter [TLS-PSK RFC 4279] is set to the value of the Pre-Provisioned Symmetric Key Kpp.