| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC#10 |
| Title:* | Certificate-Based Security Association Establishment Framework |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Phil Hawkes, Qualcomm , phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2014-03-31 |
| Abstract:* | This contribution describes the Certificate-Based Security Association Establishment Framework. |
| Agenda Item:* |  |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate text into an appropriate section of the Security TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Note on R01: See Note in SEC-2014-0224R01.

Note on R02:

- See motivation for SEC-2014-0xxx “Overview of Security Frameworks”.

- Text about Master Credential Configuration and Certificate Verification has been moved to Clause 8.1.5, because these details are common to this framework and the “Certificate-Based Security Bootstrap Framework”.

- After moving these details to Clause 8.1.5, we felt that clause 8.2.5 was too small to partition into sub-clauses – this is why the sub-clause headings have been removed.

==================<Start of Change 1 (New Text) >=================

### 8.2.5 The Certificate-Based Security Association Establishment Framework

This clause describes the Master Credential Configuration, Identity Mapping Configuration and Security for Certificate-Based Security Association Establishment Framework.

Figure 8.2.5-1 illustrates the sequence of events when using the Certificate-Based Security Association Establishment Framework. In this description, “Entity A” and “Entity B” correspond to either two CSEs or a CSE and an AE.

Figure 8.2.5-1	The sequence of events when using the Certificate-Based Security Association Establishment Framework.  See Table 8.2.1-1 for details of the abbreviations used in this figure. The following font colours differentiate the general topic that the text relates to:

- Blue italic text highlights details specific to this particular Security Association Establishment Framework.

- Purple italic text highlights technical actions that may include steps not specified by oneM2M.

- Red italic text highlights security-related properties.

Master Credential Configuration: The master credentials for each entity are pre-provisioned as described in Clause 8.1.5.1 “Credential Configuration for Certificate-Based Security Frameworks”

Identity Mapping Configuration: Entity A and Entity B  are configured with the information needed for the authentication and identification (during Security Handshake) of  Entity B and Entity A respectively:

  - Entity A is commanded to initiate a Security Handshake, and the command includes the following arguments:

    - The Entity B Certificate Name (Entity B Certificate must include this value in a name field);

    - The Entity B Root of Trust (Entity B Certificate must be self-signed using this root of trust, or have a Certificate Chain to this root of trust);

    - The Entity A identity (IdA) Entity A is to use this entity identity with Entity B.

    - The Entity B identity (IdB). Entity A is to use this identity for Entity B authenticating using the above arguments. This is used to route the (D)TLS exchange).

The mechanisms for achieving this are discussed in clause g.h.i.

Note: The Entity A will associate Entity B’s identity with messages secured within Security Contexts established in accordance with the configured Entity B Certificate Name and Entity B Root of Trust.

  - The Entity B is configured with the following arguments describing Entity A authorized to perform Security Handshake with Entity B:

    - The Entity A Certificate Name. The Entity A Certificate must include this value in a name field.

    - The Entity A Root of Trust. The Entity A Certificate must be self-signed using this root of trust, or have a Certificate Chain to this root of trust.

    - The Entity A identity (IdA). Entity B is to use this entity identity for Entity A authenticating using the above arguments.

    - The Entity B Identity (IdB), if not already configured to Entity B. Entity B is to assume this identity when interacting with Entity A.

The mechanisms for achieving this are discussed in clause g.h.i.

Note: Entity B will associate Entity A’s identity with messages secured within Security Contexts established in accordance with the configured Entity A Certificate Name and Entity A Root of Trust.

### Centralized Key Distribution Server Handshake: There is no Centralized Key Distribution Server Handshake applied in the Certificate-Based Security Association Establishment Framework.

Security Handshake:

- Each entity verifies the other entity’s certificate as described in Clause 8.1.5.2 “Certificate Verification”.

- The entities authenticate each other using the validated certificates as specified in TLS 1,2 RFC 5246 [RFC 5246] and DTLS 1.2 RFC 6347 [RFC 6347] specifications.

Editor’s note: the applicable (D)TLS ciphersuites are FFS.

# Comments

This editor’s note is moved to Clause 8.1.5 “Common Details of the Certificate-Based Security Frameworks”