| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 (SEC) at TP#10 |
| Title:* | SEC CSF Authorization Procedure for Security TS |
| Source:* | CATT, CATR |
| Contact: | Wei Zhou, zhouwei@catt.cn Jiadong Du, dujiadong@catr.cn Hui Xu, xuhui@catt.cn |
| Date:* | 2014-04-07 |
| Abstract:* | This contribution proposes a description of the authorization procedure for the security TS. |
| Agenda Item:* | Security TS |
| Work item(s): | WI-0007 |
| Document(s) Impacted* | oneM2M-TS-0003 Security Solutions |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To add the proposed text into the Security TS. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

This contribution aims to provide a description of authorization procedure which should be added in the section of “6.3.2 Authorization Architecture”.

2	Proposal

-----------------------Start of 1st change-------------------------------

### 6.3.2	Authorization Architecture

The following figure provides a high level overview of the authorization architecture. This architecture comprises four subcomponents that are described as follows:

- Policy Enforcement Point (PEP)

PEP intercepts resource access requests, makes access control decision requests, and enforces access control decisions. The PEP coexists with the CSFs that need authorization services.

- Policy Decision Point (PDP)

PDP interacts with the PAP and PIP to get applicable authorization polices and attributes needed for evaluating authorization policies respectively, and then evaluates access request using authorization policies for rendering an access control decision. The PDP is located in the Authorization component of SEC CSF.

- Policy Access Point (PAP)

PAP obtains applicable authorization policies according to an access control decision request. These applicable policies should be combined in order to get a finial access control decision. The PAP is located in the Authorization component of SEC CSF.

- Policy Information Point (PIP)

PIP provides attributes that are needed for evaluating authorization policies, for example IP address of the requester, creation time of the resource, current time or location information of the requester. The PIP is located in the Authorization component of SEC CSF.

The SEC CSF Authorization component may comprise any of the subcomponents: PDP, PAP and/or PIP. It means that the subcomponents PEP, PAP, PDP and PIP could be distributed across different nodes. For example the PEP is located in an ASN/MN and the PDP is located in the IN.

Note: Release 1 does not support separation of PAP and PIP on different CSE from PDP.

-----------------------End of 1st change-------------------------------

-----------------------Start of 2nd change-------------------------------

The authorization procedure is shown in the following figure.

Step 001:	Mutual authentication (Prerequisite).

Step 002:	Access Requester sends an Access Request to the PEP.

Step 003:	PEP makes an Access Control Decision Request according to the requester’s Access Request, and sends the Access Control Decision Request to the PDP.

Step 004: 	PDP sends an Access Control Policy Request that is generated based on the Access Control Decision Request to the PAP.

Step 005:	PAP finds all applicable access control policies to the access request and sends them back to the PDP. When multiple access control polices are involved, the PAP also provides a policy combination algorithm for combining multiple evaluation results into one finial result.

Step 006	PDP sends Attribute Request to the PIP if any attributes are required for evaluating these access control policies.

Step 007:	PIP gets required attributes and sends them back to the PDP.

Step 008:	PDP evaluates Access Request using access control policies. When there are multiple applicable access control policies, the PEP needs to calculate a final Access Control Decision using the policy combination algorithm.

Step 009:	PDP returns the Access Control Decision back to the PEP.

Step 010:	PEP enforces the access control decision, i.e. either forwards the Access Request to the resource or denies this access.

Step 011:	PEP returns access result back to the Access Requester.

-----------------------End of 2nd change-------------------------------