| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC8.0 (WG4 at TP#10) |
| Title:* | SEC CSF Architecture General Description for Security TS |
| Source:* | CATT, CATR, Giesecke & Devrient, Oberthur Technologies |
| Contact: | Wei Zhou, zhouwei@catt.cn Ying Huang, huangying@catr.cn Hui Xu, xuhui@catt.cn Claus Dietze, G&D Dragan Vujcic, Oberthur Technologies |
| Date:* | 2014-04-07 |
| Abstract:* | This contribution proposes to update SEC CSF Architecture figure and provides some high level general description for some boxes shown in this figure. |
| Agenda Item:* | Security TS |
| Work item(s): | WI-0007 |
| Document(s) Impacted* | oneM2M-TS-0003 Security Solutions |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To add the proposed text into the Security TS. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

This contribution contains two proposals for the Security TS:

Proposal 1:

The process of authentication is often considered to consist of two distinct phases: (1) identification and (2) (actual) authentication. However, identification generally belongs to authentication, so the identification box in the SEC CSF Architecture figure should be merged into one. The identification will be described in authentication part.

Proposal 2:

In the Section 5.1 of Security TS it should contain some high level general description for each box shown in the SEC CSF Architecture figure. This proposal provides two subsections that give some general description about Authentication and Authorization respectively.

2	Proposal 1

## 5.1	Overview

-----------------------Start of 1st   change-------------------------------

[x]	TS-0001 Functional Architecture (draft)

-----------------------End of 1st  change-------------------------------

-----------------------Start of 2nd   change-------------------------------

### 5.1.1	Identification

The Identification service provides oneM2M identities / identifiers to the requesting entity in case those identities are stored within the secure environment. oneM2M identifiers as defined in [x] may also be treated as sensitive data that are accessible to AEs or CSEs and used independently of Authentication or Authorization functions.

### 5.1.2	Authentication

The Authentication service is in charge of i mutual authentication of CSEs and AEs.

Authentication is the process of validating the supplied  enrolled and/or subscribed identity  with associated trustworthy credential. How to perform an authentication process will depend on the applied mutual authentication mechanism. For example, in the case of using certificate based authentication mechanism, the authentication function may require the authentication to verify a digital signature; in the case of using symmetric key based authentication mechanism, the authentication function may require the authentication to verify a Message Authentication Code (MAC). Once passing this validating process, the AE or CSE is authenticated.

### 5.1.3	Authorization

The Authorization service is responsible to control access to resources and services by CSEs and AEs according the associated access control policies. Access control policy is a set of access control rules derived from privileges. These privileges define CSE or AE (originator) privileges for certain access modes (operation) privileges associated to certain context privileges. The authorization/access grant involves an Access Decision to allow the access to the requested resource by evaluating the CSE or AE  originator privileges with the set of allowed operations and context privileges,

Prior authorization it is required that the originator CSE or AE has been identified first to an M2M Authentication Function and mutually authenticated and associated with an M2M Service Subscription.

.-----------------------End of 2nd  change-------------------------------