| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC#10 |
| Title:* | Overview on Security Frameworks for Security TS |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Phil Hawkes, Qualcomm , phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2014-04-09 |
| Abstract:* | This contribution provides an introduction to the Security Frameworks for the Security TS. |
| Agenda Item:* | TS-0003 |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate text into the appropriate section of the Security TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Note: Following discussions during SEC#9.4, we understand that  this text should be included in Clause 8.

We believe that it is appropriate to separate out

- Security Association Establishment Frameworks, establishing a secure session between oneM2M entities which may use one of: a Pre-Provisioned Symmetric Key; MAF-based Centralised Key Distribution; GBA-based Centralised Key Distribution; or certificates.

- Security Bootstrapping of an MAF which may use one of: a Pre-Provisioned Symmetric Key; GBA-based Centralised Key Distribution; or certificates.

That is – security bootstrapping is used only to provision a long-term symmetric key to an AE/CSE and an MAF providing Centralised Key Distribution; security bootstrapping is not used for any other purpose. For example, security bootstrapping is not used to establish a long term symmetric key between an AE and CSE or between two CSEs.

R01: Gemalto proposed categorizing the security frameworks into those that use a central key distribution server, and those that don’t. We have reorganized the clauses accordingly..

R02: Changes suggested by SEC-2014-0261 from Gemalto, plus removal of sections 8.3.4, 8.3.5 and 8.3.6 as agreed during 2014-04-08 WG2 session.

R03: corrected numbering of subsection 8.3.1 -> 8.3.2 Direct Security Bootstrap Frameworks

==================<Start of Change 1 >=================

# 8	Security Frameworks for SEC CSF

# 8.1	General Introductions to the Security Frameworks

### The security frameworks can be categorized into two main types

### Direct Security Frameworks: where the entities authenticate each other directly, without assistance from a Central Key Distribution Server

### Centralized Security Frameworks: where the entities authenticate each other with the assistance of a Central Key Distribution Server.

### Editor’s Note: Direct Security Framework and Central security Framework, and Central Key Distribution Server should be added to the definitions.

### 8.1.1	General Introduction to the Direct Security Frameworks

### 8.1.1.1	General Introduction to the Pre-Provisioned Symmetric Key Framework

### Editor’s Note: Text is needed here.

### 8.1.1.2	General Introduction to the Certificate Framework

Editor’s Note: See SEC-2014-0224R01and revisions. Editor – please remove this note when incorporating into the TS.

### 8.1.2	General Introduction to the Centralized Security Frameworks

### 8.1.2.1	General Introduction to the M2M Authentication Function Framework

### Editor’s Note: Text is needed here.

### 8.1.2.2	General Introduction to the GBA (Generic Bootstrapping Architecture) Framework

A general introduction to GBA is included in TR-0008 [i.6].

After a successful GBA bootstrapping, the M2M Application Service/Middle Node and the BSF share a security association which consists of a bootstrapping transaction identifier (B-TID) and key material (GBA bootstrap Ks).

This security association may be used by the M2M Application Service/Middle Node to derive NAF keys (Ks_(ext/int)_NAF) shared between a M2M Application Service/Middle Node and a M2M Infrastructure Node or an M2M Authentication Framework.

Figure 8.1.2.2-1	GBA framework for SEC CSF. Note that the Network application Function (NAF) may be an Infrastructure Node or an M2M Authentication Function.

### 8.2 Security Association Establishment Frameworks

### 8.2.2 Overview on Security Association Establishment Frameworks

### Contributor’s Note: See SEC-2014-0224R02 and revisions. Editor – please remove this note when incorporating into the TS.

### 8.2.2 Direct Security Association Establishment Frameworks

### 8.2.2.1 Pre-Provisioned Symmetric Key Security Association Establishment Frameworks

### Contributor’s Note: See SEC-2014-0226R02 and revisions. Editor – please remove this note when incorporating into the TS.

### 8.2.2.2 Certificate-Based Security Association Establishment Frameworks

### Contributor’s Note: See SEC-2014-0227R02 and revisions. Editor – please remove this note when incorporating into the TS.

### 8.2.3 Centralized Security Association Establishment Frameworks

### 8.2.3.1 MAF-Based Symmetric Key Security Association Establishment Frameworks

### Editor’s Note: Text is required here.

### 8.2.3.2 GBA-Based Security Association Establishment Frameworks

To obtain a short term key used for M2M Service Connection between a M2M Application Service/Middle Node and a M2M Infrastructure Node, the M2M Application Service/Middle Node shall perform a successful GBA bootstrapping and derive a NAF key (Ks_(ext/int)_NAF). This NAF key is the M2M Secure Connection Key used for M2M Service Connection.

### Editor’s Note: Further text is required here.

### 8.3 Security Bootstrap Frameworks

### 8.3.1 Overview on Security Bootstrap Frameworks

### Contributor’s Note: See SEC-2014-0247R01 and revisions. Editor – please remove this note when incorporating into the TS.

### 8.3.2 Direct Security Bootstrap Frameworks

### 8.3.2.1 Pre-Provisioned Symmetric Key Security Bootstrap Frameworks

### Contributor’s Note: See SEC-2014-0226R02 and revisions. Editor – please remove this note when incorporating into the TS.

### 8.3.2.2 Certificate-Based Security Bootstrap Frameworks

### Contributor’s Note: See SEC-2014-0252 and revisions. Editor – please remove this note when incorporating into the TS.

### 8.3.3 Centralized Security Bootstrap Frameworks

### 8.3.3.1 GBA-Based Security Bootstrap Frameworks

To share a long term Master Credential between an Application Service/Middle Node and an M2M Authentication Function, the M2M Application Service/Middle Node shall perform a successful GBA bootstrapping and derive a NAF key (Ks_(ext/int)_NAF). This NAF key is the Master Credential.

### Editor’s Note: Further text is required here.

==================<End of Change 1 >=================