| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC#10 |
| Title:* | Certificate-Based Security Bootstrap Framework |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Phil Hawkes, Qualcomm , phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2014-04-10 |
| Abstract:* | This contribution describes the Certificate-Based Security Bootstrap Framework. |
| Agenda Item:* |  |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate text into an appropriate section of the Security TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

See Note at start of SEC-2014-243 “Overview of Security Frameworks”.

These revision marks show the changes from SEC-2014-0227R01.

These revision marks show the changes from SEC-2014-044

Notes on R01:

- Updated to align with new phases in Overview of SEC-2014-0247R01 “Security Bootstrap Frameworks”

Notes on R02:

- Updated to align with Terminology and Abbreviations suggested by Gemalto in SEC-2014-0259 and SEC-2014-0260. In particular

  - “Kmm” replaced by “Km”

    - We also replaced “KmmId” with “KmId”, to align with “Km” notation.

- The figure correct

  - Previous version Had “MAF” in many places where it should have had “MEF”

  - Previous version did not mention that Enrolee is configured with MEF URI in Bootstrap Instruction Configuration.

R03

- IdMAF ( MAF-ID

- IdEnrolee (Enrolee-ID

- Temporary Enrolment Key ( Enrolment Key

- Kte(Ke

- KteId(KeId

- Added Editor’s note after Figure: “Editor’s Note: More parameters may need to be transferred from MAF to MEF in the “Usage in Centralized Key Distribution Server Handshake”. This is FFS.”

- Added four Editor’s notes of form “Editor’s Note: Clause [xxx] referred to above is a suggested clause where the appropriate location is not yet clear.”

- Corrections in the Figure:

  - 8.1.5.1 ( 8.1.1.2

  - MAF ( MEF in Bootstrap Credential Configuration box

  - Field Domain Entity ( Enrolee

R04

- In the figure, changed “Generate KeID  from KeID” (Clause r.s.t)” to “Generate KeID  (Clause r.s.t) “

- Added new Editor’s Note “Reference to RFC 5705 is FFS.” after the figure.

==================<Start of Change 1 (New Text) >=================

### 8.3.2.2 The Certificate-Based Security Bootstrap Framework

This clause describes the Certificate-Based Security Bootstrap Framework. The Bootstrap Credentials for this framework are Certificates.

Figure 8.3.2.2-1 illustrates the sequence of events when using the Certificate-Based Security Bootstrap Framework.

Figure 8.3.2.2-1	The sequence of events when using the Certificate-Based Security Bootstrap Framework.  See Table 8.2.1-1 for details of the abbreviations used in this figure. The following font colours differentiate the general topic that the text relates to:

- Black text contains Security Bootstrap-Framework-independent details

- Blue italic text highlights details specific to this particular Security Bootstrap Framework.

- Purple italic text highlights technical actions that may include steps not specified by oneM2M.

- Red italic text highlights security-related properties.

Editor’s Note: More parameters may need to be transferred from MAF to MEF in the “Usage in Centralized Key Distribution Server Handshake”. This is FFS.

Editor’s Note: Reference to RFC 5705 is FFS.

Editor’s Note: Clause r.s.t referred to in above figure is a suggested clause where the appropriate location is not yet clear.

Bootstrap Credential Configuration: For this Security Bootstrap Framework, Enrolee and M2M Enrolment Function authenticate to each other using a Public Key Certificates. The Bootstrap Credentials for the Enrolee and M2M Enrolment Function are pre-provisioned as described in Clause 8.1.1.2.1 “Credential Configuration for Certificate-Based Security Frameworks”.

Note: The identities of the M2M Enrolment Function and M2M Authentication Function are assumed to have been configured prior to this phase.

Editor’s Note: The specification may need more details regarding configuring the identities of the M2M Enrolment Function and M2M Authentication Function.

Bootstrap Instruction Configuration: The Enrolee and M2M Enrolment Function  are configured with the information needed for authorizing the remote provisioning:

  - The Enrolee is configured with (or otherwise obtains) the following arguments to initiate remote provisioning:

    - The URI of the M2M Enrolment Function which will facilitate the remote provisioning, for the purpose of routing the (D)TLS exchange.

    - The M2M Enrolment Function Certificate Name (M2M Enrolment Function Certificate must include this value in a name field);

    - The M2M Enrolment Function Root of Trust (M2M Enrolment Function Certificate must be self-signed using this root of trust, or have a Certificate Chain to this root of trust);

    - The target M2M Authentication Function Identity (MAF-ID), with whom the Enrolee is to be provisioned using Security Bootstrap.

    - The Enrolee identity (Enrolee-ID): The Enrolee is to use this entity identity with the identified M2M Authentication Function.

The mechanisms for achieving this are discussed in clause x.y.z.

Editor’s Note: Clause x.y.z referred to above is a suggested clause where the appropriate location is not yet clear.

  - The M2M Enrolment Function is configured with the following arguments describing Enrolee authorized to perform Security Handshake with M2M Enrolment Function:

    - The Enrolee Certificate Name. The Enrolee Certificate must include this value in a name field.

    - The Enrolee Root of Trust. The Enrolee Certificate must be self-signed using this root of trust, or have a Certificate Chain to this root of trust.

    - The target M2M Authentication Function Identity (MAF-ID), with whom the Enrolee (authenticated using the above Enrolee Certificate Name and Enrolee Root of Trust) is to be provisioned using Security Bootstrap.

    - The Enrolee identity (Enrolee-ID). The M2M Enrolment Function is to provide this entity identity for the Enrolee with the Master Credential (Km) to the target M2M Authentication Function, when requested by the M2M Authentication Function..

The mechanisms for achieving this are discussed in clause m.n.o

Editor’s Note: Clause m.n.o referred to above is a suggested clause where the appropriate location is not yet clear.

Bootstrap Security Handshake: The Enrolee and M2M Enrolment Function perform a (D)TLS handshake as specified in TLS 1,2 RFC 5246 [RFC 5246] and DTLS 1.2 RFC 6347 [RFC 6347] specifications.to establish a secure session.

- Each entity (Enrolee and M2M Enrolment Function) verifies the other entity’s certificate as described in Clause 8.1.1.2.2 “Certificate Verification”.

- The Enrolee and M2M Enrolment Function authenticate each other using the validated certificates as specified in TLS 1,2 RFC 5246 [RFC 5246] and DTLS 1.2 RFC 6347 [RFC 6347] specifications.

Editor’s note: the applicable (D)TLS ciphersuites are FFS.

Enrolment Key Generation:

- The Enrolment Key (Ke) is generated from the (D)TLS session secrets by the Enrolee and M2M Enrolment Function using TLS Key Export (RFC 5705) [RFC5705], as described in Clause 8.3.6.

- The Enrolment Key Identifier (KeId) is generated by the Enrolee and M2M Enrolment Function, as described in Clause r.s.t.

Editor’s Note: Clause r.s.t referred to above is a suggested clause where the appropriate location is not yet clear.

- The Enrolee and M2M Enrolment store the Enrolment Key (Ke) and Enrolment Key Identifier (KeId).

Note: The Enrolment Key Generation for the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework is identical to the Enrolment Key Generation for the Certificate-Based Security Bootstrap Framework.

Usage in Centralized Key Distribution Server Handshake: See “Overview of Security Frameworks” in Clause 8.3.1.