| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC |
| Title:* | Access Control Mechanism |
| Source:* | LG Electronics |
| Contact: | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Date:* | 2014-03-31 |
| Abstract:* | This contribution proposes Access Control Mechanism of oneM2M R01: wording edited (Thanks to Wolfgang and Claus) Due to request from some members, I make it as case 1. Case 2 will be introduced by another contribution. For X.X.X.1 and X.X.X.2, the Hosting CSE ( PDP (To make generic) |
| Agenda Item:* | SEC |
| Work item(s): | WI 0002 |
| Document(s) Impacted* | Technical Specification – Security Solution |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve the proposed change and integrate it into the TS document |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Rationale

This contribution proposes new clause for Access Control Mechanism

========================Start of 1st Change==========================

### X.X.X	Access Control Mechanism

This clause specifies the access control mechanisms. There are two access control mechanisms considered in this release.

- Case 1: Hosting CSE works as PDP and PEP.

In this case, Hosting CSE provides the PEP and PDP functionality as described in clause 6.3.2. When a request message is received by the Hosting CSE, the Hosting CSE shall check whether the request to access a target resource can be granted or not. The request contains the identifier of the Originator, the operation to be executed, and the target resource URI. It may also include an access token applied for access control.

The Hosting CSE shall perform following steps to validate the Request to access a target resource.

Step 001:	When Hosting CSE receives a request from an Originator, The Hosting CSE verifies whether Originator has M2M Service Subscription enough to perform the request. The detailed description of this step is specified in clause X.X.X.1 M2M Service Subscription verification.

Step 002: 	If the request is validated in step 1, the Hosting CSE proceeds to step 2.

In this step, the Hosting CSE verifies whether Originator has enough privileges to perform the request by checking <accessControlPolicy> resource that applies to the targeted resource

The detailed description of this step is specified in clause X.X.X.2 Access Control Policy verification.

Step 003:	If step 1 and step 2 verifications have been passed, the Hosting CSE performs the request.

After this procedure, Hosting CSE sends proper response to the Originator.

### X.X.X.1	M2M Service Subscription verification

The <m2mServiceSubscription> resource describes which entities have the privilege to perform which operations on which resource types. M2M Service Subscription verification shall be performed to check whether Originator requests no more than M2M service roles that the Originator subscribes.

For example, an Originator may be subscribed only to  M2M service role “Data exchange” (see Annex G of TS-00001) on Hosting CSE and the M2M service role allows the Originator to perform Create, Retrieve, Update, and Delete operations on the <container> resource type. Then the request of Create, Retrieve, Update, or Delete operation from Originator is authorized to perform on <container> resource by M2M Service Subscription. Therefore if the request is to access other resource types than <container> resource type, then the request is fail to be authorized in this step If the request is to Create, Retrieve, Update or Delete <container> resource type, then the request is authorized in this step.

All <m2mServiceSubscription> resources are stored in an IN-CSE. For case 1, to enable a Hosting CSE to perform M2M Service Subscription verification, the Hosting CSE shall internally keep <m2mServiceSubscription> resources which are applied by the resource hosting CSE and synchronize those resources with the ones in the IN-CSE. This could be done by retrieving the <m2mServiceSubscription> resources periodically or by subscribing to <m2mServiceSubscription> resources and receiving changes notifications from IN-CSE. The <m2mServiceSubscription> resource stored in the hosting CSE shall not be exposed to any other entities.

Editor’s note: for case 1, how to synchronize M2M Service Subscription in Hosting CSE is FFS.

M2M Service Subscription verification procedure shall happen at PDP and the procedure is described as follows:

- PDP shall find <m2mServiceSubscription> resources which belong to the Originator by considering App-ID and where the Originator resides.

- PDP shall check whether any of M2M service roles in <m2mServiceSubscription> resources found at step 1 contains the requested operation pertaining to resource type of the target resource.

- If PDP shall finds a matching M2M service role, M2M Service Subscription verification has passed successfully

- If PDP does not find any matching <m2mServiceSubscription> resources, M2M Service Subscription validation has failed. The PDP shall send a respective response, and shall not proceed to step 2

### X.X.X.2	Access Control Policy verification

To be able to verify access control policy, PDP shall find the <accessControlPolicy> resource applicable to the target resource.

Editor’s note: how to find <accessControPolicy> resource is FFS. If the target resource doesn’t have accessControlPolicyID, the PDP finds <accessControPolicy> resource by using accessControlPolicyID of the parent resource. If the target resource doesn’t have accessControlPolicyID also at the parent resource, how to select access control policy resource is FFS.

After finding the <accessControlPolicy> resource, the following procedures shall be performed.

- PDP verifies whether Originator attributes in the request match with originatorPrivileges and operationFlags of the matched originatorPrivileges contain the operation in the request.

- PDP verifies whether environment conditions in contexts are satisfied.

If  validation passes both above procedures, the access request shall be granted.

If validation does not pass the two procedures, the access request shall not be granted.

Editor’s note: when Originator is CSE, whether to follow two steps is FFS. Step 2 may be only considered when Originator is CSE.