| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC8.0 (WG4 at TP#10) |
| Title:* | Symmetric Key Based Authentication Description for Security TS |
| Source:* | CATT |
| Contact: | Wei Zhou, zhouwei@catt.cn Hui Xu, xuhui@catt.cn |
| Date:* | 2014-04-07 |
| Abstract:* | This contribution proposes a general description of symmetric key based authentication for the security TS. |
| Agenda Item:* | Security TS |
| Work item(s): | WI-0007 |
| Document(s) Impacted* | oneM2M-TS-0003 Security Solutions |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To add the proposed text into the Security TS. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

This contribution aims to provide a general description of symmetric key based authentication and authentication procedure. This content should be in a new section that does not currently exist.

2	Proposal

-----------------------Start of 1st   change-------------------------------

#### 6.3.x	Authentication Framework

The oneM2M supports two kinds of authentication mechanisms, they are symmetric key based authentication mechanism and asymmetric key based authentication mechanism. The asymmetric key based authentication mechanism is also called as certificate based authentication.

#### 6.3.x.1	Symmetric key based authentication

The symmetric key based authentication mechanism is realized through using a pre-provisioned secret key to generate and verify Message Authentication Codes (MACs) that is used for providing authentication evidences. The pre-provisioned secret key is also called as Root Key that is only known by the authentication participants. The root key is provisioned to the authentication participants in a secured method and stored in secure environments.

In a symmetric key based authentication process the MACs are not directly generated with a root key. A secret key called Master Key is firstly derived from the root key according to some pre-defined rules. The Master key is unique in each authentication process. All other keys for one connection are derived from this master key, for example the authentication key used to generate MAC and the data encryption key used to secure the communication.

Editor's note: It is FFS about the key derivation rules.

#### 6.3.x.1.2	Symmetric key based authentication procedure

Symmetric key based authentication procedure is shown in the following figure and described as follows:

- Originator Hello. The Originator initiates a session by sending an Originator Hello message to the Receiver. The Client Hello message contains:

- Originator Identity that could be either the AE or CSE.

- Key Derivation Information that specifies using which key and what rules for this key derivation.

- Originator Random Number that will be used together with the Receiver Random Number in a key derivation process.

- Receiver Hello. The Receiver responds to the Originator with a Receiver Hello message. The Receiver Hello message contains:

- Receiver Identity

- Key Derivation Information that repeats the key derivation information suggested by the originator for a confirmation.

- Receiver Random Number that will be used together with the Originator Random Number in a key derivation process.

- Receiver Hello Done. This message indicates that the receiver is finished and awaiting a response from the Originator

- Master Key Derivation. Both Originator and Receiver derive a symmetric key called Master Key from the shared Root Key using the Originator Random Number, Receiver Random Number and other required key derivation parameters. All other keys for this connection are derived from this Master Key.

- Originator Change Cipher Spec. This message notifies the Receiver that all messages that follow the Originator Finished message will be encrypted using the keys and algorithms just negotiated.

- Originator Finished. The Originator sends an encrypted Originator Finished message that contains a hash of the entire conversation to provide authentication of the Originator.

The Receiver will attempt to decrypt the Originator Finished message and verify the hash. If the decryption or verification fails, the handshake is considered to have failed and the connection should be torn down.

- Receiver Change Cipher Spec. This message notifies the Originator that all messages that follow the Receiver Finished message will be encrypted using the keys and algorithms just negotiated.

- Receiver Finished. The Receiver sends an encrypted Receiver Finished message that contains a hash of the entire conversation to provide authentication of the Receiver.

If the Originator is able to successfully decrypt this message and validate the contained hash, it is assured that the authentication is successful, and the key computed on the Originator match this computed on the Receiver.

-----------------------End of 1st  change-------------------------------