| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC#10 |
| Title:* | Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Phil Hawkes, Qualcomm , phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2014-04-03 |
| Abstract:* | This contribution describes the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework. |
| Agenda Item:* |  |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate text into an appropriate section of the Security TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

See Note in SEC-2014-0243 “Overview of Security Frameworks”. Revision marks show the changes from R02.

An overview of the Security Bootstrap Frameworks is provided in SEC-2014-0247 “Overview of Security Bootstrap Frameworks” and subsequent revisions.

The revision marks in the “_rev” version show the changes from SEC-2014-0226R01.

==================<Start of Change 1 (New Text) >=================

### 8.3.2.1 The Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework

This clause describes the Pre-Provisioned Symmetric Key Security Bootstrap Framework.  The Bootstrap Credential for this framework is a long-term symmetric key that has been pre-provisioned into the Enrolee and M2M Enrolment Function; this key is called a Pre-Provisioned Symmetric Enrolee Key and is denoted Kee.

Note: Long term Pre-Provisioned Symmetric Enrolee Keys can pose a security risk if not adequately secured, and for this reason Long term Pre-Provisioned Symmetric Enrolee Keys are recommended to be stored in Secure Environments.

Figure 8.3.2.1-1 illustrates the sequence of events when using the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework.

Figure 8.3.2.1-1	The sequence of events when using the Pre-Provisioned Symmetric Key Security Bootstrap Framework.  See Table 8.2.1-1 for details of the abbreviations used in this table. The following font colours differentiate the general topic that the text relates to:

- Black text contains Security-Bootstrap-Framework-independent details

- Blue italic text highlights details specific to this particular Security Bootstrap Framework.

- Purple italic text highlights technical actions that may include steps not specified by oneM2M.

Bootstrap Credential Configuration: The Pre-Provisioned Symmetric Enrolee Key (Kee) and the corresponding Pre-Provisioned Symmetric Enrolee Key Identifier, denoted KeeId, are pre-provisioned to both entities. The Enrolee is also provisioned with the M2M Enrolment Function’s URI (MEF URI), for the purpose of routing the (D)TLS exchange.

Note:  This pre-provisioning (by definition) uses mechanisms not specified by oneM2M.

Bootstrap Instruction Configuration:  The Enrolee and M2M Enrolment Function are configured with the information needed for authorizing the remote provisioning:

  - The Enrolee is configured with (or otherwise obtains) the following arguments to initiate remote provisioning :

    - M2M Authentication Function identity (IdMAF): Identifying the M2M Authentication Function for which the Enrolee is to be provisioned.

    - Enrolee identity (IdEnrolee): the Enrolee is to use this identity with the identified M2M Authentication Function.

    - The Enrolee associates these arguments with the M2M Enrolment Function. The M2M Enrolment Function can be identified to the Enrolee using the Pre-Provisioned Symmetric Enrolee Key Identifier (KeeId) or the M2M Enrolment Function URI.

The mechanisms for achieving this are discussed in clause x.y.z.

  - M2M Enrolment Function is configured with the following arguments to authorize the M2M Enrolment Function to remotely provision the Enrolee for a M2M Authentication Function:

    - M2M Authentication Function Identity (IdMAF) of the M2M Authentication Function for which the Enrolee is to be provisioned.

    - Enrolee identity (IdEnrolee). The M2M Enrolment Function is to provision this identity to the Enrolee for use with the identified M2M Authentication Function.

    - The M2M Enrolment Function associates these arguments with an Enrolee. The Enrolee can be identified to the M2M Enrolment Function using the Pre-Provisioned Symmetric Enrolee Key Identifier (KeeId).

The mechanisms for achieving this are discussed in clause m.n.o.

Bootstrap Security Handshake: The Enrolee and M2M Enrolment Function perform a (D)TLS-PSK handshake [TLS-PSK RFC 4279] to establish a secure session.

- The “psk_identity” parameter [TLS-PSK RFC 4279] is set to the value of the Pre-Provisioned Symmetric Enrolee Key Identifier (KeeId).

- The “psk” parameter [TLS-PSK RFC 4279] is set to the value of the Pre-Provisioned Symmetric Enrolee Key (Kee).

Editor’s note: the applicable (D)TLS ciphersuites are FFS.

Temporary Enrolment Key Generation:

- The Temporary Enrolment Key (Kte) is generated from the (D)TLS session secrets by the Enrolee and M2M Enrolment Function using TLS Key Export (RFC 5705) [RFC5705], as described in Clause 8.3.6.

- The Temporary Enrolment Key Identifier (KteId) is generated by the Enrolee and M2M Enrolment Function, as described in Clause r.s.t.

- The Enrolee and M2M Enrolment store the Temporary Enrolment Key (Kte) and Temporary Enrolment Key Identifier (KteId).

Note: The Temporary Enrolment Key Generation for the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework is identical to the Temporary Enrolment Key Generation for the Certificate-Based Security Bootstrap Framework.

Usage in Centralized Key Distribution Server Handshake: See “Overview of Security Frameworks” in Clause 8.3.1.