| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 - SEC 10 |
| Title:* | Precisions on M2M Trust Functions |
| Source:* | Gemalto (ETSI) |
| Contact: | francois.ennesser@gemalto.com |
| Date:* | 2014-04-01 |
| Abstract:* | Attached contribution provides further precisions on the M2M Trust Functions and their respective usage. R01 clarifies / corrects the proposed text (Changes highlighted). |
| Agenda Item:* |  |
| Work item(s): | WI-0007 |
| Document(s) Impacted* | TS-0003 v0.3.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to changes to TS-0003 in revision marks. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### Proposed change:

In section 6.3.6 of TS-0003 v0.3.0, make changes highlighted below in revision marks:

### 6.3.6 Trust Enabler security functions

OneM2M Trust Enabling Architecture requires the presence of three security functionalities within the Infrastructure Domain: the M2M Authentication Function (MAF), the M2M Enrolment Function (MEF) and the M2M Authorization Function (MZF). They can be either under M2M Service Provider control or delegated to a M2M Trust Enabler.

- M2M  Enrolment Function (MEF)

The MEF supports the security bootstrap procedure enabling the provisioning of the Master Credentials to be used to authenticate entities accessing the infrastructure of an M2M Service Provider. The MEF relies on an initial credential pre-provisioned in the M2M node (e.g. during manufacturing). In case of M2M Security Remote Provisioning procedure, the MEF provides the M2M Master Credential both to the MAF and the SEC CSF of ASN/MN-CSE.

- M2M Authentication Function (MAF)

M2M Master Credentials, used to authenticate M2M Nodes before granting them access to M2M services, shall be securely stored. M2M Master Credentials shall be securely stored in a specific infrastructure functionality named M2M Authentication Function (MAF).

The MAF securely contains the set of M2M Master Credentials that are used for authenticating CSEs/AEs that have been enrolled for M2M services. The MAF stores the M2M Master Credentials and possibly the identifiers of the associated CSE/AE. The MAF is identified thanks to its MAF-ID.

When M2M Security Remote Provisioning procedure takes place to share a M2M Master Credential between an ASN/MN CSE and the M2M Authentication Function, the M2M Enrolment Function (MEF) communicates with the MAF through an appropriate secure interface, if not co-located.

The MAF is also in charge of all security operations involving the usage of the M2M Master Credentials.

- M2M Authorization Function (MZF)

The MZF is in charge of authorization aspects. It provides an M2M entity (AE or CSE) with authoritative proof that it may use specific M2M services, application, or privilege (i.e. apply an existing role to perform  specific operations on an M2M resource).