| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4(SEC) during SEC 10 |
| Title:* | Credentials definitions |
| Source:* | Gemalto |
| Contact: | Mireille Pauliac, Gemalto, mireille.pauliac@gemalto.com |
| Date:* | 2014-03-25 |
| Abstract:* | This contribution proposes definitions for credentials used in oneM2M security procedures. R01 modifies the definition of “Master Credentials”. |
| Agenda Item:* | TBD |
| Work item(s): |  |
| Document(s) Impacted* | oneM2M SEC TS-0003 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

This contribution proposes below abbreviations for credentials used in oneM2M security procedures. The changes to SEC TS-003 are indicated via revision marks.

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in [i.2] and the following apply:

Local CSF:  A CSF may provide services to another local CSF, i.e. a CSF that is present in the same CSE than the CSF providing the services.

Certificate: See Public Key Certificate

M2M Secure Connection Key: Key shared between two CSEs of M2M Nodes (e.g. ASN/MN-CSE and IN-CSE) in order to secure the communication between those two entities. This M2M Secure Connection Key results from a successful M2M Security Association Establishment procedure.

Master Credentials: Credentials used to mutually authenticate between an ASN/MN-CSE and the MAF. This is done to secure access to the infrastructure of an M2M Service Provider. The Master Credentials are either pre-provisioned or remotely provisioned (without relying on those credentials).

Policy Access Point: The system entity that finds applicable policy or policy set.

Policy Decision Point [i.7]: The system entity that evaluates applicable policy and renders an authorization decision.

Policy Enforcement Point [i.7]: The system entity that performs access control, by making decision requests and enforcing authorization decisions.

Policy Information Point [i.7]: The system entity that acts as a source of attribute values.

Public Key Certificate [i.4]: An electronic document that uses a digital signature to bind a public key with an identity.

Public Key Infrastructure [i.5]: a set of hardware, software, people, policies, and procedures needed to create, manage, distribute, use, store, and revoke Public Key Certificates