| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC |
| Title:* | Access Control Mechanism Part 2 |
| Source:* | LG Electronics |
| Contact: | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Date:* | 2014-03-31 |
| Abstract:* | This contribution proposes Access Control Mechanism of oneM2M R01: Alignment to 245R03 |
| Agenda Item:* | SEC |
| Work item(s): | WI 0002 |
| Document(s) Impacted* | Technical Specification – Security Solution |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve the proposed change and integrate it into the TS document |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Rationale

This contribution proposes new clause for Access Control Mechanism

========================Start of 1st Change==========================

### X.X.X.1 Hosting CSE acting as PEP and IN-CSE acting as PDP

In this case, Hosting CSE works PEP and IN-CSE works PDP functionality as described in clause 6.3.2. When a request message is received by the Hosting CSE, the Hosting CSE sends access control decision request to IN-CSE and gets access control response from IN-CSE. The request contains the identifier of the Originator, the operation to be executed, and the target resource URI. It may also include an access token applied for access control.

The Hosting CSE and IN-CSE shall perform following steps to validate the Request to access a target resource.

Editor’s note: FFS for the interface between Hosting CSE and IN-CSE and request/response of the interface.

Step 001:	When Hosting CSE receives a request from an Originator, Hosting CSE makes an access control decision request based on the information in Originator’s request and sends the access control decision request to IN-CSE.

Step 002: 	IN-CSE verifies the M2M Service Subscription details of the Originator. This step is specified in clause X.X.X.3 M2M Service Subscription verification.

Step 003:	If the M2M Service Subscription Verification is validated, the IN-CSE proceeds to step 3.

In this step, the Hosting CSE verifies whether Originator has sufficient privileges to perform the request by checking <accessControlPolicy> resource that applies to the targeted resource

This step is specified in clause X.X.X.4 Access Control Policy verification.

Step 004: 	IN-CSE sends access control decision response. If both step 2 and step 3 have been passed, the response contains “access granted”. If any of step 2 and step 3 is not passed, the response contains “access denied”.

Step 005:	Hosting CSE performs the request only if the response of step 4 has “access granted”.

After this procedure, Hosting CSE sends proper response to the Originator.