| CHANGE REQUEST |
| --- |
| Group Name:* | REQ |
| Source:* | LG Electronics, Oberthur Technologies |
| Format:* | Plenary |
| Date:* | 2014-04-29 |
| Contact:* | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com Dragan Vujcic, v.dragan@oberthur.com |
| Reason for Change/s:* | Alignment of Acces Control voucabulary for consistancy with ARC TS R02: considering all the comments during SEC 10.3 conference call. |
| CR against: Release* | Release 1 |
| CR against: TS/TR* | TS-0011 V0.5.0 |
| Clauses/Sub Clauses* | Clause 3.17 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

Privilege definition is not consistant with ARC TS. Originally privilege means allowed operations (currently called operationFlags in ARC TS). To be able to align, this contribution proposes to change Privilege definition.

### -----------------------Start of change 1-------------------------------------------

Access Control Attributes: Set of parameters of the originator, target resource, and environment against which there could be rules evaluated to control access.

NOTE:	An example of Access Control Attributes of Originator is a role. Examples of Access Control Attributes of Environment are time, day and IP address. An example of Access Control Attributes of targeted resource is creation time.

Access Decision:  Authorization reached when an entity’s Privilegesare evaluated

Privilege:  Qualification given to an entity that allows a specific operation (e.g. Create/Retreive/Update/Delete, etc.) on a specific resource  within a specified context.

### -----------------------End of change 1---------------------------------------------