| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC WG4 |
| Title:* | General Mutual Authentication Mechanism |
| Source:* | OBERTHUR Technologies, CATT, BT Group |
| Contact: | Dragan Vujcic, Oberthur Technologies, v.dragan@oberthur.com Wei Zhou, zhouwei@catt.cn Colin Blanchard, colin.blanchard@bt.com |
| Date:* | 2014-03-31 |
| Abstract:* | This contribution proposes a informative section in the SEC TS 0003 for General Mutual authentication Mechanism applied to both symmetric and asymmetric key based schemes |
| Agenda Item:* | Tbd |
| Work item(s): |  |
| Document(s) Impacted* | SEC TS-0003 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

- Introduction

Many of deployed cryptography systems use the concept where an entity can identify itself to another entity without giving anything away that an eavesdropper could use. An entity is securely identified to a second entity where no exchange of key material or subsequent non-repudiation of the identification is required. The used concept allows a entity to prove that it knows about credentials, without having to exchange the value of the credentials.

The same techniques should be used as a promising way of providing CSEs with an efficient and flexible mutual authentication procedure that could be used to meet existing and future oneM2M security requirements. A pre-requisite is that the CSE’s Master key shall be stored in a secure a way in the SEC CSF secure environment as a means to protect against attacks of stored and processed related information.

This contribution proposes a section in the SEC TS 0003 for General Mutual Authentication Mechanism applied to both symmetric and asymmetric key based schemes.

- Proposal

-------------------------------------------Start -------------------------------------------------

Annex X. General Mutual Authentication Mechanism

oneM2M mutual authentication schemes allow oneM2M entities to prove that they know related credentials such as Master Credentials, without having to exchange value of those credentials, and sensitive data such as identities and identifiers. To prevent reading and copying of credentials, a secure environment within the Security CSF provides protection against tampering of those credentials and related processed information.

Editor’s Note: It needs to be defined which oneM2M identities represent sensitive data that should not be exchanged over the communication link between entities A and B.

A general mutual authentication protocol is applied to both symmetric and asymmetric key based schemes. Precise protocol messages and parameters depend on the chosen scheme and the security parameters selected. Typically it consists of following steps:

Figure X: Mutual Authentication

Editor’s Note: Adding a reference to an existing and suitable Challenge Response scheme/specification/standard is FFS.

1.	An initial step where an entity A is securely identified to an entity B with whom previous or no previous contact has been made. In this step entity A identifies itself to an entity B protected against eavesdropping, i.e. no exchange of key material (Master Credential).

2.	In the second step entity B sends a challenge to entity A. The Authentication challenge consists of random challenge, authentication token of entity B derived from Master credentials, etc. The authentication challenge depends on the chosen scheme and the security parameters selected for symmetric and asymmetric key based schemes.

3.	The entity A replies with an authentication response derived from its known Master Credentials and the received Athentication challenge. This response is sent if entity B has been successfully authenticated by entity A.

4.	Entity B then verifies the relation between entity A’s identity and the response received in step 3, which gives a high probability that the entity B knows a secret value associated with the entity A’s identity provided in step 1.

-------------------------------------------End -------------------------------------------------

# Comments

“must” is misleading since some other SDOs use “must” as normative text.