| CHANGE REQUEST |
| --- |
| Group Name:* | WG2 |
| Source:* | SEC WG4 |
| Format:* | ARC#10 |
| Date:* | 2014-03-31 |
| Contact:* | Dragan Vujcic, v.dragan@oberthur.com |
| Reason for Change/s:* | Alignemnt with the access control terminology |
| CR against: Release* | 1 |
| CR against: TS/TR* | TS-0001 v0.4.3 |
| Clauses/Sub Clauses* | 9.6.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes alighment with the definitions of the access control terminology. In addition as per minutes of TP#9  to remove “list “ by making sure the accessControlPolicy defines the set of rules and privileges  that each entity must comply with to grant access to an object. The agreed acces control terminilofy are reminded below:

Access Control Attributes: Set of parameters of the originator, target resource, and environment against which there could be rules evaluated to control access.

NOTE:	An example of Access Control Attributes of Originator is a role. Examples of Access Control Attributes of Environment are time, day and IP address. An example of Access Control Attributes of targeted resource is creation time.

Access Decision:  Authorization reached when an entity’s Privileges, as well as other Access Control Attributes, are evaluated

Privilege: Qualification given to an entity that allows a specific operation (e.g. Read/Update) on a specific resource (e.g.: an entry in ACL specifies a privilege, not an Access Decision).

NOTE:	In addition to being granted a Privilege, the entity must also satisfy any conditions of the Access Control Attributes.

## -----------------------Start of change 1-------------------------------------------

### 9.6.2	Resource Type accessControlPolicy

The <accessControlPolicy> resource is comprised of  privileges and selfPrivileges attributes which represents access control rules defining "allowed" entities (defined as accessControlOriginator) for certain access modes (defined as accessContolOperationFlags) within a specified context (defined as accessControlContexts) .

The selfPrivilege attribute lists those that are allowed to Read/Update/Delete for the <accessControlPolicy> resource itself.

Each attribute  may also refer to a subscriber group described in a <m2mServiceSubscripion> resource. Such subscriber group is identified by a subscriber group name and a URL addressing a <m2mServiceSubscription> resource where such subscriber group is defined. In case the originator is presenting itself with a specific subscriber group, the access control policy operates by matching the request originator with the list belonging to such specific subscriber group as described in the <m2mServiceSubscription> resource (achieved by partial addressing).

By setting an accessControlPolicyID attribute on a resource, the access decision for that resource are then granted by evaluating access control rules access control rule by the privileges attribute defined in the <accessControlPolicy> resource.

The selfPrivilege attribute lists those that have the rights to Read/Update/Delete for the resource <accessControlPolicy> itself.

By setting an accessControlPolicyID attribute on a resource, the access decision for that resource is then defined by evaluating attributes defined in the <accessControlPolicy> resource.

Access control procedures using the <accessControlPolicy> resource is specified in TS-0003.

{9.6.2.a} Editor's Note: There is a need for a global replacement of accessRight with accessControlPolicy, accessRightsID with accessControlPolicyID, permission with privilege.

Figure 9.6.2-1: Structure of <accessControlPolicy> resource 
(only resource specific attributes are shown)

{9.6.2.b} Editor's Note: To update the picture to include "link", "announceTo" and "announcedAttribute" attribute.

# Table 9.6.2-1: Child resources of <accessControlPolicy> resource

| Child Resource Name of <accessControlPolicy> | Child Resource Type | Multiplicity | Description | <accessControlPolicyAnnc> Child Resource Type |
| --- | --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 | <subscriptionAnnc> |

{9.6.2.c} Editor's Note: Contribution ARC-2014-0089R03 does not provide the table for the <subscription> child-resource. The contributor to verify the accuracy of the proposal.

This resource shall contain the attributes according to their multiplicity in Table 9.6.2-2 (0 indicates the optionality of the attribute).

# Table 9.6.2-2: Attributes of <accessControlPolicy> resource

| Attribute Name of <accessControlPolicy> | Multiplicity | RW/ RO/ WO | Description | <accessControlPolicyAnnc> Attribute |
| --- | --- | --- | --- | --- |
| resourceType (rT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| parentID (pID) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| expirationTime (eT) | 1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| labels (lBs) | 0..1 | RW | See clause 9.6.1 where this common attribute is described. | MP |
| creationTime (cT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| lastModifiedTime (lMT) | 1 | RO | See clause 9.6.1 where this common attribute is described. | MP |
| Link | 1 | WO | See section 9.6.1 where this common attribute is described. This is only for <accessControlPolicyAnnc>. | MP |
| announceTo | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| announcedAttribute | 1 | RW | See section 9.6.1 where this common attribute is described. | NP |
| privileges (ps) | 1 | RW | Represents an access control rule defining "allowed" entities for certain access modes within a specified. this rule is applied to resources referencing this <accessControlPolicy> resource using the accessControlPolicyID attribute. . | OP |
| selfPrivileges (sP) | 1 | RW | Defines an access control rule for the <accessControlPolicy> resource itself. | OP |

{9.6.2.d} Editor's Note:  Mechanisms for announcing are FFS.

The privileges attribute could be generalised to actions (which might be granting access, but might also be more specific, like granting access to a subset, i.e. filtering part of the data). The privileges attribute could be generalised to conditions, which may include the identity of the requestor, everybody except specified identities, but it might also include time based conditions, etc.

Selfprivileges and privileges attributes are both lists of originator privilege associated with privilege flags applied respecively to <accessControlPolicy> resource itself (selfprivileges) and to all other resource types addressing the <accessControlPolicy> resource with the accessControlPolicyID common attribute (privileges).

The access granting mechanism, specified in TS-0003, based on access control policy operates by evaluating  privileges and selfPrivileges attributes with the associated subscribtion.  Each privilege in the privileges and selfprivileges lists is constituted by the following parameters

Table 9.6.2-3: Parameters of Privileges

| Name | Description |
| --- | --- |
| accessControlOriginator | See 9.6.2.1 |
| accessControlContexts | See 9.6.2.2 |
| accessControlOperationFlags | See 9.6.2.3 |

#### 9.6.2.1	accessControlOriginator

The following originator privilege types shall be considered for access control policy check. as defined in TS 003.

Table 9.6.2.1-1: accessControlOriginator Parameter

| Name | Description |
| --- | --- |
| originator identifier | CSE-Id or AE-ID which represent a originator identity |
| Token | Access token usually provided as query parameter |
| All | All originators |
| Subscriber Group | A subscriber group name associated with the URL the a M2M Service Subscription resource where such subscriber group(subsGroup) is defined |

#### 9.6.2.2	accessControlContexts

The following originator contexts privilege types shall be considered for access control policy check as defined in TS 003.

Table 9.6.2.2-1: accessControlContexts Parameter

| Name | Description |
| --- | --- |
| Context | Defines the context in which every privileges of the present access control policy resource applies, e.g. time windows, location, IP address. Editor’s note: the detailed definition for the access con trol context is FFS. |

#### 9.6.2.3	accessControlOperationFlags

The following originator operation privilege flags shall be considered for access control policy check  as definied in TS 003.

Table 9.6.2.3-1: accessControlOperationFlags Parameter

| Name | Description |
| --- | --- |
| RETRIEVE | Privilege to retrieve the content of an addressed resource |
| CREATE | Privilege to create a child resource |
| UPDATE | Privilege to update the content of an addressed resource |
| DELETE | Privilege to delete an addressed resource |
| DISCOVER | Privilege to discover the resource |
| NOTIFY | Privilege to receive a notification |

{9.6.2.3.a} Editor’s Note:  A non-verbose  privilege flag description could be the following: <pf>RcUeDN</pf> that means: RETRIEVE allowed, CREATE not allowed, UPDATE allowed, DELETE not allowed, DISCOVER allowed, NOTIFY allowed.

## -----------------------End of change 1-------------------------------------------

# Comments

I think this sentence is not necessary as we said above that access control rule is defined within a specified context, with attributes listed in accessControlcontext.

Do we need this description in stage 2 or should it be in stage 3 decribed by TS-003 ?

Moved  above

Can this redundant text  be rermoved ?

Moved above

I don’t see a need for this since CSE-ID is a form of FQDN.