| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC |
| Title:* | Secure Channel |
| Source:* | Giesecke & Devrient |
| Contact: | Claus Dietze |
| Date:* | 2014-06-03 |
| Abstract:* | This contribution proposes to introduce a secure channel on the Mca reference point |
| Agenda Item:* | Security TS |
| Work item(s): | WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Accept this proposal as baseline for the Security API and allow further contributions in this direction |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This document proposes to add a secure channel protocol that is applied between entities residing in the same physical device within the field domain. A reference to existing standards is made to include that security feature.

Several security associations have to be distinguished:

### -----------------------Start of change 1-------------------------------------------

# 6	Security CSF Components and Interactions

## 6.1	Interaction on Reference Points

### 6.1.1	Mca-Reference Point

The Security API offers its functions to ADN-AEs, ASN-AEs and MN-AEs through the Mca-Reference point. Implementation of the Security API is dependent on the operating system of the physical device it resides in.

Editor’s note: Categories of physical devices are currently discussed in WI-0006. Depending on the outcome of this WID, definitions of Security CSF may have to be adapted.

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 6.3.3	Security Association Establishment

This component shall provide functions to establish a security association between different entities. Following cases are distinguished:

- End to end secure connection between entities distributed over the Field Domain and Infrastructure Domain and communicating over multiple reference points, e.g. between ASN-AE and IN-AE

- Secure connection between entities residing in the field domain

- Security Association between SE and CSE, if the SE resides within a field domain CSE

In addition, the Security Association Establishment component shall be able to use an existing security association to perform the following functions:

- Set up a Secure Connection via secure session establishment.

- Set up a Secure Connection via object security.

The Security Association Establishment component may rely on an external M2M Authentication Function to establish security associations.

Editor’s note: to be completed.

#### 6.3.3.2	CSE to SE security association

In case a security association between a SE and a CSE is required, a secure channel shall be established between the two.

In case the SE is implemented as a Secure Element as defined in [ETSI TS 102221] a secure connection shall be established as specified in [b].

Editor’s note: Suitability of a Secure Channel Protocol (SCP) according to [a] is FFS.

Editor’s note: introduction of security reference points may be required and is FFS. The CSE to SE security association applies to the security reference point.

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of Changes to References Section -------------

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

[2]	Open Mobile API specification V2.0.5

[a]	GlobalPlatform Card Technology Secure Channel Protocol 03, Version 1.1

[b]	ETSI TS 102 484 Secure channel between a UICC and an end-point terminal

### -----------------------End of Changes to References  -------------

### -Start of changes to Definitions Symbols Abbreviations Acronyms -

# 3	Definitions, symbols, abbreviations  and acronyms

## 3.3	Abbreviations

SCP	Secure Channel Protocol

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---