| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC |
| Title:* | Secure Channels |
| Source:* | Giesecke & Devrient (ETSI), Gemalto (ETSI) |
| Contact: | Claus Dietze |
| Date:* | 2014-06-03 |
| Abstract:* | This contribution (R03) proposes clarification to Section 6 on Security associations. |
| Agenda Item:* | Security TS |
| Work item(s): | WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Accept this proposal as baseline |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This document proposes clarifications to section 6 on Secure connections.

Note that proposed text in revisions earlier than R02 on Secure channel has moved to a more appropriate place in SEC-2014-0276R03.

### -----------------------Start of change 1-------------------------------------------

# 6	Security CSF Components and Interactions

## 6.1	Interaction on Reference Points

### 6.1.1	Mca-Reference Point

The Security API offers its functions to ADN-AEs, ASN-AEs and MN-AEs through the Mca-Reference point. Implementation of the Security API is dependent on the operating system of the physical device it resides in.

Editor’s note: Categories of physical devices are currently discussed in WI-0006. Depending on the outcome of this WID, definitions of Security CSF may have to be adapted.

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 6.3.3	Security Association Establishment

This component shall provide functions to establish  secure connections between CSEs in the Field Domain and and IN-CSE, to protect the infrastructure of an M2M Service Provider.

NOTE 1: Such secure connections provide hop-by-hop protection to information exchange by M2M applications.

- NOTE 2 : Use of hop-by-hop connection by AEs assumes trust in the M2M SP. For AEs affiliated with different M2M SP, this also implies that M2M SPs are part of a circle of trust.In addition, the Security Association Establishment component shall be able to use an existing security association to set up a Secure Connection via secure session establishment.

The Security Association Establishment component may rely on an external M2M Authentication Function to establish security associations.

### -----------------------End of change 2-------------------------------------------