| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC |
| Title:* | Security API |
| Source:* | Giesecke & Devrient Group |
| Contact: | Claus Dietze |
| Date:* | 2014-06-03 |
| Abstract:* | This contribution proposes some basic concepts and ideas for the Security API |
| Agenda Item:* | Security TS |
| Work item(s): | WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Accept this proposal as baseline for the Security API and allow further contributions in this direction |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This document proposes to add API functions enabling differnet types of AEs to call certain security services of the security CSF. The API is offered on the Mca reference point and in a first version only applies to the field domain. The document is intended as a starting point and is not complete. The intention is to agree on the basic principle to add such an API to the specification.

In addition the document proposes to add some security service related resources. Those resources are kept within the security CSF or the SE respectively. The resources are accessible via the security API and managed via the security administration API or other administration interfaces such as OTA.

To support this the present document outlines:

- Basic principle that the API only applies to field domain and the Mca

- Several API functions

- References to dedicated SE such as Secure Element and TEE

- Update to the resource structure, clarifying that those resources are kept within the SE

### -----------------------Start of change 1-------------------------------------------

# 7	Security  Services

## 7.1	Overview

The Security API (S-API) as defined within the present clause applies to the following field domain nodes:

- Application Dedicated Node

- Application Service Node

- Middle Node

Editor’s note: definition of a S-API for infrastructure domain components is FFS.

The S-API is made available on the Mca reference point as part of the Mca API and provides high level Security Service API (SSer-API) methods for all security functions within the security functions layer as depicted  in figure 5-1. The SSer-API relies on the Secure Environment Abstraction layer that is responsible to accomplish the communication to the secure environments available within the Secure Environment Layer.

### 7.2	Generic Methods

Depending on the CSE configuration, the security functions and levels as well as the Secure Environments may vary. For this purpose an API is required to discover available security functions, levels and environments.

The following generic methods shall be implemented:

openSession(): Establishes an active session between the AE and the Security CSF. An active session is required to use any security function.

Editor’s note: Method details / parameters to be completed.

closeSession(): Close a previously opened session.

Editor’s note: Method details / parameters to be completed.

GET_SecLevel(): Returns the list of available security levels of the available Secure Environments.

Editor’s note: Method details / parameters to be completed.

GET_SE(): Detects the types and characteristics of all available Secure Environments available within the respective field domain CSE. The GET_SE() method returns the Secure Environment Attribute as defined in clause 5.2.

Editor’s note: Method details / parameters to be completed. In addition the Secure Environment Resource in clause 5.2 needs to be completed

SELECT_SE(): Selects the indicated Secure Environment based on the SE security level and/or the SE_ID. Other parameters may be provided by the AE.

Editor’s note: Method details / parameters to be completed. In addition the Secure Environment Resource in clause 5.2 needs to be completed

GET_SESecLevel(): Returns the security level associated to a particular secure environment.

Editor’s note: Method details / parameters to be completed.

## 7.3	Secure Environment Abstraction

The Secure Environment Abstraction API (SAb-API) provides a communication framework to the secure environment. The physical communication to the SE depends on its characteristics and its integration within the Security CSF. Following types of SEs are distinguished within the scope of the present document:

- Secure Element as defined in [x]

- TEE as defined in [za]

Editor’s note: additional Secure Environments are FFS.

7.3.1	Secure Element

If the Secure Environment is implemented as a Secure Element according to [x] the Secure Environment Abstraction shall be implemented according to the Transport API as defined in [2].

### 7.3.2	TEE

If the Secure Environment is implemented as a TEE according to [za] the Secure Environment Abstraction shall be implemented as defined in [3].

## 7.4	Security Services API

## 7.4.1	Authorization

The following Authorization API functions shall be supported:

authorize(REQUESTER, ENTITY, OPERATION): Authorizes REQUESTER within the SE to get access to ENTITY in order to perform indicated OPERATION.

Boolean isAuthorized(REQUESTER, OPERATION): checks the authorization status of REQUESTER.

Editor’s note: to be completed

## 7.4.2	Sensitive Data Handling

Sensitive Data Handling provides access to data securely stored within the SE. Following functions shall be supported:

storeData(AE_ID, SE_ID, DATA): stores DATA of the associated AE within the secure storage of the indicated SE

retrieveData(AE_ID, SE_ID, DATA): retrieves the DATA associated to the given AE from the indicated SE and transfers it to the authorized AE

deleteData(AE_ID, SE_ID, DATA): deletes DATA of the calling entity AE_ID from the indicated SE if it is authorized to perform this activity.

Boolean hasValue(): checks if data is stored for a specific AE.

Editor’s note: Mapping to respective APIs as defined in [2] and [3,y] to be added in case the SE is a Secure Element or a TEE is FFS

Editor’s note: further functions are FFS.

## 7.4.3	Security Association

The Security Association API provides methods to establish a secure connection between entities. This API shall be implemented for the following scenarios:

- Secure connection establishment between ADN-AE and MN-CSE

- Secure connection establishment between ASN-AE and ASN-CSE

- Secure connection establishment between MN-AE and MN-CSE

NOTE: This API is not applicable for a secure connection establishment between ADN-AE and IN-CSE.

The following methods shall be supported:

OpenChannel()

CloseChannel()

SelectChannel()

isChannelEstablished()

Editor’s note: to be completed.

Editor’s note: Reference to [a] and [b] ETSI or GP secure channel is FFS.

## 7.4.4	Security Administration

Provides functions to securely administer the content of the SE locally. Remote administration as defined in clause 6.3.4.1 is not considered within this clause.

Editor’s note: add API functions required to provide Security Administration here.

Editor’s note: references to GP specifications are FFS.

## 7.4.5	Identity Management

Editor’s note: add API functions required to provide Identity Protection here.

## 7.4.6	Identification and Authentication

Provides authentication functions to perfom mutual authentication as defined in Annex X (General Mutual Authentication Mechanism).

Editor’s note: Mapping to Authentication Service API as defined in [2] to be added in case the SE is a Secure Element is FFS

Editor’s note: add API functions required to provide Authentication Service here.

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

## 5.2	Resource Structure

## 5.2.1	Resource Type SecurityService

A <SecurityService> resource represents information about certain security services provided by a given CSE to an AE. The <SecurityService> resource shall be implemented within the Secure Environment of the given CSE. Modifications of the <SecurityCapability> resource shall only be possible via respective Security Administration functions.

Figure 5-2: Security CSF resource structure

Editor’s note: Resource and attribute structure will be completed if the general approach is agreeable.

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of Changes to References Section -------------

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

[2]	Open Mobile API specification V2.0.5

[3]	GlobalPlatform Device Technology TEE Client API Specification, Version 1.0

[a]	GlobalPlatform Card Technology Secure Channel Protocol 03, Version 1.1

[b]	ETSI TS 102 484 Secure channel between a UICC and an end-point terminal

[y]	GlobalPlatform Device Technology TEE Internal API Specification, Version 1.0

[za] 	GlobalPlatform Device Technology TEE System Architecture, Version 1.0

[x]		ISO/IEC 7816-4 Identification cards - Integrated circuit cards - Part 4: Organisation, security and commands for interchange

### -----------------------End of Changes to References  -------------

### -Start of changes to Definitions Symbols Abbreviations Acronyms -

# 3	Definitions, symbols, abbreviations  and acronyms

## 3.3	Abbreviations

SECCSF_ID	Security CSF Identifier

SE_ID	Secure Environment Identifier

SF_SE_ID	Secure Environment Identifier supporting a specific Security Function

SF_ID	Security Function Identifier

SF_SEC_Level	Security Level offered by a dedicated Security Function

TEE	Trusted Execution Enviroment

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---