| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC |
| Title:* | Overall Access Control Mechanism |
| Source:* | LG Electronics |
| Contact: | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Date:* | 2014-05-31 |
| Abstract:* | This contribution proposes Access Control Mechanism of oneM2M R01: Applying comments received at SEC Ad-hoc meeting(14 May). PAP works as PDP when PEP and PDP are separated. Add reference to Applying Access Control Policies: High Level Description (Qualcomm’s contribution SEC-2014-0285R05) |
| Agenda Item:* | SEC |
| Work item(s): | WI 0002 |
| Document(s) Impacted* | Technical Specification – Security Solution |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve the proposed change and integrate it into the TS document |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Rationale

This contribution proposes new clause for Access Control Mechanism

========================Start of 1st Change=========================

### 7.3.X	Access Control Mechanism

This clause specifies the access control mechanisms. Following two cases are supported:

- Case 1: Hosting CSE acts as both PDP and PEP.

- Case 2: Hosting CSE acts as PEP; IN-CSE acts as PDP

### 7.3.X.1 Hosting CSE acting as PEP and PDP

In this case, Hosting CSE provides the PEP and PDP functionality as described in clause 6.3.2. When a request message is received by the Hosting CSE, the Hosting CSE shall check whether the request to access a target resource can be granted or not. The request contains the identifier of the Originator, the operation to be executed, and the target resource URI. It may also include an access token, a role and/or subscriber group applied for access control.

The Hosting CSE shall perform following steps to validate the Request to access a target resource.

Figure X.X.X.1-1 Hosting CSE acting as PEP and PDP

Step 001:	When Hosting CSE receives a request from an Originator and the Originator is an AE, The Hosting CSE verifies the M2M service role. When Originator is a CSE, this step is considered to be passed. This step is specified in clause X.X.X.3 M2M Service Role verification.

Step 002: 	In this step, the Hosting CSE verifies whether Originator has sufficient privileges to perform the request by checking <accessControlPolicy> resource that applies to the targeted resource.

This step is specified in clause X.X.X.4 Access Control Policy verification.

Step 003:	If both step 1 and step 2 have been passed, the Hosting CSE performs the request.

After this procedure, Hosting CSE sends a proper response to the Originator.

### 7.3.X.2 Hosting CSE acting as PEP and PAP acting as PDP

In this case, Hosting CSE works PEP and IN-CSE works PDP functionality as described in clause 6.3.2. When a request message is received by the Hosting CSE, the Hosting CSE sends access control decision request to IN-CSE and gets access control response from IN-CSE. The request contains the identifier of the Originator, the operation to be executed, and the target resource URI. It may also include an access token, a role and/or subscriber group applied for access control.

The Hosting CSE and IN-CSE shall perform following steps to validate the Request to access a target resource.

Editor’s note: FFS for the interface between Hosting CSE and IN-CSE and request/response of the interface.

Figure X.X.X.1-2. Hosting CSE acting as PEP and PAP acting as PDP

Step 001:	When Hosting CSE receives a request from an Originator, Hosting CSE makes an access control decision request based on the information in Originator’s request and sends the access control decision request to PDP which hosts <accessControlPolicy> resource.

Step 002: 	PDP verifies the M2M service role only when Originator is an AE. When Originator is a CSE, this step is considered to be passed. This step is specified in clause X.X.X.3 M2M Service Role verification.

Step 003:	In this step, the PDP verifies whether Originator has sufficient privileges to perform the request by checking <accessControlPolicy> resource that applies to the targeted resource

This step is specified in clause X.X.X.4 Access Control Policy verification.

Step 004: 	PDP sends access control decision response. If both step 2 and step 3 have been passed, the response contains “access granted”. If any of step 2 and step 3 is not passed, the response contains “access denied”.

Step 005:	Hosting CSE performs the request only if the response of step 4 has “access granted”.

After this procedure, Hosting CSE sends proper response to the Originator.

### 7.3.X.3	M2M Service Role verification

The subsSer&RoleList attribute of <m2mServiceSubscription> resource in TS-0001[TS0001] describes which AEs have the privilege to perform which operations on which resource types. For this purpose, M2M service role shall be checked in order to verify if the subscribed services and roles match the Originator request. This verification shall perform only when Originator is AE.

For example, an Originator is subscribed only to  M2M service role “Data exchange” (see Annex G of TS-00001[TS0001]) on Hosting CSE and the M2M service role allows the Originator to perform Create, Retrieve, Update, and Delete operations on the <container> resource type. Then the request of Create, Retrieve, Update, or Delete operation from Originator is authorized to perform on <container> resource by M2M Service Subscription. Therefore if the request is to access other resource types than <container> resource type, then the request fails to be authorized in this step. If the request is to Create, Retrieve, Update or Delete <container> resource type, then the request is authorized in this step.

All <m2mServiceSubscription> resources are stored in an IN-CSE. For case 1, to enable a Hosting CSE to perform M2M Service Role Verification, the Hosting CSE shall internally keep <m2mServiceSubscription> resources which are applied by the resource hosting CSE and synchronize those resources with the ones in the IN-CSE. How to synchronize is not defined in this specification.

M2M Service Role Verification procedure shall happen at PDP and the procedure is described as follows:

- PDP finds <m2mServiceSubscription> resources which belong to the Originator by considering App-ID and where the Originator resides (distinguished by appID attribute of the <m2mServiceSubscription> and by appID attribute of <nodeInfo> in the <m2mServiceSubscription>).

- PDP checks whether any of M2M service roles in <m2mServiceSubscription> resources found at step 1 contains the requested operation pertaining to resource type of the target resource.

- If PDP finds a matching M2M service role, M2M Service Role verification has passed successfully

- If PDP does not find any matching <m2mServiceSubscription> resources, M2M Service Role validation has failed. The PDP shall then send a respective response, and shall not proceed to step 2.

### 7.3.X.4	Access Control Policy verification

To be able to verify access control policy, PDP shall find the <accessControlPolicy> resource applicable to the target resource.

Editor’s note: how to find <accessControPolicy> resource is FFS. If the target resource doesn’t have accessControlPolicyID, the PDP finds <accessControPolicy> resource by using accessControlPolicyID of the parent resource. If the target resource doesn’t have accessControlPolicyID also at the parent resource, how to select access control policy resource is FFS.

After finding the <accessControlPolicy> resource, the procedures in 7.3.z shall be performed.

========================End of 1st Change==========================