| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC#11 |
| Title:* | Annex X.2.1 High Level Requirements for Bootstrap Credential Configuration |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Phil Hawkes, Qualcomm , phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2014-06-02 |
| Abstract:* | This contribution provides text for Annex X.2.1 containing High Level Requirements for Bootstrap Credential Configuration |
| Agenda Item:* |  |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate text into Security TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

------start of change 1------

### X.2 High Level Requirements for Security Bootstrap Framework Phases

### X.2.1 High Level Requirements for Bootstrap Credential Configuration Phases

Table X.2.1-1 recalls the information configured to various entities and functions during Bootstrap Credential Configuration phase of supported Security Bootstrap Frameworks.

Table X.2.1-1	Information configured to various entities and functions during Bootstrap Credential Configuration phase of supported Security Bootstrap Frameworks (see Figure 8.3.1.2-1 “Overview of the Security Bootstrap Frameworks…”. Examples of Underlying Network Service Provider (UNSP) Authentication Servers include HLR, HSS and AAA.

| Security Bootstrap Framework | Information configured during Bootstrap Credential Configuration to: |
| --- | --- |
|  | Enrolee | MAF | MEF | UNSP Authn Server |
| Pre-Provisioned Symmetric Enrolee Key | Enrolee-to-MEF | Kpm, KpmId, MEF URI | Not applicable | Kpm, KpmId | Not applicable |
|  | MAF-to-MEF | Not applicable | PrivateKeyMAF, CertMAF containing MAF’s FQDN, ChainMAF, RootOfTrustBSF | PrivateKeyMEF, CertMEF containing MEF’s FQDN, ChainMEF, RootOfTrustMAF | Not applicable |
| Certificate Based | Enrolee-to-MEF | PrivateKeyEnrolee, CertEnrolee, (Opt) ChainEnrolee | Not applicable | PrivateKeyMEF, CertMEF, (Opt) ChainMEF | Not applicable |
|  | MAF-to-MEF | As for Pre-Provisioned Symmetric Enrolee Key |
| GBA-Based | Enrolee (UE)-to-UNSP | Out of scope | Not applicable | Not applicable | Out of scope |
|  | MAF-to-MEF (NAF-to-BSF) | Not applicable | Details specified in [13]. Includes PrivateKeyNAF, CertNAF containing NAF’s FQDN, ChainNAF, RootOfTrustBSF | (MEF=BSF) Out of scope. Note: includes PrivateKeyBSF, CertBSF containing BSF’s FQDN, ChainBSF, RootOfTrustNAF [13] | Not applicable |

The details that are within the scope of oneM2M are:

- Bootstrap Credential Configuration of Enrolees, see Clause X.2.1.1,

- Bootstrap Credential Configuration of M2M Enrolment Functions, see Clause X.2.1.2,

- Bootstrap Credential Configuration of M2M Authentication Functions, see Clause X.2.1.3.

Applicability: Bootstrap Credential Configuration involves pre-provisioning which is (by the oneM2M definition) not specified by oneM2M. The requirements in this clause are provided as guidelines.

### X.2.1.1 High Level Requirements for Bootstrap Credential Configuration of Enrolees

In the Bootstrap Credential Configuration phase, it is necessary to configure the Enrolee with the information shown in Table X.2.1.1-1 (copied from Table X.2.1-1).

Table X.2.1.1-1	Information configured to Enrolee during Bootstrap Credential Configuration phase of supported Security Bootstrap Frameworks. Examples of Underlying Network Service Provider (UNSP) Authentication Servers include HLR, HSS and AAA.

| Security Bootstrap Framework | Information configured during Bootstrap Credential Configuration to: Enrolee |
| --- | --- |
| Pre-Provisioned Symmetric Enrolee Key | Enrolee-to-MEF | Kpm, KpmId, MEF URI |
| Certificate Based | Enrolee-to-MEF | PrivateKeyEnrolee, CertEnrolee, (Opt) ChainEnrolee |
| GBA-Based | Enrolee (UE)-to-UNSP | Out of scope |

Bootstrap Credential Configuration for the GBA-Based Security Bootstrap Framework is described in 3GPP, 3GPP2 and ETSI specifications, and is not discussed further.

Regarding Confidentiality: If an adversary compromises the confidentiality of Kpm or the Enrolee’s Private Key (PrivateKeyEnrolee), then the adversary has complete control over the Enrolee. The priority of maintaining the confidentiality of Kpm/ PrivateKeyEnrolee is at least as high as the cumulative priority of maintaining the confidentiality and integrity of all data that is stored, processed, sent or received by the Enrolee. Unless a thorough threat analysis is performed by a security expert, it should be assumed that the impact of a loss of confidentiality of Kpm/ PrivateKeyEnrolee is high to very high, and the priority of maintaining confidentiality Kpm/ PrivateKeyEnrolee is high to very high.

If confidentiality of KpmId is compromised by an adversary, then that adversary obtains some information about which KmpId is associated with which Enrolee. This provides a very small advantage over information that might be obtained through traffic analysis. In many scenarios, this loss of confidentiality poses a low to medium risk, and encryption of KpmId is a low to medium priority. In cases where KpmId can be generated directly from Kpm, it is not necessary to directly configure KpmId to the Enrolee – instead KpmId can be generated from Kpm by the Enrolee after configuration of Kpm.

If an adversary compromises the confidentiality of the Enrolee’s Certificate (and/or, where applicable, the corresponding Certificate Chain) then that adversary obtains some information about which Enrolee;s Certificate and Certificate Chain is associated with which Enrolee. This provides a small advantage over information that might be obtained through traffic analysis. In many scenarios, this loss of confidentiality poses a low to medium risk, and encryption of Enrolee’s Certificate and Certificate Chain is a low to medium priority.

If confidentiality of MEF URI (Pre-Provisioned Symmetric Enrolee Key case only) is compromised by an adversary, then that adversary obtains some information about which MEF is associated with which Enrolee. This provides a very small advantage over information that might be obtained through traffic analysis. In many scenarios, the loss of confidentiality poses a low to medium risk.

Regarding Integrity: If an adversary compromises the integrity of Kpm or PrivateKeyEnrolee then the adversary can obtain complete control over the Enrolee. The priority of maintaining the confidentiality and integrity of Kpm or PrivateKeyEnrolee is at least as high as the priority of maintaining the integrity of any data that is stored, processed, sent or received by the Enrolee. Unless a thorough threat analysis is performed by a security expert, it should be assumed that the impact of a loss of integrity any of Kpm or PrivateKeyEnrolee is high to very high.

If and adversary compromises the integrity of KpmId or the Enrolee’s Certificate (and/or, where applicable, the corresponding Certificate Chain) or MEF URI, then it may no longer me possible to perform Security Bootstrap of the Enrolee. In this case, the Enrolee is effectively disabled. The impact depends on the scenario. Unless a thorough threat analysis is performed by a security expert, it should be assumed that the impact of a loss of integrity of any of these parameters is high.

Regarding Authorization:

Editor’s note: FFS

Summary: Maintaining confidentiality and integrity of Kpm or PrivateKeyEnrolee is a high to very high priority.  For the remaining parameters, confidentiality is a low to medium priority while integrity protection is a high priority.

Editor’s note: Authorization Summary is FFS

On Secured Environments: The storage and processing for these parameters (at the Enrolee) should occur in an environment with mitigations appropriate to the combination of the threats described above and the intended deployment of the Enrolee.

What is the priority of maintaining the confidentiality and integrity of Kpm (or the Enrolee’s Private Key) while in storage and when being processed? As discussed in the above analyses, this priority is at least as high as the cumulative priority for maintaining the confidential and integrity of all data that is stored, processed, sent or received by the Enrolee. Mitigations against adversaries with physical access to the Enrolee should be provided relative to this priority. An environment providing appropriate mitigations is considered a Secured Environment.

### X.2.1.2 High Level Requirements for Bootstrap Credential Configuration of M2M Enrolment Functions

In the Bootstrap Credential Configuration phase, it is necessary to configure the M2M Enrolment Function with the information shown in Table X.2.1.2-1 (copied from Table X.2.1-1).

Table X.2.1.2-1	Information configured to M2M Enrolment Functions during Bootstrap Credential Configuration phase of supported Security Bootstrap Frameworks.

| Security Bootstrap Framework | Information configured during Bootstrap Credential Configuration to MEF |
| --- | --- |
| Pre-Provisioned Symmetric Enrolee Key | Enrolee-to-MEF | Kpm, KpmId |
|  | MAF-to-MEF | PrivateKeyMEF, CertMEF containing MEF’s FQDN, ChainMEF, RootOfTrustMAF |
| Certificate Based | Enrolee-to-MEF | PrivateKeyMEF, CertMEF, (Opt) ChainMEF |
|  | MAF-to-MEF | As for Pre-Provisioned Symmetric Enrolee Key |
| GBA-Based | MAF-to-MEF (NAF-to-BSF) | (MEF=BSF) Out of scope. Note: includes PrivateKeyBSF, CertBSF containing BSF’s FQDN, ChainBSF, RootOfTrustNAF [13] |

An MEF can bootstrap many Enrolees, and consequently the impact of a compromising the confidentiality or integrity of parameters in an M2M Enrolment Function is many times the impact of compromising the confidentiality or integrity of parameters in a single Enrolee (discussed in clause X.2.1.1 “High Level Requirements for Bootstrap Credential Configuration of Enrolees”).

The impact of compromising the confidentiality or integrity of a single Kpm of the MEF is the same as for the corresponding Enrolee (typically high to very high). The impact of compromising the confidentiality or integrity of all Kpm of the MEF multiplied accordingly (typically very high impact).

The impact of compromising the confidentiality or integrity of PrivateKeyMEF is as high as the cumulative priority of maintaining the confidentiality and integrity of all data that is stored, processed, sent or received by all the Enrolees that could be bootstrapped by the M2M Enrolment Function (typically very high impact).

The impact of compromising the confidentiality or integrity of a single Kpm of the MEF is the same as for the corresponding Enrolee (typically low to medium). The impact of compromising the confidentiality or integrity of all Kpm of the MEF multiplied accordingly (typically medium to high).

Editor’s note: the analysis below needs to be revisited.

The communication between MEF and MAF is secured using certificates. Compromise the Bootstrap Credential Configuration the MEF does not reveal the private key of the MAF, so compromising the of the MEF does not impact the MAF (beyond compromising Km distributed by the MEF).

Editor’s note: Authorization Summary is FFS

### X.2.1.3 High Level Requirements for Bootstrap Credential Configuration to M2M Authentication Functions

In the Bootstrap Credential Configuration phase, it is necessary to configure the M2M Enrolment Function with the information shown in Table X.2.1.3-1 (copied from Table X.2.1-1).

Table X.2.1.3-1	Information configured to M2M Authentication Functions during Bootstrap Credential Configuration phase of supported Security Bootstrap Frameworks.

| Security Bootstrap Framework | Information configured during Bootstrap Credential Configuration to MAF |
| --- | --- |
| Pre-Provisioned Symmetric Enrolee Key | MAF-to-MEF | PrivateKeyMAF, CertMAF containing MAF’s FQDN, ChainMAF, RootOfTrustBSF |
| Certificate Based | MAF-to-MEF | As for Pre-Provisioned Symmetric Enrolee Key |
| GBA-Based | MAF-to-MEF (NAF-to-BSF) | Details specified in [13]. Includes PrivateKeyNAF, CertNAF containing NAF’s FQDN, ChainNAF, RootOfTrustBSF |

Editor’s Note: TBD.

------end of change 1------