| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC#11 |
| Title:* | Clause 9.1.1 Credential Configuration |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Phil Hawkes, Qualcomm , phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2014-06-02 |
| Abstract:* | Adds clause 9.1.1 describing procedures and parameters for Credential Configuration of Security Association Establishment Frameworks. |
| Agenda Item:* |  |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate text into the appropriate section of the Security TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

------start of change 1------

### 9 Security Framework Procedures and Parameters

This clause specifies procedures and parameters of the phases of Security Association Establishment Frameworks (clause 8.2) and Security Bootstrap Frameworks (clause 8.3). The requirements for these phases are discussed in Annex X “High Level Requirements for Security Framework Phases”.

9.1 Security Association Establishment Framework Procedures and Parameters

### 9.1.1 Credential Configuration Procedures and Parameters

The following Credential Configuration procedures are described in the present clause:

- Credential Configuration of Field-Domain Security Association End-Points (except for the GBA-Based case as discussed above), see Clause 9.1.1.1,

- Credential Configuration of Infrastructure-Domain Security Association End-Points, see Clause 9.1.1.2,

- Credential Configuration of M2M Authentication Functions, see Clause 9.1.1.3,

The following Credential Configuration procedures are specified by other organizations:

- Credential Configuration of Underlying Network Service Provider authentication server (e.g. HLR, HSS or AAA) for the GBA-Based Security Association Establishment Framework. These details are specified by 3GPP, 3GPP2 and ETSI specifications.

- Credential Configuration of Field-Domain Security Association End-Points for the GBA-Based Security Association Establishment Framework. These details are specified by 3GPP, 3GPP2 and ETSI specifications.

Editor’s Note: List any relevant 3GPP, 3GPP2 or IETF specifications.

### 9.1.1.1 Credential Configuration of Field-Domain Security Association End-Points

Table 9.1.1.1-1 lists the parameters configured to a Field-Domain Security Association End-Points in the Credential Configuration phase.

Table 9.1.1.1-1	 Parameters configured to a Field Domain Security Association end-point during the Credential Configuration phase.

| Security Association Establishment Framework | Parameter | Mandatory /Optional |
| --- | --- | --- |
| Pre-Provisioned M2M Secure Connection Key | kpsaKey | Mandatory |
|  | kpsaId | Mandatory |
| Certificate Based | thisEntityPrivateKey | Mandatory |
|  | thisEntityCertificate | Mandatory |
|  | thisEntityCertificateChain | Optional |
| MAF-Based | mafIdentifier | Mandatory |
|  | thisEntityIdentifier | Mandatory |
|  | masterCredential | Mandatory |
|  | masterCredentialIdentifier | Mandatory |
|  | masterCredentialExpiry | Optional |

The Credential Configuration of Field-Domain Security Association End-Points for the MAF-Based Security Association Establishment Framework is achieved through either:

- Pre-provisioning to which is (by the oneM2M definition) not specified by oneM2M. This pre-provisioning is expected to satisfy the requirements for Credential Configuration of Field-Domain Security Association End-Points provided in clause X.1.1.

- Remote provisioning via one of the Security Bootstrap Frameworks in Clause 8.3.

The Credential Configuration phases of other Security Association Establishment Frameworks are performed by pre-provisioning which is (by the oneM2M definition) not specified by oneM2M. This pre-provisioning shall satisfy the Credential Configuration requirements are provided in Annex X.1.1.

### 9.1.1.2 Credential Configuration of Infrastructure-Domain Security Association End-Points

Table 9.1.1.2-1 lists the parameters configured to Infrastructure-Domain Security Association End-Points in the Credential Configuration phase.

Table 9.1.1.2-1	 Parameters configured to an Infrastructure Domain Security Association end-point during the Credential Configuration phase. In the GBA-Based framework, the Infrastructure Domain Security Association end-point plays the role of a GBA NAF.

| Security Association Establishment Framework | Parameter | Mandatory /Optional |
| --- | --- | --- |
| Pre-Provisioned M2M Secure Connection Key | kpsaKey | Mandatory |
|  | kpsaId | Mandatory |
| Certificate Based | thisEntityPrivateKey | Mandatory |
|  | thisEntityCertificate | Mandatory |
|  | thisEntityCertificateChain | Optional |
| MAF-Based | Editor’s note: FFS | Editor’s note: FFS |
| GBA-Based Entity plays role of NAF. Details specified in 3GPP 33.220 [13]. Where this description differs from [13], [13] takes precedence | nafPrivateKey | See 3GPP 33.220 [13]. |
|  | nafCertificate | See 3GPP 33.220 [13]. |
|  | nafCertificateChain | See 3GPP 33.220 [13]. |
|  | rootCertificateBSF | See 3GPP 33.220 [13]. |

The procedure for the Credential Configuration of Infrastructure-Domain Security Association End-Points is expected to use business logic of the M2M Service Provider, and the details are not described in this specification.

The procedure for the Credential Configuration of Infrastructure-Domain Security Association End-Points shall satisfy the requirements in Annex X.1.1.1 “High Level Requirements for Credential Configuration of Infrastructure Domain Security Association End-points”.

### 9.1.1.3 Credential Configuration of M2M Authentication Functions

Table 9.1.1.3-1 lists the parameters configured to M2M Authentication Functions in the Credential Configuration phase. The M2M Authentication Function’s identifier (MAF-ID) is presumed to have been configured prior to the Credential Configuration phase.

Table 9.1.1.3-1		 Parameters configured to a M2M Authentication Functions during the Credential Configuration phase.

| Security Association Establishment Framework | Parameter | Mandatory /Optional |
| --- | --- | --- |
| MAF-Based | A-to-MAF Authentication | thisEntityIdentifier | Mandatory |
|  |  | masterCredential | Mandatory |
|  |  | masterCredentialIdentifier | Mandatory |
|  |  | masterCredentialExpiry | Optional |
|  | B-to-MAF Authentication | Editor’s note: FFS |  |

The procedure for the Credential Configuration of Infrastructure-Domain Security Association End-Points is expected to use business logic of the M2M Service Provider, and the details are not described in this specification.

The procedure for the Credential Configuration of Infrastructure-Domain Security Association End-Points shall satisfy the requirements in Annex X.1.1.3 “High Level Requirements for Credential Configuration of M2M Authentication Functions”.

------end of change 1------