| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC#11 |
| Title:* | Clause 9.1.2 Association Configuration |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Phil Hawkes, Qualcomm , phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2014-06-12 |
| Abstract:* | Adds clause 9.1.2 describing procedures and parameters for Association Configuration of Security Association Establishment Frameworks. |
| Agenda Item:* |  |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate text into the appropriate section of the Security TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

R01

- Added “Mandatory /Optional for all Security Association Establishment Frameworks”, “Mandatory /Optional for this Security Association Establishment Framework”

- Removed text referring to Annex X.

- Removed text about establishing security for remote management protocol.

- Expanded list of remote management protocols

R02: Updated text related to remote provisioning protocol and security administration protocols

------start of change 1------

### 9.1.2 Association Configuration Procedures and Parameters

The following Association Configuration procedures are described in this clause:

- Association Configuration of Field-Domain Security Association End-points, see Clause 9.1.2.1,

- Association Configuration of Infrastructure Domain Security Association End-points, see Clause 9.1.2.2,

- Association Configuration of M2M Authentication Functions and Underlying Network Service Provider authentication servers (e.g. HLR, HSS or AAA), see Clause 9.1.2.3.

### 9.1.2.1 Association Configuration of Field-Domain Security Association End-Points

Table 9.1.2.1-1 lists the parameters configured to Field-Domain Security Association End-Points in the Credential Configuration phase of all Security Association Establishment Frameworks.

Table 9.1.2.1-1		 Parameters configured to a Field-Domain Security Association End-Point during the Credential Configuration phase of all Security Association Establishment Frameworks.

| Parameters common to all Security Association Establishment Frameworks | Mandatory /Optional for all Security Association Establishment Frameworks |
| --- | --- |
| otherEntityIdentifier | Mandatory |
| associationConfigurationExpiry | Optional |
| securityAssociationLifespan | Optional |

Table 9.1.2.1-2 lists the Security Association Establishment Framework-specific parameters configured to Field-Domain Security Association End-Points in the Credential Configuration phase.

Table 9.1.2.1-2		 Security Association Establishment Framework-specific parameters configured to a Field-Domain Security Association End-Point during the Credential Configuration phase.

| Security Association Establishment Framework | Parameters specific to the Security Association Establishment Frameworks | Mandatory /Optional for this Security Association Establishment Framework |
| --- | --- | --- |
| Pre-Provisioned M2M Secure Connection Key | thisEntityIdentifier | Mandatory |
| Certificate Based | thisEntityIdentifier | Mandatory |
|  | otherEntityCertificateName | Mandatory |
|  | otherEntityRootOfTrust | Mandatory |
| MAF-Based | None: the Security Association End-Point is assumed to already know its CSE-ID/AE-ID in this case. |
| GBA-Based | thisEntityIdentifier | Mandatory |

This specification provides two procedures for Association Configuration of Field Domain Security Association End-points:

- Integrating Association Configuration with Credential Configuration. Implementation and use of this procedure is optional.

NOTE: This approach has limited flexibility, but can be useful in many cases.

Editor’s Note: We need to determine where and how we describe this procedure.

- A remote management protocols or security administration protocol that provides at least integrity protection and authentication of the configuration source.

Other mechanisms are not prohibited.

NOTE: For example, in some cases it is appropriate to use manual entry via user interface integrated to the Field Domain equipment (provided there is appropriate user authentication).

Editor’s Note: Stage 3 details of the data model are needed.

Editor’s Note: We need to interact with MAS WG5 to determine how to describe the data modelhow to “associate’ the MO with the Security Association End-point – e.g. does the MO path including the identity of the Security Association End-point?

### 9.1.2.2 Association Configuration of Infrastructure-Domain Security Association End-Points

Table 9.1.2.2-1 lists the parameters configured to Infrastructure-Domain Security Association End-Points in the Association Configuration phase of all Security Association Establishment Frameworks. It is assumed that an Infrastructure-Domain Security Association End-Point knows its CSE-ID/AE-ID prior to Association Configuration.

Table 9.1.2.2-1	 Parameters configured to an Infrastructure Domain Security Association end-point during the Association Configuration phase of all Security Association Establishment Frameworks.

| Parameter common to all Security Association Establishment Frameworks | Mandatory /Optional for all Security Association Establishment Frameworks |
| --- | --- |
| otherEntityIdentifier | Mandatory |
| associationConfigurationExpiry | Optional |
| securityAssociationLifespan | Optional |

Table 9.1.2.2-2 lists the parameters configured to Infrastructure-Domain Security Association End-Points in the Association Configuration phase.

Table 9.1.2.2-2	 Security Association Establishment Framework –specific parameters configured to an Infrastructure Domain Security Association end-point during the Association Configuration phase.

| Security Association Establishment Framework | Parameters specific to the Security Association Establishment Framework | Mandatory /Optional for this Security Association Establishment Framework |
| --- | --- | --- |
| Pre-Provisioned M2M Secure Connection Key | None |
| Certificate Based | otherEntityCertificateName | Mandatory |
|  | otherEntityRootOfTrust | Mandatory |
| MAF-Based | None |
| GBA-Based | None |

The Association Configuration of Infrastructure-Domain Security Association End-Points is expected to use business logic of the M2M Service Provider, and the details are not described in this specification.

### 9.1.2.3 Association Configuration of M2M Authentication Functions

Table 9.1.2.3-1 lists the parameters configured to M2M Authentication Functions in the Association Configuration phase.

Table 9.1.2.3-1		 Parameters configured to a M2M Authentication Functions during the Association Configuration phase.

| Security Association Establishment Framework | Parameter | Mandatory /Optional for this Security Association Establishment Framework |
| --- | --- | --- |
| MAF-Based | A-to-MAF Authentication | otherEntityIdentifier | Mandatory |
|  |  | associationConfigurationExpiry | Optional |
|  |  | securityAssociationLifespan | Optional |
|  | B-to-MAF Authentication | Editor’s note: FFS. |  |

This specification assumes that Association Configuration of the M2M Authentication Functions will utilize business logic of the Stakeholder that operates the M2M Authentication Function, and the details are not described in this specification.

### 9.1.2.4 Association Configuration of UNSP Authentication Servers

Table 9.1.2.4-1 lists the parameters configured to an Underlying Network Service Provider authentication server (e.g. HLR, HSS or AAA) in the Association Configuration phase.

Table 9.1.2.4-1		 Parameters configured to an Underlying Network Service Provider authentication server (e.g. HLR, HSS or AAA) during the Association Configuration phase.

| Security Association Establishment Framework | Parameter | Mandatory /Optional for this Security Association Establishment Framework |
| --- | --- | --- |
| GBA-Based. Parameters are configured to UE’s GBA User Security Settings (GUSS). GUSS details are specified in 3GPP 33.220 [13]. Where this description differs from [13], [13] takes precedence | thisEntityIdentifier | Mandatory |
|  | otherEntityIdentifier | Mandatory |
|  | associationConfigurationExpiry | Optional |
|  | securityAssociationLifespan | Optional |

The Association Configuration of the Underlying Network Service Provider authentication server is achieved by updating the GBA User Security Settings (GUSS) (3GPP 33.220 [13]) of the User Equipment (UE) upon which the Enrolee is executed. This specification assumes that this Association Configuration will utilize business logic of the Underlying Network Service Provider, and the details are not described in this specification.

Editor’s Note: List any relevant 3GPP, 3GPP2 or IETF specifications.

------end of change 1------