| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC#11 |
| Title:* | Clause 9.2.1 Bootstrap Credential Configuration |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Phil Hawkes, Qualcomm , phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2014-06-02 |
| Abstract:* | Adds clause 9.2.1 describing procedures and parameters for Bootstrap Credential Configuration of Security Bootstrap Frameworks. |
| Agenda Item:* |  |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate text into the appropriate section of the Security TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

------start of change 1------

### 9. 2 Security Bootstrap Framework Procedures and Parameters

### 9.2.1 Bootstrap Credential Configuration Procedures and Parameters

The following Bootstrap Credential Configuration procedures are described in this clause:

- Bootstrap Credential Configuration of Field-Domain Security Association End-Points (except for the GBA-Based case as discussed above), see Clause 9.2.1.1,

- Bootstrap Credential Configuration of M2M Enrolment Functions (except for the GBA-Based case as discussed above), see Clause 9.2.1.2,

- Bootstrap Credential Configuration of M2M Association Functions, see Clause 9.2.1.3.

The following Bootstrap Credential Configuration procedures are specified by other organizations:

- Bootstrap Credential Configuration of Underlying Network Service Provider authentication servers (e.g. HLR, HSS or AAA) for the GBA-Based Security Association Establishment Framework. These details are specified by 3GPP, 3GPP2 and ETSI specifications.

- Bootstrap Credential Configuration of Field-Domain Security Association End-Points for the GBA-Based Security Association Establishment Framework. These details are specified by 3GPP, 3GPP2 and ETSI specifications.

Editor’s Note: List any relevant 3GPP, 3GPP2 or IETF specifications.

### 9.2.1.1 Bootstrap Credential Configuration of Enrolees

Table 9.2.1.1-1 lists the parameters configured to Enrolees in the Bootstrap Credential Configuration phase.

Table 9.2.1.1-1	 Parameters configured to Enrolees during the Bootstrap Credential Configuration phase.

| Security Association Establishment Framework | Parameter | Mandatory /Optional |
| --- | --- | --- |
| Pre-Provisioned M2M Secure Connection Key | kpmKey | Mandatory |
|  | kpmId | Mandatory |
|  | mefURI | Mandatory |
| Certificate Based | thisEntityPrivateKey | Mandatory |
|  | thisEntityCertificate | Mandatory |
|  | thisEntityCertificateChain | Optional |

The Bootstrap Credential Configuration of Enrolees for the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework and Certificate-Based Security Bootstrap Framework performed by pre-provisioning which is (by the oneM2M definition) not specified by oneM2M.

The Bootstrap Credential Configuration of Enrolees shall satisfy the Bootstrap Credential Configuration phase requirements provided in Annex X.2.1.1 “High Level Requirements for Bootstrap Credential Configuration Enrolees”.

### 9.2.1.2 Bootstrap Credential Configuration of M2M Enrolment Functions

Table 9.2.1.2-1 lists the parameters assumed to be configured to M2M Enrolment Functions prior to the Bootstrap Credential Configuration phase of the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework and Certificate-Based Security Bootstrap Framework.

Table 9.2.1.2-1 Parameters assumed to be configured to M2M Enrolment Functions prior to the Bootstrap Credential Configuration phase in both of the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework and Certificate-Based Security Bootstrap Framework.

| Parameter common to all Security Bootstrap Frameworks | Mandatory /Optional |
| --- | --- |
| mefUri | Mandatory |
| mefPrivateKey | Mandatory |
| mefCertificate | Mandatory |
| mefCertificateChain | Mandatory |

Table 9.2.1.2-2 lists the parameters configured to M2M Enrolment Functions in the Bootstrap Credential Configuration phase of the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework and Certificate-Based Security Bootstrap Framework.

Table 9.2.1.2-2 Security Bootstrap Framework –specific parameters configured to the M2M Enrolment Function during the Bootstrap Credential Configuration phase of the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework and Certificate-Based Security Bootstrap Framework.

| Security Bootstrap Framework | Parameters specific to the Security Bootstrap Frameworks | Mandatory /Optional |
| --- | --- | --- |
| Pre-Provisioned Symmetric Enrolment Key | kpmKey | Mandatory |
|  | kpmId | Mandatory |
| Certificate Based | None |

The Bootstrap Credential Configuration of M2M Enrolment Functions is expected to use business logic of the stakeholder operating the M2M Enrolment Function, and the details are not described in this specification.

The Bootstrap Credential Configuration of M2M Enrolment Functions shall satisfy the Bootstrap Credential Configuration phase requirements provided in Annex X.2.1.2 “High Level Requirements for Bootstrap Credential Configuration of M2M Enrolment Functions”.

### 9.2.1.3 Bootstrap Credential Configuration of M2M Authentication Functions

Table 9.2.1.3-1 lists the parameters assumed to be configured to M2M Authentication Functions prior to or during the Bootstrap Credential Configuration phase.

Table 9.2.1.3-1 Parameters assumed to be configured to the M2M Authentication Functions prior to or during the Bootstrap Credential Configuration phase.

| Parameter common to all Security Bootstrap Frameworks | Mandatory /Optional |
| --- | --- |
| mafIdentifier | Mandatory |
| mafPrivateKey | Mandatory |
| mafCertificate | Mandatory |
| mafCertificateChain | Mandatory |

The Bootstrap Credential Configuration of M2M Authentication Functions is expected to use business logic of the M2M Service Provider, and the details are not described in this specification.

The Bootstrap Credential Configuration of M2M Authentication Functions shall satisfy the Bootstrap Credential Configuration phase requirements provided in Annex X.2.1.3 “High Level Requirements for Bootstrap Credential Configuration of M2M Authentication Functions”.

------end of change 1------