| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC#11 |
| Title:* | Clause 9.2.1 Bootstrap Credential Configuration |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Phil Hawkes, Qualcomm , phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2014-06-12 |
| Abstract:* | Adds clause 9.2.1 describing procedures and parameters for Bootstrap Credential Configuration of Security Bootstrap Frameworks. |
| Agenda Item:* |  |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate text into the appropriate section of the Security TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

R01:

- Changed table headings to indicate “Mandatory /Optional for this Security Bootstrap Framework”, Mandatory /Optional for the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework and Certificate-Based Security Bootstrap Framework,  or “Mandatory /Optional for all Security Bootstrap Frameworks” as applicable

- Corrected tables 9.2.1.2-1, 9.2.1.2-2, 9.2.1.3-1.

- Deleted text referring to Annex X.

- Added text for pre-provisioning “via out-of-band mechanisms which are not specified in the present document”

R02: Moved “M2M Service Provider” to “Stakeholder operating the MAF”.

------start of change 1------

### 9. 2 Security Bootstrap Framework Procedures and Parameters

### 9.2.1 Bootstrap Credential Configuration Procedures and Parameters

The following Bootstrap Credential Configuration procedures are described in this clause:

- Bootstrap Credential Configuration of Field-Domain Security Association End-Points (except for the GBA-Based case as discussed above), see Clause 9.2.1.1,

- Bootstrap Credential Configuration of M2M Enrolment Functions (except for the GBA-Based case as discussed above), see Clause 9.2.1.2,

- Bootstrap Credential Configuration of M2M Association Functions, see Clause 9.2.1.3.

The following Bootstrap Credential Configuration procedures are specified by other organizations:

- Bootstrap Credential Configuration of Underlying Network Service Provider authentication servers (e.g. HLR, HSS or AAA) for the GBA-Based Security Association Establishment Framework. These details are specified by 3GPP, 3GPP2 and ETSI specifications.

- Bootstrap Credential Configuration of Field-Domain Security Association End-Points for the GBA-Based Security Association Establishment Framework. These details are specified by 3GPP, 3GPP2 and ETSI specifications.

Editor’s Note: List any relevant 3GPP, 3GPP2 or IETF specifications.

### 9.2.1.1 Bootstrap Credential Configuration of Enrolees

Table 9.2.1.1-1 lists the parameters configured to Enrolees in the Bootstrap Credential Configuration phase.

Table 9.2.1.1-1	 Parameters configured to Enrolees during the Bootstrap Credential Configuration phase.

| Security Association Establishment Framework | Parameter | Mandatory /Optional for this Security Framework |
| --- | --- | --- |
| Pre-Provisioned M2M Secure Connection Key | kpmKey | Mandatory |
|  | kpmId | Mandatory |
|  | mefURI | Mandatory |
| Certificate Based | thisEntityPrivateKey | Mandatory |
|  | thisEntityCertificate | Mandatory |
|  | thisEntityCertificateChain | Optional |

The Bootstrap Credential Configuration of Enrolees for the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework and Certificate-Based Security Bootstrap Framework is performed by pre-provisioning via out-of-band mechanisms which are not specified in the present document.

### 9.2.1.2 Bootstrap Credential Configuration of M2M Enrolment Functions

Table 9.2.1.2-1 lists the parameters assumed to be configured to M2M Enrolment Functions prior to the Bootstrap Credential Configuration phase of the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework and Certificate-Based Security Bootstrap Framework.

Table 9.2.1.2-1 Parameters assumed to be configured to M2M Enrolment Functions prior to the Bootstrap Credential Configuration phase in both of the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework and Certificate-Based Security Bootstrap Framework.

| Parameter common to all Security Bootstrap Frameworks | Mandatory /Optional for the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework and Certificate-Based Security Bootstrap Framework |
| --- | --- |
| mefUri | Mandatory |

Table 9.2.1.2-2 lists the parameters configured to M2M Enrolment Functions in the Bootstrap Credential Configuration phase of the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework and Certificate-Based Security Bootstrap Framework.

Table 9.2.1.2-2 Security Bootstrap Framework –specific parameters configured to the M2M Enrolment Function during the Bootstrap Credential Configuration phase of the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework and Certificate-Based Security Bootstrap Framework.

| Security Bootstrap Framework | Parameters specific to the Security Bootstrap Frameworks | Mandatory /Optional for this Security Framework |
| --- | --- | --- |
| Pre-Provisioned Symmetric Enrolment Key | kpmKey | Mandatory |
|  | kpmId | Mandatory |
| Certificate Based | mefPrivateKey | Mandatory |
|  | mefCertificate | Mandatory |
|  | mefCertificateChain | Mandatory |

The Bootstrap Credential Configuration of M2M Enrolment Functions is expected to use business logic of the stakeholder operating the M2M Enrolment Function, and the details are not described in this specification.

### 9.2.1.3 Bootstrap Credential Configuration of M2M Authentication Functions

Table 9.2.1.3-1 lists the parameters assumed to be configured to M2M Authentication Functions prior to the Bootstrap Credential Configuration phase of all Security Bootstrap Frameworks.

Table 9.2.1.3-1 Parameters assumed to be configured to the M2M Authentication Functions prior to or during the Bootstrap Credential Configuration phase for all Security Frameworks.

| Parameter common to all Security Bootstrap Frameworks | Mandatory /Optional for all Security Bootstrap Frameworks |
| --- | --- |
| mafIdentifier | Mandatory |

The Bootstrap Credential Configuration of M2M Authentication Functions is expected to use business logic of the Stakeholder operating the MAF, and the details are not described in this specification.

------end of change 1------