| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC#11 |
| Title:* | Clause 9.2.2 Bootstrap Instruction Configuration |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Phil Hawkes, Qualcomm , phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2014-06-11 |
| Abstract:* | Adds clause 9.2.2 describing procedures and parameters for Bootstrap Instruction Configuration of Security Bootstrap Frameworks. |
| Agenda Item:* |  |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate text into the appropriate section of the Security TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

R01:

- Changed table headings to indicate “Mandatory /Optional for this Security Bootstrap Framework” or “Mandatory /Optional for all Security Bootstrap Frameworks” as applicable.

- Removed text referring to Annex X.

- Removed text about establishing security for remote management protocol.

- Expanded list of remote management protocols.

------start of change 1------

### 9.2.2 Bootstrap Instruction Configuration Procedures and Parameters

The following Bootstrap Instruction Configuration procedures are described in this clause:

- Bootstrap Instruction Configuration of Enrolees, see Clause 9.2.2.1,

- Bootstrap Instruction Configuration of M2M Authentication Functions, see Clause 9.2.2.2,

- Bootstrap Instruction Configuration of M2M Enrolment Functions, see Clause 9.2.2.3

- Bootstrap Instruction Configuration of Underlying Network Service Provider authentication servers (e.g. HLR, HSS or AAA), see Clause 9.2.2.4.

### 9.2.2.1 Bootstrap Instruction Configuration of Enrolees

Table 9.2.2.1-1 lists the common parameters configured to Enrolees during the Bootstrap Instruction Configuration phase of a Security Bootstrap Framework.

Table 9.2.2.1-1 Parameters configured to Enrolees during the Bootstrap Instruction Configuration phase of a Security Bootstrap Framework.

| Parameter common to all Security Bootstrap Frameworks | Mandatory /Optional for this Security Bootstrap Framework |
| --- | --- |
| thisEntityIdentifier | Mandatory |
| mafIdentifier | Mandatory |

Table 9.2.2.1-2 lists the Security Bootstrap Framework–specific parameters configured to Enrolees in the Bootstrap Instruction Configuration phase of the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework and Certificate-Based Security Bootstrap Framework.

Table 9.2.2.1-2 Security Bootstrap Framework –specific parameters configured to an Enrolee during the Instruction Instruction Configuration phase of the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework and Certificate-Based Security Bootstrap Framework.

| Security Bootstrap Framework | Security Bootstrap Framework-specific Parameters | Mandatory /Optional for this Security Bootstrap Framework |
| --- | --- | --- |
| Pre-Provisioned Symmetric Enrolment Key | None |
| Certificate Based | mefURI | Mandatory |
|  | mefCertificateName | Mandatory |
|  | mefRootOfTrust | Mandatory |
| GBA-Based | None |

This specification provides two mechanisms for Bootstrap Instruction Configuration of Field Domain Security Association End-points:

- Integrating Bootstrap Instruction Configuration with Bootstrap Credential Configuration. Implementation and use of this mechanism is optional.

NOTE: This approach has limited flexibility, but can be useful in many cases.

Editor’s Note: We need to determine where and how we describe this procedure.

- Bootstrap Instruction Configuration using an oneM2M-supported remote management protocols (e.g. OMA-DM 1.3, OMA DM 2.0, OMA LWM2M or BBF-TR-069) – see below. Implementation and use of this mechanism is Recommended (optional).

Other mechanisms are not prohibited.

Bootstrap Instruction Configuration using an oneM2M-supported Remote Management: This mechanism has the following pre-requisites

- The Field Domain equipment executing the Enrolee supports being remotely managed by an oneM2M-supported remote management protocol (e.g. OMA-DM 1.3, OMA DM 2.0, OMA LWM2M or BBF-TR-069). For this clause, “management client” refers to the implementation executing this functionality in the Field Domain equipment.

- The Enrolee supports being managed via a management client.

- The management client has established credentials with a management server that has authority to remotely manage the Enrolee, and these credentials enable establishing mutually authenticated secure communication between the management client and management server.

The Bootstrap Instruction Configuration of the Security Association End-point is achieved through secure management of a securityBootstrapInstruction Management Object associated with the Enrolee.

The structure and processing of the securityBootstrapInstruction Management Object is specified in TBD.

Editor’s Note: We need to interact with MAS WG5 to determine how to “associate’ the MO with the Enrolee– e.g. does the MO path including the identity of the Enrolee? We also need to specify the MO.

### 9.2.2.2 Bootstrap Instruction Configuration of M2M Authentication Functions

Table 9.2.2.2-1 lists the common parameters configured to M2M Authentication Functions during the Bootstrap Instruction Configuration phase of the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework and Certificate-Based Security Bootstrap Framework.

Table 9.2.2.2-1 Common parameters configured to M2M Authentication Functions during the Bootstrap Instruction Configuration phase of the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework and Certificate-Based Security Bootstrap Framework.

| Parameter common to all Security Bootstrap Frameworks | Mandatory /Optional for all Security Bootstrap Frameworks |
| --- | --- |
| thisEntityIdentifier | Mandatory |
| mefRootOfTrust | Mandatory |

This specification assumes that Bootstrap Instruction Configuration of the M2M Authentication Functions utilizes business logic of the Stakeholder that operates the M2M Authentication Function, and the details are not described in this specification.

### 9.2.2.3 Bootstrap Instruction Configuration of M2M Enrolment Functions

Editor’s Note: TO DO - list parameters that may be configured to this entity in this phase.

Table 9.2.2.3-1 lists the parameters configured to an M2M Enrolment Function during the Bootstrap Instruction Configuration phase of the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework and Certificate-Based Security Bootstrap Framework.

Table 9.2.2.3-1 Parameters configured to M2M Enrolment Functions during the Bootstrap Instruction Configuration phase of the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework and Certificate-Based Security Bootstrap Framework.

| Parameter common to all Security Bootstrap Frameworks | Mandatory /Optional for all Security Bootstrap Frameworks |
| --- | --- |
| thisEntityIdentifier | Mandatory |
| mafIdentifier | Mandatory |

Table 9.2.2.3-2 lists the Security Bootstrap Framework–specific parameters configured to an M2M Enrolment Functions in the Bootstrap Instruction Configuration phase of the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework and Certificate-Based Security Bootstrap Framework.

Table 9.2.2.3-2 Security Bootstrap Framework–specific parameters configured to an M2M Enrolment Function during the Instruction Instruction Configuration phase of the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework and Certificate-Based Security Bootstrap Framework.

| Security Bootstrap Framework | Security Bootstrap Framework-specific Parameters | Mandatory /Optional for this Security Bootstrap Framework |
| --- | --- | --- |
| Pre-Provisioned Symmetric Enrolment Key | None |
| Certificate Based | thisEntityCertificateName | Mandatory |
|  | thisEntityRootOfTrust | Mandatory |

This specification assumes that Bootstrap Instruction Configuration of the M2M Enrolment Functions utilizes business logic of the Stakeholder that operates the M2M Enrolment Function, and the details are not described in this specification.

### 9.2.2.4 Bootstrap Instruction Configuration of UNSP Authentication Server

Table 9.2.2.4-1 lists the parameters configured to an Underlying Network Service Provider authentication server (e.g. HLR, HSS or AAA) during the Bootstrap Instruction Configuration phase of the GBA-Based Security Bootstrap Framework.

Table 9.2.2.4-1 Parameters configured to M2M Enrolment Functions during the Bootstrap Instruction Configuration phase of the GBA-Based Security Bootstrap Framework.

| Parameter | Mandatory /Optional for all Security Bootstrap Frameworks |
| --- | --- |
| thisEntityIdentifier | Mandatory |
| mafIdentifier | Mandatory |

The Bootstrap Instruction Configuration of the Underlying Network Service Provider authentication server is achieved by updating the GBA User Security Settings (GUSS) (3GPP 33.220 [13]) of the User Equipment (UE) upon which the Enrolee is executed. This specification assumes that this Bootstrap Instruction Configuration utilizes business logic of the Underlying Network Service Provider, and the details are not described in this specification.

Editor’s Note: List any relevant 3GPP, 3GPP2 or IETF specifications.

------end of change 1------