| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC#11 |
| Title:* | Group Authentication Mechanism for Security TS |
| Source:* | China Mobile |
| Contact: | Judy Zhu, China Mobile , zhuhongru@chinamobile.com Ziyao Cheng, China Mobile, chengziyao@chinamobile.com Minpeng Qi, China Mobile, qiminpeng@chinamobile.com |
| Date:* | 2014-06-09 |
| Abstract:* | This contribution presents the description of group authentication mechanism for the security TS. |
| Agenda Item:* |  |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate text into an appropriate section of the Security TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

==================<Start of Change (New Text 1)>=================

#### 3.3	Abbreviations

For the purposes of the present document, the abbreviations given in [x] and the following abbreviations apply:

ACL	Access Control List

API	Application Programming Interface

ASN	Application Service Node

Authn	Authentication

BSF	Bootstrapping Server Function

B-TID		Bootstrapping Transaction Identifier

CA	Certification Authority

Cert[Entity]	A Certificate containing a Public Verification Key for which [Entity] knows the corresponding Private Signing Key,

CertName[Entity]An identifier that matches a unique value in a name field of Cert[Entity].

Chain[Entity]	Certificate Chain from Cert[Entity] to a Root Certificate signed by RootOfTrust[Entity]

DTLS	Datagram Transport Layer Security (Protocol)

Enrolee-ID	Enrollee Identity

FQDN	Fully Qualified Domain Name

GBA	Generic Bootstrapping Architecture

GBA_ME	ME-based GBA

GBA_U	GBA with UICC-based enhancements

GUSS	GBA User Security Settings

HLR	Home Location Register

HSS	Home Subscriber System

HW	Hardware

IdA	Identifier for entity A

IdB	Identifier for entity B

Kc	M2M Secure Connection Key

Ke	Enrolment Key

KeId	Enrolment Key Identifier

Km	Master Credential

KmId	Master Credential Identifier

Kpm	pre-provisioned credential for Master Credential provisioning

KpmId	pre-provisioned credential for Master Credential provisioning Identifier

Kpsa	pre-provisioned credential for M2M Security Association Establishment

KpsaId	pre-provisioned credential for M2M Security Association Establishment Identifier

Ks	temporary Key material referred to in GBA

Ks_(ext/int)_NAF Derived key in GBA_ME / Derived key in GBA_U which remains on UICC

Ks..NAF	Abbreviation of Ks_(int/ext)_NAF

M-TID	MAF Transaction Identifier

MAF	M2M Authentication Function

MAF-ID	M2M Authentication Function Identifier

MEF	M2M Enrolment Function

MIC	Message Integrity Code

MN	Middle Node

MZF	M2M Authorization Function

NAF	Network Application Function

PAP	Policy Access Point

PDP	Policy Decision Point

PEP	Policy Enforcement Point

PIP	Policy Information Point

PKI	Public Key Infrastructure

PrivateKey[Entity]		 Private Signing Key of [Entity]

RBAC	Role Based Access Control

RootOfTrust[Entity]	 A Root of Trust for Cert[Entity]

SE	Secure Environment

SW	Software

TLS	Transport Layer Security (Protocol)

(D)TLS-PSK	(D)TLS Pre-Shared Key (ciphersuites)

UE	(3GPP) User Equipment

USS	User Security Settings

URI	Uniform Resource Identifier

IMPIg                   IP Multimedia Private Identity of Group Agent

AUTNg                Authentication Token of Group Agent

RANDg                Random Challenge of Group Agent

RESg                    Response of Group Agent

XRESg                 Respect Response of Group Agent

Kg                         Root Key of Group Agent

CKg                      Cipher Key of Group Agent

IKg                      Integrity Key of Group Agent

IMPIi                   IP Multimedia Private Identity of Group Member Ai

AUTNi                Authentication Token of Group Member Ai

RANDi                Random Challenge of Group Member Ai

RESi                    Response of Group Member Ai

XRESi                 Respect Response of Group Member Ai

Ki                        Root Key of Group Member Ai

CKi                      Cipher Key of Group Member Ai

IKi                       Integrity Key of Group Member Ai

ski                        Session Key between Group Member Ai and Group Agent

Ksg                      Session Key between Group Agent and Infrastructure Node

Ksi                       Session Key between Group Member Ai and Infrastructure Node

==================<End of Change 2>==========================

==================<Start of Change (New Text 2)>=================

#### 6.3.1.3	Authentication

This component provides authentication services to the Application Layer.

There may exist the following group authentication mechanism:Group authentication is a kind of authentication technologies that a group of members (e.g., Application Service Node (ASN) or Application Dedicate Node (ADN)) can be authenticated together at the same time. Instead of authenticating group members one by one, group authentication mechanism treats these members in the group as a whole, and authenticates them together. Each group has a unique identifier, and an agent (e.g., Middle Node (MN)), which can be called as group agent, group gateway, etc.

- Solution:

As shown in Figure 6-3-1-3-1, group authentication mechanism can be divided into three phases such as inner group authentication, outer group authentication and end-to-end secure tunnel establishment.

- The first phase called inner group authentication (from ASN or ADN to MN) is that each group member (e.g., ASN or ADN) and the group agent (e.g., MN) should be mutually authenticated.

- The second phase called outer group authentication (from MN to IN) is that mutual authentication should be made between a given entity (e.g., Infrastructure Node (IN)) in the infrastructure domain and a group agent (e.g., MN) who is responsible to delegate all members in the group.

- The third phase called end-to-end secure tunnel establishment is that the group member (e.g., ASN or AND) and IN can set up secure communication individually and make implicit authentication between ASN/ADN and IN.

Figure: 6-3-1-3-1: Group Authentication general logic

- General Procedure:

The general procedure is depicted as shown in Figure 6-3-1-3-2:

Note1: Ai is the example of a group member (e.g., ASN or ADN) to illustrate the general procedure.

  - Inner group authentication

In the first phase, group member Ai, sends authentication request to group agent, e.g., MN. The flows are demonstrated as follows:

- Group member Ai sends access message to trigger authentication at first.

- Group agent sends authentication request to each group member.

- Group member Ai  and group agent make the mutual authentication internally as follows:

  - Group member Ai verifies group agent at first. If it is successful, Ai generates the inner group secure tunnel information with group agent and sends authentication response to group agent internally. If it is not successful, the authentication is failed and group authentication procedure is aborted.

  - Group agent authenticates each group member Ai through the response message. If the inner authentication is successful, inner group secure tunnel between group member and group agent is built; otherwise, it is aborted.

  - Outer group authentication

If the inner group authentication is successful, then the group agent represents all of the members to perform mutual authentication with the entity (e.g., Infrastructure Node) in the infrastructure domain.

- Group agent sends access message on behalf of the group members to Infrastructure Node to trigger the authentication outside the group.

- After receiving the authentication request, Infrastructure node can recognize that is a group authentication performing based on group agent identity and generate authentication request, containing authentication information for group agent and each group member Ai. And then, Infrastructure node forwards the group agent response to the agent.

- Group agent authenticates Infrastructure Node. If it is successful, group agent generates the outer group secure tunnel information and sends authentication response back to Infrastructure Node.

- Infrastructure Node authenticates group agent. If it is successful, it can be considered that group agent and all group members are authenticated successfully, Infrastructure Node generates the group agent secure tunnel information and individual secure tunnel information with Ai; which derives the individual session keys for different members for their communication with the IN; otherwise, it is aborted.

  - End-to-end secure tunnel establishment

- After Step 7, Infrastucture node sends the group agent secure information to agent.

- Upon receiving the information, group agent sends group agent secure parameters derived from the information and the authentication request in Step 5 to each group member Ai.

10)   Group member Ai will generate corresponding individual secure tunnel information, which is same with the information generated by the infrastructure node in the Step 7.

Figure: 6-3-1-3-2: Group Authentication general procedure

- Detailed Procedure:

In the group authentication mechanism, IN records the identity (e.g., IMPIg) and root key Kg of group agent, the identity (e.g., IMPIi) and root key Ki of each group member and the mapping table in its database. The detailed procedure is depicted in Figure 6-3-1-3-3.

Note: There is pre-configuration on the group and the group agent has configured the group members in advance.

Note : The signalling parameters in our group authentication can be carried by the service layer protocol which is defined by oneM2M.

  - Inner group authentication

In the first phase, group agent authenticates each group member. The details are demonstrated as follows:

Note: this is just an example to use AKA here, it is not limited to AKA only.

Note: The root key Ki is only shared between the Ai and IN

- Ai sends access message with its identity (e.g., IMPIi) to its group agent to initiate inner group authentication.

- When receives the request, the group agent generates authentication vectors (RANDi, AUTNi, RESi) and session key ski for each group member Ai, and then sends Authentication request (RANDi, AUTNi) to Ai.

- Ai verifies the received AUTNi by calculating the XMACg to check whether XMACg=MACg and the SQNg is in the correct range. If this check is correct, Ai calculates XRESi and generate session key ski. Then Ai sends Authentication Response (IMPIi, XRESi) to the group agent as response. Upon receiving the Authentication Response, the group agent authenticates Ai by checking whether the received XRESi is equal to RES maintained locally. If correct, Ai passes the authentication. Thus, the inner group authentication is done and inner group secure tunnel is built between Ai and group agent.

  - Outer group authentication

In the second phase, group agent performs mutual authentication with the network on behalf of all group members:

- Group agent sends Access message to IN, which includes the group agent’s identity (e.g., IMPIg) (permanent identity of group agent).

- After receiving the authentication request, Infrastructure node can recognize that is a group authentication performing based on the group agent’s identity (e.g., IMPIg) and generate authentication request:

  - According to the IMPIg, IN looks up its database to find the agent’s root key Kg and generates the authentication vector ( RANDg, AUTNg, XRESg, CKg, and IKg).

  - Meanwhile, IN also finds the each group member’s identity IMPIi and the root key Ki based on the group name according to the IMPIg and generates the key parameters CKi, IKi. In the database, there is a mapping between the group name and the group member’s identity IMPIi as well as their root key Ki.

  - IN sends Authentication Request (RANDg, AUTNg) to group agent.

- Upon the Authentication Request, the group agent takes the AUTNg from the received authentication vector, which includes a MACg and the SQNg. The group agent verifies the AUTNg by calculating the XMACg to check whether XMACg=MACg and the SQNg is in the correct range. And then, agent calculates authentication response RESg based on Kg and RANDg, and generates group session key Ksg=CKg||IKg. Group agent sends authentication response (RESg) to IN.

- IN checks whether the received RESg is equal to XRESg. If correct, it can be considered that group agent and all group members are authenticated successfully. IN generates Ksg for group agent and Ksi=CKi||IKi for each group member Ai.

  - End-to-end secure tunnel establishment

- IN sends group agent secure information to the group agent, which includes Acknowledgement message.

- Group agent sends RANDg with the group agent secure information to each group member correspondingly through the inner group secure tunnel.

Note 5: RANDg should be refreshed with the network AKA frequency.

- Ai calculates CKi, IKi based on Ki and RANDg, and generates the Ksi=CKi||IKi to establish the individual secure tunnel with IN.

Figure: 6-3-1-3-3: Group Authentication detailed procedure

==================<End of Change 2>========================