| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 (SEC) at TP#11 |
| Title:* | Proposing Clause 9 for Authorization Architecture |
| Source:* | CATT |
| Contact: | Wei Zhou, zhouwei@catt.cn Hui Xu, xuhui@catt.cn |
| Date:* | 2014-06-09 |
| Abstract:* | This contribution proposes creating a new clause for describing Authorization Architecture in the Security TS. |
| Agenda Item:* | TBD |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | oneM2M-TS-0003 Security Solutions |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

This contribution aims to provide description about oneM2M Authorization Architecture in the proposed Clause 9.

2	Proposal

# 9	Authorization Architecture

## 9.1	General Introduction to the Authorization Architecture

### 9.1.1	General Authorization Architecture

Editor’s Note: Moving the authorization architecture described in Section 6.3.2

### 9.1.2	General Authorization Procedure

Editor’s Note: Moving the authorization procedure described in Section 6.3.2

## 9.2	oneM2M Access Control Policy

### 9.2.1	Policy Structure

### 9.2.2	Policy Decision Request

### 9.2.3	Policy Decision Results

### 9.2.4	Rule and Policy Combing Algorithms

### 9.2.5	Policy Evaluation

## 9.3	Interfaces between Authorization Components

### 9.3.1	Interfaces between PEP and PDP

### 9.3.2	Interfaces between PDP and PAP

### 9.3.3	Interfaces between PDP and PIP

## 9.4	Operations and Procedures in PDP

### 9.4.1	Overview of PDP

### 9.4.2	Obtaining Policies

### 9.4.3	Obtaining Attributes

### 9.4.4	Making Decision

## 9.5	Operations and Procedures in PAP

### 9.5.1	Overview of PAP

### 9.5.2	Obtaining Access Control Policies

### 9.5.3	Access Control Policies Integration

### 9.5.4	Pre Configuration File

## 9.6	Operations and Procedures in PIP

### 9.6.1	Overview of PIP

### 9.6.2	Obtaining Access Control Policies from Service Subscription Resources

## 9.7	Access Token Management

### 9.7.1	Overview of Access Token Management

### 9.7.2	Access Token Structure

### 9.7.3	Access Token Generation and Verification