| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC WG4 |
| Title:* | Request for Changing the Text of SEC-2014-0249R05 |
| Source:* | Huawei Technologies Co.,Ltd. |
| Contact: | Guilin Wang, wang.guilin@huawei.com |
| Date:* | 2014-06-06 |
| Abstract:* | This contribution proposes a request for changing the text of SEC-2014-0249R05. |
| Agenda Item:* | Tbd |
| Work item(s): | WI0007 |
| Document(s) Impacted* | SEC TS-0003 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

- Introduction

On 29 May 2014, I gave several editorial and technical comments on Contribution SEC-2014-0249R05. However, this contribution was already agreed for inclusion in TS-0003 at the SEC 10.3 teleconference. Therefore, the chair of WG4 suggested me provide a contribution at TP 11 to modify the text of SEC-2014-0249R05.

- Proposal

-------------------------------------------Start -------------------------------------------------

Annex X. General Mutual Authentication Mechanism

oneM2M mutual authentication schemes allow oneM2M entities to prove that they know related credentials such as Master Credentials, without having to exchange value of those credentials, and sensitive data such as identities and identifiers   sensitive data such as security identities and security identifiers.To prevent reading and copying of credentials, secure environment within the Security CSF provides protection against tampering of those credentials and related processed information.

Editor’s Note: It needs to be defined which oneM2M identities represent sensitive data that should not be exchanged over the communication link between entities A and B.

A general mutual authentication protocol is applied to both symmetric and asymmetric key based schemes. Precise protocol messages and parameters depend on the chosen scheme and the security parameters selected. Typically it consists of following steps:

Figure X: Mutual Authentication

Editor’s Note: Adding a reference to an existing and suitable Challenge Response scheme/specification/standard is FFS.

1.	An initial step where an entity A is securely identified to an entity B with whom previous or no previous contact has been made. In this step entity A identifies itself to an entity B protected against eavesdropping, i.e. no exchange of key materials (Master Credentials).

2. In the second step entity B sends a challenge to entity A. The Authentication challenge consists of random challenge, authentication token (AUTN) of entity B derived from Master cCredentials, etc. The authentication challenge depends on the chosen scheme and the security parameters selected for symmetric and asymmetric key based schemes.

3. The eEntity A replies with an authentication response token (AUTN) derived from its known Master Credentials and the received Athentication challenge. This AUTN response is sent if entity B has been successfully authenticated by entity A.

4. Entity B then verifies the relation between entity A’s identity and the response received in step 3, which gives a high probability that the entity B knows a secret value associated with the entity A’s identity provided in step 1. . If the verification is positive, entity B is assured that the response has been created by entity A using a secret associated with entity A’s identity provided in step 1.

-------------------------------------------End -------------------------------------------------

Further notes: The following two changes for Figure X are also suggested. However, my software DOES NOT allow me to change the content of the figure.

2. Auth.Challenge (e.g.: random challenge, AUTN derived from Master cCredentials etc.)

3. Auth.Response (e.g.: AUTN derived from Entity A’s Master Credentials etc.)