| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 (SEC) during SEC 11 |
| Title:* | Details of MAF-based Security Association Establishment Framework |
| Source:* | Gemalto |
| Contact: | Mireille Pauliac, Gemalto, mireille.pauliac@gemalto.com |
| Date:* | 2014-06-02 |
| Abstract:* | This contribution completes the description of MAF-based Security Association Establishment. It addresses Editor’s Notes in section 8.2.3.1. |
| Agenda Item:* | TBD |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | oneM2M SEC TS-0003 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

This contribution completes the description of MAF-based Security Association Establishment. It addresses Editor’s Notes in section 8.2.3.1.

2	Proposal

**************************** Start of change *********************

#### 8.2.3.1	MAF-Based Symmetric Key Security Association Establishment Frameworks

This clause describes the MAF-based Security Association Establishment Framework.

This release addresses the scenario where the Entity B is an Infrastructure Node.

Figure 8.2.3.1-1: 	The sequence of events when using the MAF-Based Security Association Establishment Framework.

The following font colours differentiate the general topic that the text relates to:

- Blue italic text highlights details specific to this particular Security Association Establishment Framework.

- Purple italic text highlights technical actions that may include steps not specified by oneM2M.

Credential Configuration: The Master Credential (Km) and corresponding Master Credential Identifier (KmId) are  either pre-provisioned for Entity A and the MAF or remotely provisioned thanks to Security Bootstrap Frameworks described in Clause 8.3.

Association Configuration: Entity A, Entity B, and the BSF shall be configured with the information needed for the authentication and identification during Centralized Key Distribution Server Handshake and Association Security Handshake:

  - Entity A has to know Entity B Identity (IdB)

  - Entity B has to know Entity A Identity (IdA)

  - The MAF has to know Entity B Identity (IdB). In this case, IdB corresponds to IN Identity.

Association Security Handshake with Centralized Key Distribution Server Handshake:

### Centralized Key Distribution Server Handshake

### The Centralized Key Distribution Server Handshake in MAF-based Security Association Establishment framework enables the establishment of a M2M Secure Connection Key (Kc) and associated M2M Secure Connection Key Identifier (KcId) shared between the Entity A and the MAF thanks to (D)TLS-PSK handshake [15]

### The “psk_identity” parameter [15] is set to the value of the Master Credential Identifier KmId.

### The “psk” parameter [15] is set to the value of the Master Credential Km.

### Entity A sends KcId to Entity B (Infrastructure Node).

### Entity B (Infrastructure Node) can retrieve the M2M Secure Connection Key (Kc) from the MAF.

**************************** End of change *********************