| INPUT CONTRIBUTION |
| --- |
| Group Name:* | SEC#11 |
| Title:* | HTTP In-Protocol Security |
| Source:* | Qualcomm Inc. (TIA) |
| Contact: | Phil Hawkes, Qualcomm , phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2014-06-12 |
| Abstract:* | This contribution proposes HTTP In-Protocol Security (HIPS) procedures providing authentication-only, authentication + integrity, and authentication + integrity + encryption that is integrated to the HTTP protocol messages (rather than being provided by TLS or DTLS). Two session security mechanisms are provided, both based on pre-shared key: a Basic end-to-end handshake, and a Trusted-Agent-Assisted handshake using group authentication concepts. Other authentication mechanisms can be added in the future. |
| Agenda Item:* |  |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | Security TS (TS-0003) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1. Rationale

This contribution specifies HTTP In-Protocol Security (HIPS) procedures providing authentication-only, authentication + integrity, and authentication + integrity + encryption that is integrated to the HTTP Request and HTTP Response messages (rather than being provided by TLS).

| Quality of Protection | Descvription | Target use cases, |
| --- | --- | --- |
| Authentication-only | Entities are authenticated in HIPS Session Handshake, but there is no integrity protection or encryption of messages. | Scenarios where the lower layers (and intermediate entities) provide sufficient protection of the integrity and confidentiality of messages, but the AE-ID/CSE-ID of the peer is not authenticated at lower layers. For example, when an AE and CSE are running within a single execution environment, then the execution environment can provide integrity and confidentiality protection in an implementation specific manner, but the execution environment cannot authenticate the AE-ID and CSE-ID |
| Authentication + integrity | Entities are authenticated in HIPS Session Handshake Core primitive parameters cn,fr,op,to,ty,rc,rs (when present) have integrity and replay protection in every message. No encryption. | Multi-hop communication scenarios where intermediate entities are not trusted regarding the integrity of the message but are trusted regarding the confidentiality of the content |
| Authentication + integrity + encryption | Entities are authenticated in HIPS Session Handshake Core primitive parameters cn,fr,op,to,ty,rc,rs (when present) have integrity and replay protection in every message. Content cn parameter is encrypted (when present) in every message. | Multi-hop communication scenarios where intermediate entities are not trusted regarding the integrity of the message and are not trusted regarding the confidentiality of the content. |

At present only psk-key authentication is supported, although the procedures are defined to allow other authentication mechanisms to be added in the future.

Two session security mechanisms are provided, both based on pre-shared key: one with an end-to-end handshake, and group authentication mechanism using a Trusted Agent

Fig X.1 End-to-End Security of HTTP Request & Response using HTTP In-Protocol Security

This text should not be considered complete and will be inconsistent in many places. This text is provided to demonstrate the feasibility of specifying an end-to-end security protocol including support for group authentication (Trusted Agent-assisted handshake).

This could be easily  extended to CoAP also.

2. Proposed Text

# x.	HTTP In-Protocol Security

This clause describes in-band security mechanisms, which are security mechanism that exchange data using HTTP Header parameters of HTTP Request and Response messages.

## x.1	HTTP In-Protocol Security Parameter Descriptions

| Parameter | Datatype | Description | Profile Parameter? | Primitive Parameter? | State Parameter? |
| --- | --- | --- | --- | --- | --- |
| HIPS_AuthnScheme | enum | Identifies the type of authentication. May be one of: Symmetric | Yes | Yes | No |
| HIPS_AuthnParams | xs:complex | Content of this parameter depend on the HIPS_AuthnScheme and message being exchanged | No | Yes | No |
| HIPS_Destination | CSE/AE-ID or empty? | If empty, then this parameter indicates that the intended destination of the HIPS_Header is the entity that sent the HTTP Request/Response. If not empty, then this parameter provides the identity of the intended destination of the HIPS_Header. | No | No | Yes |
| HIPS_EndPoint | Type of AE-ID or CSE-ID | Identity of the other entity. | Yes | No | Yes |
| HIPS_HandshakeHeader | xs:complex | Contains the HTTP In-Protocol Security parameters using the HTTP In-Protocol Security Session Handshake. | No | Yes | No |
| HIPS_HandshakeMessageId | Enum | Identifies the order of the handshake message within the handshake, and also the type of handshake. |  |  |  |
| HIPS_HandshakeVerifier | xs:binary (256-bits) | Contains the value authenticating the HTTP In-Protocol Security Session Handshake. | No | Yes |  |
| HIPS_InitRand | xs:binary (128-bits) | Random challenge used for authentication and key establishment | No | Yes | yes |
| HIPS_Mac |  | Message authentication code used when the Quality of Protection includes integrity protection. | No | Yes | No |
| HIPS_MacInputFlags |  | Indicates which Request primitive parameters have been used in the input for computing the HIPS_Mac. | No | Yes | No |
| HIPS_MessageCounter | xs:integer (32-bits) | Set to the value of HIPS_MyMessageCounter of the End-Point that sends the message | No | Yes | Yes |
| HIPS_MessageHeader | xs:complex | Contains the HTTP In-Protocol Security parameters | No | Yes | No |
| HIPS_Nonce |  | A nonce is a “number used once” that is unique to a message within the scope of a session. Used to detect replay attacks as part of integrity protection. When encryption is applied, then this is used to prevent re-use of keystream. See “NOTE: Regarding HIPS_Nonce” below for more details. | No | Yes | No |
| HIPS_psk |  | A secret value known only to the HIPS-Initiator and HIPS-Responder. | Yes | No | No |
| HIPS_pskIdentity |  | This value is used to determine when a new psk key has been established. The scope of this session identity is only within the pair of entities. | Yes | Yes |  |
| HIPS_QoP | enum | Quality of protection to be provided for the HTTP In-Protocol Security Session. May be one of authentication-only authentication+integrity authentication+integrity+encryption | Yes | Yes | Yes |
| HIPS_ReceivedMessageCounter | xs:integer (32-bits) | Stores the value of verified HIPS_MyMessageCounters received from the other end-point. | No | Yes | Yes |
| HIPS_RespRand | xs:binary (128-bits) | Random challenge used for authentication and key establishment | No | Yes | yes |
| HIPS_SessionEncryptionKey |  | Key used for integrity protection of content | No | No | Yes |
| HIPS_SessionEpochCounter |  | Forms part of HIPS_Nonce and HIPS_Nonce. See Regarding HIPS_Nonce below for details. | No | Yes | Yes |
| HIPS_SessionId |  | This value is used to determine when a message for one session has been received after another session had been established. The scope of this session identity is only within the pair of entities that established the session. The all zeroes session identity is used when the message is not associated with a current session. | No | Yes | Yes |
| HIPS_SessionIntegrityKey |  | Key used for integrity protection of primitive parameters. | No | No | Yes |
| HIPS_SessionRandom | xs:binary (256-bits) | HIPS_InitRand ¦¦ HIPS_RespRand | No | Yes | yes |
| HIPS_Source | CSE/AE-ID or empty? | If empty, then this parameter indicates that the claimed source of the HIPS_Header is the entity that sent the HTTP Request/Response. If not empty, then this parameter provides the identity of the claimed source of the HIPS_Header. | No | No | Yes |
| HIPS_TargetResponder | CSE-ID or AE-ID | Indicates to a (HIPS Trusted Agent) the HIPS Target Responder: that is, end-point with whom the HIPS Initiator would like assistance in establishing a HIPS Session |  |  |  |
| HIPS_TargetRespRand | See HIPS_RespRand | A trusted, fresh HIPS_RespRand being provided to an HIPS Initiator on behalf of the HIPS Target Responder. |  |  |  |
| HIPS_TargetAuthnParams |  | Trusted, fresh HIPS_AithnParams being provided to an HIPS Initiator on behalf of the HIPS Target Responder. |  |  |  |
| HIPS_Version | TBD | Indicates the version of HIPS selected for this handshake |  |  |  |
| HIPS_Window |  | TBD |  |  |  |
| HIPS_WindowMax |  | TBD |  |  |  |

NOTE: Regarding HIPS_Nonce. To reduce the size of nonce sent in messages, the nonces are formed from

- An ASCI string “request” or “response” to distinguish the direction of the message.

- A small counter, either HIPS_InitiatorCounter or HIPS_ResponderCounter – with the appropriate counter passed in the HIPS_MessageHeader.

- An HIPS_SessionEpochCounter, which is kept as state at the two end-point.

  - The HIPS_SessionEpochCounter changes infrequently.

  - Either end-point can use the HIPS Counter Reset Procedure reset HIPS_Request/ ResponderCounter and start using a fresh SessionEpochCounter, as described in clause X.5.1. The HIPS Counter Reset Procedure should be initiator if HIPS_InitiatorCounter or HIPS_ResponderCounter is approaching the upper limit, or if either side detects loss of synchronization.

## x.2	VOID

## x.3	HTTP In-Protocol Security Data Models

### x.3.1	HTTP In-Protocol Security Profile

The HIPS Profile is configured to a HIPS end-point to provide details needed for that entity to perform HIPS with another HIPS end-point.

The following data model describes the HIPS Profile

- HIPS_EndPoint: the CSE-ID or AE-ID of theother HIPS end-point

- HIPS_AcceptableVersions

- HIPS_AuthnScheme: {psk }

- HIPS_AuthnScheme-Specific parameters

  - If HIPS_AuthnScheme = psk

    - HIPS_psk

    - HIPS_pskIdentity

Editor’s note: the following parameters might be applicable when HIPS_AuthnScheme = certificate

  - If HIPS_AuthnScheme = certificate // These are provided as examples

    - EntityCredentials

      - inBandPrivateKey //ECDSA Private Key of this entity

      - inBandCertificate //Certificate containing ECDSA Public Key of this entity

      - (opt) inBandCertificateChain //Certificate chain to the root of trust for this entity

    - PeerCredentials

      - inBandPeerCertificateName

      - inBandPeerCertificateRootOfTrust

- HIPS_QoP: {authentication-only, authentication+integrity, authentication+integrity+encryption}

- HIPS_WindowMax:

The HIPS Profile may be configured to an end-point via a remote management protocol or security administration protocol that provides mutual authentication, integrity protection and confidentiality.

### x.3.2	HTTP In-Protocol Security Session State

The An entity that has established an HTTP In-Protocol Security Session shall maintain the following state:

- HIPS_Version (1);

- HIPS_SessionId (1):

- (If HIPS_QoP = authentication+integrity or authentication+integrity+encryption)

  - HIPS_SessionIntegrityKey (1)

  - HIPS_SessionEpochCounter  (1),

  - HIPS_MyMessageCounter (1)

  - HIPS_Window (1).

  - HIPS_ReceivedMessageCounters (0.. HIPS_MaxReceivedMessageCounters).

- (If HIPS_QoP = authentication+integrity+encryption)

  - HIPS_SessionEncryptionKey (1)

### x.3.3	HTTP In-Protocol Security Information Elements

#### x.3.3.1	HTTP In-Protocol Security Headers

A HIPS_Header can be used to protect any portion of the end-to-end delivery of the HTTP Request or Response. Where a HTTP Request or Response contains more than one HIP_Header, then each HIPS_Header protects a different portion of the end-to-end delivery of the HTTP Request or Response.

A HTTP Request or Response may contain zero or more HIPS_Header parameters.

Table X.3.3.2-1 lists the HTTP In-Protocol Security Parameters in a HIPS_Header parameter.

Table X.3.3.2-1	the HTTP In-Protocol Security Parameters in a HIPS_Header parameter.

| Parameter | Presence in HIPS_MessageHeader parameter |
| --- | --- |
| HIPS_SummaryHeader | Mandatory |
| HIPS_HandshakeHeader | Optional |
| HIPS_MeassageHeader | Mandatory |

#### x.3.3.2	HTTP In-Protocol Security Summary Header (HIPS_EndPointIdentities)

The HIPS_SummaryHeader allows an entity to determine if that entity is the intended destination of the HIPS _Header-– and if so, who generated the HIPS parameters. The HIPS_SummaryHeader also informs the HIPS Destination End-Point if message protection (e.g. integrity protection and replay protection) has been applied to the message.

Table X.3.3.2-1 lists the HTTP In-Protocol Security Parameters in a HIPS_EndPointIdentities parameter.

Table X.3.3.2-1	the HTTP In-Protocol Security Parameters in a HIPS_EndPointIdentities parameter.

| Parameter | Presence in HIPS_MessageHeader parameter |
| --- | --- |
| HIPS_SourceId | Mandatory |
| HIPS_DestinationId | Mandatory |
| HIPS_QoP | Mandatory |

#### X.3.3.3	HTTP In-Protocol Security Handshake Header (HIPS_HandshakeHeader)

The HIPS_HandshakeHeader parameter contains all HTTP In-Protocol Security parameters involved in establishing an HTTP In-Protocol Security Session.

Table X.3.3.3-1 lists the HTTP In-Protocol Security Parameters in a HIPS_HandshakeHeader parameter.

Table X.3.3.3-1	the HTTP In-Protocol Security Parameters in a HIPS_HandshakeHeader parameter, and presence in the three HIPS (M = Mandatory for this message, “-“ = Not Present for this message, “O” = Optional for this message).

| Parameter | Presence for HIPS Handshake Message |
| --- | --- |
|  | Basic | TA-TR | Ai-TA | Ai-TR |
|  | A.1 | A.2 | A.3 | B.1 | B.2 | C.1 | C.2 | D |
| HIPS_HandshakeMessageId | M | M | M | M | M | M | M | M |
| HIPS_Version | M | - | - | M | - | M | - | M |
| HIPS_SessionId | M | - | - | - | - | - | - | M |
| HIPS_AuthnScheme | M | - | - | M | M | M | M | M |
| HIPS_QoP | M | - | - | - | - | - | - | M |
| HIPS_InitRand | M | M | - | M | M | M | M | M |
| HIPS_TargetResponder | - | - | - | - | - | M | - | - |
| HIPS_RespRand | - | M | M | - | M | - | M | - |
| HIPS_AuthnParams | O | O | O | O | O | O | O | O |
| HIPS_TargetRespRand | - | - | - | - | - | - | M | M |
| HIPS_TargetAuthnParams | - | - | - | - | - | - | O | O |
| HIPS_HandshakeVerifier | - | M | M | - | M | - | M | M |

#### x.3.3.4	HTTP In-Protocol Security Message Header (HIPS_MessageHeader)

The HIPS_Message Header primitive parameter contains all HTTP In-Protocol Security parameters specific to a particular HTTP Request/Response exchanged between the HTTP In-Protocol Security end-points.

Table X.3.3.4-1 lists the HTTP In-Protocol Security Parameters in a HIPS_MessageHeader parameter.

Table X.3.3.4-1	the HTTP In-Protocol Security Parameters in a HIPS_MessageHeader parameter.

| Parameter | Presence in HIPS_MessageHeader parameter |
| --- | --- |
| HIPS_SessionId | Mandatory |
| HIPS_MessageCounter | Mandatory |
| HIPS_MacInputFlags | Mandatory |
| HIPS_Mac | Mandatory |
| HIPS_MessageEpochCounter | Optional |

### X.3.4	Example Call Flows

These call flows show how the HIPS headers would be used in establishing session keys for end-to-end security.

#### X.3.4.1	Example Call flow for Basic HIPS Handshake

#### X.3.4.2 Example Call Flow Using a Trusted Agent