| CHANGE REQUEST |
| --- |
| Group Name:* | SEC#11.3 |
| Source:* | Francois Ennesser, Gemalto (ETSI) |
| Title | Proposed improvements to Section 8 |
| Date:* | 2014-06-24 |
| Contact:* | francois.ennesser@gemalto.com |
| Reason for Change/s:* | Clarifications to Section 8 R01 after Qualcomm’s review. |
| CR against: | TS-0003 |
| Clauses/Sub Clauses Affected* | Clause 8 and sub-clauses |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree on changes to current baseline. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

Some clarifications are proposed to improve readability of the

### -----------------------Start of change 1-------------------------------------------

# 8	Security Frameworks

## 8.1	General Introductions to the Security Frameworks

### The security frameworks can be categorized into two main types

Direct Security Frameworks: where the entities authenticate each other directly, without assistance from a Central Key Distribution Server

Centralized Security Frameworks: where the entities authenticate each other with the assistance of a Central Key Distribution Server.

### 8.1.1	General Introduction to the Direct Security Frameworks

#### 8.1.1.1	General Introduction to the Pre-Provisioned Symmetric Key Framework

Editor's Note: Text is needed here.

#### 8.1.1.2	General Introduction to the Certificate-Based Security Frameworks

Editor's Note: Further Introductory material could be appropriate here.

This clause describes the Credential Configuration and Certificate Verification used in the Certificate-Based Security Association Establishment Framework and Certificate-Based Security Bootstrap Framework.

##### 8.1.1.2.1	Credential Configuration for Certificate-Based Security Frameworks

If an entity is to authenticate itself using a Certificate-Based Security Framework, then the entity shall be pre-provisioned with the following information

The entity's Private Signing Key and the corresponding Public Verification Key.

NOTE 1:	An entity authenticates itself to other entities by proving that it knows the Private Signing Key corresponding to a particular Public Verification Key.

Editor's Note: In some cases the Private Signing Key is unique to a single entity. In other cases, the Private Signing Key might be used to authenticate all entity's executing on a particular piece of hardware or used to authenticate all AEs executing a particular piece of software. This needs clarification text.

The entity's Certificate containing the entity Public Verification Key and the entity's Certificate Name (a unique identity) provided in a name field of the Certificate (e.g. in the X.509 "Subject" or "Subject Alternative Name" attribute). Two options are available:

The entity is configured with a valid Certificate Chain from the entity's Certificate to a Root Certificate. The entity's Root of Trust is the cryptographic hash of the Public Verification Key in this Root Certificate.

Alternatively, the entity's Certificate is a self-signed certificate, for which the entity's Private Signing Key is used to generate the Certificate signature (the certificate is verified using the entity's Public Verification Key).  In this case the cryptographic hash of entity's Public Verification Key is both the entity's Root of Trust and the entity's Certificate Name. This implies that the cryptographic hash of the entity's Public Verification Key shall be present in a name field of the entity's Certificate.

Editor's Note: Conditions under which a self-signed certificate can be trusted or possible means to verify it (e.g. OCSP) are FFS.

Editor's Note: Details for OCSP [RFC2560] and Certificate Revocation Lists (CRLs) are FFS.

Editor's Note: Usage of certificates other than X.509 is FFS.

##### 8.1.1.2.2	Certificate Verification

This clause describes how an entity authenticates the other entity in the Security Handshake of a Certificate-Based Security Framework.

The other entity's Certificate is received during the Security Handshake.

The other entity's Certificate is verified as follows:

If the other entity's Certificate is a self-signed certificate, then verify each of the following:

The other entity's Certificate Name and other entity's Root of Trust (received during Association Configuration or Bootstrap Instruction Configuration) are identical.

The other entity's Certificate Name (received during Association Configuration or Bootstrap Instruction Configuration) is identical to a value in a name field (e.g. in the X.509 "Subject" or "Subject Alternative Name" attribute) of other entity's Certificate (received during the Security Handshake).

The other entity's Root of Trust (received during Association Configuration or Bootstrap Instruction Configuration) is identical to the Public Verification Key (or hash thereof) in the other entity's Certificate (received during the Security Handshake).

If the other entity's Certificate is not a self-signed certificate, then  verify each of the following:

The other entity's Certificate Name (received during Association Configuration or Bootstrap Instruction Configuration) is identical to a value in a name field (e.g. in the X.509 "Subject" or "Subject Alternative Name" attribute) of the other entity's Certificate (received during the Security Handshake)..

The other entity Certificate has a valid Certificate Chain (received during the Security Handshake) to a Certificate whose Public Verification Key (or hash thereof) is identical to the other entity' Root of Trust (received during Association Configuration or Bootstrap Instruction Configuration).

NOTE:	After a successful Security Handshake in which the other entity provides a Certificate Chain, the other entity's identity (received during Association Configuration or Bootstrap Instruction Configuration) can be associated with additional information extracted from the other entity's Certificate Chain (e.g. the other entity Manufacturer, other entity owner, or conformance criteria). These details are not described in the present document.

Editor's Note: Details of credentials for OCSP [RFC2560] may be required here.

### 8.1.2	General Introduction to the Centralized Security Frameworks

#### 8.1.2.1	General Introduction to the M2M Authentication Function Framework

Editor's Note: Text is needed here.

#### 8.1.2.2	General Introduction to the GBA (Generic Bootstrapping Architecture) Framework

A general introduction to GBA is included in TR-0008 [i.6].

After a successful GBA bootstrapping, the M2M Application Service/Middle Node and the BSF share a security association which consists of a bootstrapping transaction identifier (B-TID) and key material (GBA bootstrap Ks).

This security association may be used by the M2M Application Service/Middle Node to derive NAF keys (Ks_(ext/int)_NAF) shared between a M2M Application Service/Middle Node and a M2M Infrastructure Node or an M2M Authentication Framework.

Figure 8.1.2.2-1: GBA framework. Note that the Network application Function (NAF)
may be an Infrastructure Node or an M2M Authentication Function

## 8.2	Security Association Establishment Frameworks

### 8.2.1	Overview on Security Association Establishment Frameworks

The oneM2M system supports the following Security Association Establishment Frameworks:

Direct Security Association Establishment Frameworks:

Pre-Provisioned M2M Secure Connection Key Security Association Establishment. A symmetric key is pre-provisioned to the entities: this is called the Pre-Provisioned M2M Secure Connection Key, and denoted Kpsa. The entities authenticate each other by verifying Message Integrity Codes (MIC) in the Security Handshake which were generated using the symmetric key.  For more details see clause 8.2.2.1.

Certificate-Based Security Association Establishment: The entities are each issued with

a Private Signing Key that is known only to that entity,

a Certificate containing the corresponding Public Verification Key, and

(Optionally) a Certificate Chain from the entity's Certificate to a Root Certificate.

The entities shall validate each other's Certificate before trusting the Public Verification Keys in the Certificate. Within the Security Handshake, entity A creates a digital signature of the session parameters using its private signing key and entity B verifies the digital signature using entity A's public verification key. Then the roles are reversed: entity B creates a digital signature and entity A verifies it. For more details see clause 8.2.2.2.

Centralized Security Association Establishment Frameworks: In such schemes, entity A and a Central Key Distribution Server authenticate each other and derive a M2M Secure Connection key (Kc) that the Central Key Distribution Server delivers to entity B. The entities then authenticate each other using the M2M Secure Connection key (Kc). The oneM2M authentication Frameworks using centralized key distribution are:

GBA based Security Association Establishment. This Security Association Establishment Framework uses 3GPP or 3GPP2 symmetric keys to authenticate entity A and the Central Key Distribution Server. The details are specified by 3GPP [4] and 3GPP2 [14]. For more details see clause 8.2.2.

M2M Authentication Function (MAF)-based Security Association Establishment. This Security Association Establishment Framework uses symmetric keys to authenticate the entity A and the Central Key Distribution Server. For more details see clause 8.2.3.1.

For a more detailed description of the above Security Association Establishment Frameworks, it is useful to compare the following aspects of the Security Association Establishment Frameworks:

Credential Configuration:

For Central Key Distribution Security Association Establishment Frameworks:

Entity A is configured with (or otherwise establishes) the Master Credential (Km) that the entity A will use to authenticate the entity A to the Central Key Distribution Server.

The Central Key Distribution Server is configured with the Master Credential (Km) that will be used to authenticate the Central Key Distribution Server to entity A.

Association Configuration: Configuration of entity identifiers (that is, CSE-ID or AE-ID) for the entities to be authenticated.

Additionally, in the case of Certificate-Based Authentication Framework: each entity is configured with the Certificate Name and Root of Trust that the entity will use to verify the other entity.

Central Key Distribution Server Handshake: When a Centralized Security Association Establishment Framework is used, entity A and the Central Key Distribution Server (MAF or GBA-BSF) perform mutual authentication and generate a key, Km or Ks respectively, which is then used to derive a M2M Secure Connection Key (Kc) used in the Security Handshake for mutual authentication between entity A and entity B. This is not applicable to Direct Security Association Establishment Frameworks.

Association Security Handshake: Identification, authentication and security context establishment between the entities.

Figure 8.2.1-1 provides a summary of the above defined four Security Association Establishment Frameworks.

Figure 8.2.1-1: Overview of the Security Association Establishment Frameworks
supported by oneM2M.

Editor's note: In the above figure, the illustrations of the MAF-based and GBA-based centralized security frameworks may need to be updated when the detailed flows have been agreed.

### 8.2.2	Direct Security Association Establishment Frameworks

#### 8.2.2.1	Pre-Provisioned Symmetric Key Security Association Establishment Frameworks

This clause describes the Pre-Provisioned Secure Connection Key Security Association Establishment Framework.  This framework enables mutual authentication of two entities (CSEs or AE). The Credential for this framework is a long-term symmetric key that has been pre-provisioned into the entities to be authenticated. This key is called a Pre-Provisioned Secure Connection Key and is denoted Kpsa. The entities authenticate each other by verifying Message IntegrityCodes in the Security Handshake which were generated using the Pre-Provisioned Secure Connection Key.

NOTE:	Long term Pre-Provisioned Secure Connection Keys can pose a security risk if not adequately secured, and for this reason are recommended to be stored in Secure Environments.

Figure 8.2.2.1-1 illustrates the sequence of events when using the Pre-Provisioned Secure Connection Key Security Association Establishment Framework. In this description, "Entity A" and "Entity B" correspond to two CSEs or AEs.

NOTE:	The following font colours differentiate the general topic that the text relates to:
Blue italic text highlights details specific to this particular Security Association Establishment Framework.

Purple italic text highlights technical actions that may include steps not specified by oneM2M.

Red italic text highlights security-related properties.

Figure 8.2.2.1-1: The sequence of events when using the Pre-Provisioned Secure Connection Key
Security Association Establishment Framework

Credential Configuration: The Pre-Provisioned Secure Connection Key (Kpsa) and the corresponding Pre-Provisioned Secure Connection Key Identifier, denoted KpsaId, are pre-provisioned to both entities.

Association Configuration: Each entity is configured with the information needed for mutual authentication and identification:

Entity A is commanded to initiate Security Context Establishment, and includes the following arguments:

The Pre-Provisioned Secure Connection Key Identifier KpsaId.

Entity A identity (IdA). Entity A is to assume this identity when interacting with Entity B.

Entity B identity (IdB). Entity A is to use this identity for Entity B authenticating using the above arguments. This identity is also used to route the (D)TLS exchange.

The mechanisms for achieving this are discussed in clause 8.4.1.2 (for the cases where Entity A is in the Field Domain) and Clause 8.4.2 (for the cases where Entity A is in the Infrastructure Domain).

NOTE 2:	Entity A will associate Entity B's identity with messages secured within Security Contexts established using the Pre-Provisioned Secure Connection Key Kpsa associated with the Pre-Provisioned Secure Connection Key Identifier KpsaId.

Entity B is configured with the following arguments describing Entity A authorized to perform Security Context Establishment with the Registrar:

The Pre-Provisioned Secure Connection Key Identifier KpsaId.

Entity A identity (IdA). Entity B is to use this identity for Entity A authenticating using the above arguments..

Entity B Identity (IdB), if not already configured to Entity B. Entity B is to assume this identity when interacting with Entity A.

The mechanisms for achieving this are discussed in clause 8.4.1.2 (for the cases where Entity B is in the Field Domain) and Clause 8.4.2 (for the cases where Entity B is in the Infrastructure Domain).

NOTE 3:	Entity B will associate the configured Entity A identity with messages secured within Security Contexts established using the Pre-Provisioned Secure Connection Key Kpsa associated with the Pre-Provisioned Secure Connection Key Identifier KpsaId.

NOTE 4:	In many scenarios, the entity identities will be configured when the Pre-Provisioned Secure Connection Key Kpsa is established, so a separate configuration is not required in those scenarios.

### Centralized Key Distribution Server Handshake: There is no Centralized Key Distribution Server Handshake applied in the Pre-Provisioned Secure Connection Key Security Association Establishment Framework.

Association Security Handshake: The entities perform a (D)TLS-PSK handshake [15] to establish a secure session.

The "psk_identity" parameter [15] is set to the value of the Pre-Provisioned Secure Connection Key Identifier KpsaId.

The "psk" parameter [15] is set to the value of the Pre-Provisioned Secure Connection Key Kpsa.

Mandatory and optional (D)TLS cipher suites for this phase are specified in clause 9.2.

#### 8.2.2.2	Certificate-Based Security Association Establishment Frameworks

This clause describes the Certificate-Based Security Association Establishment Framework.

Figure 8.2.2.2-1 illustrates the sequence of events when using the Certificate-Based Security Association Establishment Framework. In this description, "Entity A" and "Entity B" correspond to CSEs or AEs.

NOTE:	The following font colours differentiate the general topic that the text relates to:

Blue italic text highlights details specific to this particular Security Association Establishment Framework.

Purple italic text highlights technical actions that may include steps not specified by oneM2M.

Red italic text highlights security-related properties.

Figure 8.2.2.2-1: The sequence of events when using the Certificate-Based Security
Association Establishment Framework

Credential Configuration: The master credentials for each entity are pre-provisioned as described in clause 8.1.1.2.1 "Credential Configuration for Certificate-Based Security Frameworks".

NOTE:	Long term master credentials (private keys) can pose a security risk if not adequately secured, and for this reason are recommended to be stored in Secure Environments.

Association Configuration: Entity A and Entity B  are configured with the information needed for the authentication and identification (during Security Handshake) of  Entity B and Entity A respectively:

Entity A is commanded to initiate a Security Handshake, and the command includes the following arguments:

The Entity B Certificate Name. This value is used by Entity A when verifying Entity B’s Certificate in the Association Security Handshake.

The Entity B Root of Trust. This value is used by Entity A when verifying Entity B’s Certificate in the Association Security Handshake.

The Entity A identity (IdA) Entity A is to use this entity identity with Entity B.

The Entity B identity (IdB). Entity A is to use this identity for Entity B authenticating using the above arguments. This is used to route the (D)TLS exchange).

The mechanisms for achieving this are discussed in clause 8.4.1.2 (for the cases where Entity A is in the Field Domain) and clause 8.4.2 (for the cases where Entity A is in the Infrastructure Domain).

NOTE 1:	The Entity A will associate Entity B's identity with messages secured within Security Contexts established in accordance with the configured Entity B Certificate Name and Entity B Root of Trust.

The Entity B is configured with the following arguments describing Entity A authorized to perform Security Handshake with Entity B:

The Entity A Certificate Name. This value is used by Entity B when verifying Entity A’s Certificate in the Association Security Handshake.

The Entity A Root of Trust. This value is used by Entity B when verifying Entity A’s Certificate or Certificate Chain in the Association Security Handshake.

The Entity A identity (IdA). Entity B is to use this entity identity for Entity A authenticating using the above arguments.

The Entity B Identity (IdB), if not already configured to Entity B. Entity B is to assume this identity when interacting with Entity A.

The mechanisms for achieving this are discussed in clause 8.4.1.2 (for the cases where Entity A is in the Field Domain) and Clause 8.4.2 (for the cases where Entity A is in the Infrastructure Domain).

NOTE 2:	Entity B will associate Entity A's identity with messages secured within Security Contexts established in accordance with the configured Entity A Certificate Name and Entity A Root of Trust.

### Centralized Key Distribution Server Handshake: There is no Centralized Key Distribution Server Handshake applied in the Certificate-Based Security Association Establishment Framework.

Association Security Handshake:

Each entity verifies the other entity's certificate as described in clause 8.1.1.2.2 "Certificate Verification".

The entities authenticate each other using the validated certificates as specified in TLS 1.2 RFC 5246 [16] and DTLS 1.2 RFC 6347 [17] specifications.

Mandatory and optional (D)TLS cipher suites for this phase are specified in clause 9.2.

### 8.2.3	Centralized Security Association Establishment Frameworks

#### 8.2.3.1	MAF-Based Symmetric Key Security Association Establishment Frameworks

Editor's Note: Text is required here.

Editor's Note: This will include reference to the communication (protocol?) between the entity B and the MAF in clause 8.5.

#### 8.2.3.2	GBA-Based Security Association Establishment Frameworks

To obtain a short term key used for M2M Service Connection between a M2M Application Service/Middle Node and a M2M Infrastructure Node, the M2M Application Service/Middle Node shall perform a successful GBA bootstrapping and derive a NAF key (Ks_(ext/int)_NAF). This NAF key is the M2M Secure Connection Key used for M2M Service Connection.

Editor's Note: Further text is required here.

## 8.3	Security Bootstrap Frameworks

### 8.3.1	Overview on Security Bootstrap Frameworks

#### 8.3.1.1	Purpose of Security Bootstrap Frameworks

The MAF-based Security Association Establishment Framework uses a Master Credential (Km) and corresponding Master Credential Identifier (KmId), shared by a CSE/AE and an M2M Authentication Function, to establish security associations between the CSE/AE and other CSEs and/or AEs as described in clause 8.2.3.

The Master Credential (Km) and corresponding Master Credential Identifier (KmId) shall either be pre-provisioned or remotely provisioned to the CSE/AE and M2M Authentication Function.

The details for pre-provisioning are not described in this specification.

Clause 8.3 describes the set of remote provisioning mechanisms; called Security Bootstrap Frameworks. An M2M Enrolment Function facilitates the remote provisioning.

#### 8.3.1.2	Overview on Security Bootstrap Frameworks

An AE or CSE that requires remote provisioning of a Master Credential and Master Credential Identifier is called an Enrolee.

The oneM2M system supports the following Security Bootstrap Frameworks:

Direct Security Bootstrap Frameworks

Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework: A symmetric key is pre-provisioned to the Enrolee and M2M Enrolment Function for the mutually authentication of those entities. For more details, see clause 8.3.2.1.

Certificate-Based Security Bootstrap Framework: The Enrolee and M2M Enrolment Function are each issued with

a Private Signing Key that is known only to that entity,

a Certificate containing the corresponding Public Verification Key, and

(Optionally) a Certificate Chain from the entity's Certificate to a Root Certificate.

The Enrolee and M2M Enrolment Function shall validate each other's Certificate before trusting the Public Verification Keys in the Certificate. Within the Security Handshake, the M2M Enrolment Function creates a digital signature of the session parameters using its private signing key and the Enrolee verifies the digital signature using the M2M Enrolment Function's public verification key. Then the roles are reversed: the Enrolee creates a digital signature and the M2M Enrolment Function verifies it. For more details see clause 8.3.2.2.

Centralized Security Bootstrap Frameworks

GBA-based Security Bootstrap Framework. In this case, the M2M Enrolment Function includes the functionality of a GBA Bootstrap Server Function. This framework uses 3GPP or 3GPP2 symmetric keys to authenticate the Enrolee and the M2M Enrolment Function (which is also a GBA BSF). The details are specified by 3GPP [4] and 3GPP2 [14]. For more details see clause 8.3.3.1.

For a more detailed description of the above Security Bootstrap Frameworks, it is useful to compare the following aspects of the Security Bootstrap Frameworks.

Bootstrap Credential Configuration: The Enrolee and M2M Enrolment Function are pre-provisioned with the Bootstrap Credential that the entity will use to authenticate itself to the other entity. This configuration can for example be done at manufacturing before a device is associated with a particular M2M SP. The mechanisms for this pre-provisioning are not described in this specification.

Bootstrap Instruction Configuration: The Enrolee and M2M Enrolment Function are provided with

The M2M Authentication Function Identifier (MAF-ID) identifying the M2M Authentication Function for which the Enrolee is to be remotely provisioned.

NOTE 1:	The identity of the M2M Authentication Function is assumed to have been configured prior to the Bootstrap Instruction Configuration phase.

The CSE-ID or AE-ID that the M2M Authentication Function is to associate with the Enrolee.

Additionally, in the case of Certificate-Based Security Bootstrap Framework:

The Enrolee is configured with the M2M Enrolment Function URI (for the purpose of routing the (D)TLS messages to the M2M Enrolment Function), M2M Enrolment Function Certificate Name and M2M Enrolment Function Root of Trust that the Enrolee will use to verify the M2M Enrolment Function.

The M2M Enrolment Function is configured with the Enrolee Certificate Name and Enrolee Root of Trust that the M2M Enrolment Function will use to verify the Enrolee.

Bootstrap Enrolment Handshake: Identification, authentication and security context establishment between the Enrolee and M2M Enrolment Function.

Enrolment Key Generation: generating a symmetric Enrolment Key,(Ke) and corresponding Enrolment Key Identifier (KeId) shared by the Enrolee and M2M Enrolment Function, which is used for subsequent generation of the Master Credential (Km).

Usage in Centralized Key Distribution Server Handshake: During the Centralized Key Distribution Server Handshake of the MAF-Based Security Association Establishment, the following steps occurs

The Enrolee derives the Master Credential (Km) from the Enrolment Key (Ke) and M2M Authentication Function Identifier (MAF-ID). Details of the derivation are provided in clause 9.4.

The Enrolee generates the Master Credential Identifier (KmId) from Master Credential (Km) as described in clause 9.1, and stores Km and KmId.

The Enrolee passes the Enrolment Key Identifier (KeId)  to the M2M Authentication Function (see "Centralized Key Distribution Server Handshake" in clause 8.2.3.1)

NOTE 2:	When the Enrolee first communicates with the M2M Authentication Function, then the M2M Authentication Function has not yet retrieved the Km from the M2M Enrolment Function. Consequently, the Enrolee provides the KeId to the M2M Authentication function, which is then passed to the M2M Enrolment Function to identify the Enrolment Key. The M2M Enrolment Function then returns the Km from which the M2M Authentication Function can derive the KmId. In subsequent Security Establishments, the Enrolee may provide the KmId or the KeId, and the M2M Authentication Function will know that both identifiers indicate the retrieved Km. For more details, see "Centralized Key Distribution Server Handshake" in clause 8.2.3.1.

Upon receipt of the KeId, the M2M Authentication Function determines if it already has the corresponding Km and CSE-ID or AE-ID of the Enrolee

If the M2M Authentication Function already has the corresponding Km and CSE-ID or AE-ID of the Enrolee, then the Km is used for mutual authentication (see "Centralized Key Distribution Server Handshake" in clause 8.2.3.1)

If the M2M Authentication Function does not have the corresponding Master Credential (Km) and CSE-ID or AE-ID of the Enrolee, then the following steps are followed.

-	The M2M Authentication Function (securely) passes the KeId to the M2M Enrolment Function, along with the M2M Authentication Function's URI.

-	The M2M Enrolment Function derives the Km from the Ke and MAF-ID. Details of the derivation are provided in clause 9.4.

-	The M2M Enrolment Function returns the Km to the M2M Authentication Function. The M2M Enrolment Function also passes the USS, including the CSE-ID or AE-ID of the Enrolee. More details are provided in clause 8.6.

-	The M2M Authentication Function generates the Master Credential Identifier (KmId) from Master Credential (Km) as described in clause 9.1, and stores Km and KmId.

-	The Master Credential (Km) is used for mutual authentication (see "Centralized Key Distribution Server Handshake" in clause 8.2.3.1).

Figure 8.3.1.2-1 provides a summary of the above defined Security Bootstrap Frameworks.

Figure 8.3.1.2-1: Overview of the Security Bootstrap Frameworks supported by oneM2M

Editor's note: In the above figure, the illustrations of the GBA-based centralized security frameworks may need to be updated when the detailed flows have been agreed. Additionally, more parameters may need to be transferred from MAF to MEF in the "Usage in Centralized Key Distribution Server Handshake". This is FFS.

### 8.3.2	Direct Security Bootstrap Framework

#### 8.3.2.1	Pre-Provisioned Symmetric Key Security Bootstrap Framework

This clause describes the Pre-Provisioned Symmetric Key Security Bootstrap Framework. The Bootstrap Credential for this framework is a long-term symmetric key that has been pre-provisioned into the Enrolee and M2M Enrolment Function; this key is called a Pre-Provisioned Symmetric Enrolee Key and is denoted Kpm.

NOTE:	Long term Pre-Provisioned Symmetric Enrolee Keys can pose a security risk if not adequately secured, and for this reason it is recommended that Long term Pre-Provisioned Symmetric Enrolee Keys are stored in Secure Environments.

Figure 8.3.2.1-1 illustrates the sequence of events when using the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework.

NOTE:	The following font colours differentiate the general topic that the text relates to:

Black text contains Security-Bootstrap-Framework-independent details

Blue italic text highlights details specific to this particular Security Bootstrap Framework.

Purple italic text highlights technical actions that may include steps not specified by oneM2M.

Figure 8.3.2.1-1: The sequence of events when using
the Pre-Provisioned Symmetric Key Security Bootstrap Framework

Editor's Note: More parameters may need to be transferred from MAF to MEF in the "Usage in Centralized Key Distribution Server Handshake". This is FFS.

Bootstrap Credential Configuration: The Pre-Provisioned Symmetric Enrolee Key (Kpm) and the corresponding Pre-Provisioned Symmetric Enrolee Key Identifier, denoted KpmId, are pre-provisioned to both entities. The Enrolee is also provisioned with the M2M Enrolment Function's URI (MEF URI), for the purpose of routing the (D)TLS exchange.

Bootstrap Instruction Configuration: The Enrolee and M2M Enrolment Function are configured with the information needed for authorizing the remote provisioning:

The Enrolee is configured with (or otherwise obtains) the following arguments to initiate remote provisioning :

M2M Authentication Function identity (MAF-ID): Identifying the M2M Authentication Function for which the Enrolee is to be provisioned.

Enrolee identity (Enrolee-ID): the Enrolee is to use this identity with the identified M2M Authentication Function.

The Enrolee associates these arguments with the M2M Enrolment Function. The M2M Enrolment Function can be identified to the Enrolee using the Pre-Provisioned Symmetric Enrolee Key Identifier (KpmId) or the M2M Enrolment Function URI.

The mechanisms for achieving this are discussed in clause 8.4.1.3.

M2M Enrolment Function is configured with the following arguments to authorize the M2M Enrolment Function to remotely provision the Enrolee for a M2M Authentication Function:

M2M Authentication Function Identity (MAF-ID) of the M2M Authentication Function for which the Enrolee is to be provisioned.

Enrolee identity (Enrolee-ID). The M2M Enrolment Function is to provide this entity identity for the Enrolee with the Master Credential (Km) to the target M2M Authentication Function, when requested by the M2M Authentication Function.

The M2M Enrolment Function associates these arguments with an Enrolee. The Enrolee can be identified to the M2M Enrolment Function using the Pre-Provisioned Symmetric Enrolee Key Identifier (KpmId).

The mechanisms for achieving this are discussed in clause 8.4.2.

Bootstrap Security Handshake: The Enrolee and M2M Enrolment Function perform a (D)TLS-PSK handshake [15] to establish a secure session.

The "psk_identity" parameter [15] is set to the value of the Pre-Provisioned Symmetric Enrolee Key Identifier (KpmId).

The "psk" parameter [15] is set to the value of the Pre-Provisioned Symmetric Enrolee Key (Kpm).

Mandatory and optional (D)TLS cipher suites for this phase are specified in clause 9.2.

Enrolment Key Generation:

The Enrolment Key (Ke) is generated from the (D)TLS session secrets by the Enrolee and M2M Enrolment Function using TLS Key Export (RFC 5705) [18], as described in clause 9.3.

The Enrolment Key Identifier (KeId) is generated by the Enrolee and M2M Enrolment Function, as described in clause 9.1.

The Enrolee and M2M Enrolment store the Enrolment Key (Ke) and Enrolment Key Identifier (KeId).

NOTE 2:	The Enrolment Key Generation for the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework is identical to the Enrolment Key Generation for the Certificate-Based Security Bootstrap Framework.

Usage in Centralized Key Distribution Server Handshake: See "Overview of Security Frameworks" in clause 8.3.1.

#### 8.3.2.2	Certificate-Based Security Bootstrap Framework

This clause describes the Certificate-Based Security Bootstrap Framework. The Bootstrap Credentials for this framework are Certificates.

NOTE:	Long term master credentials (private keys) can pose a security risk if not adequately secured, and for this reason are recommended to be stored in Secure Environments.

Figure 8.3.2.2-1 illustrates the sequence of events when using the Certificate-Based Security Bootstrap Framework.

NOTE:	The following font colours differentiate the general topic that the text relates to:
Black text contains Security Bootstrap-Framework-independent details.
Blue italic text highlights details specific to this particular Security Bootstrap Framework.
Purple italic text highlights technical actions that may include steps not specified by oneM2M.
Red italic text highlights security-related properties.

Figure 8.3.2.2-1: The sequence of events when using
the Certificate-Based Security Bootstrap Framework.

Editor's Note: More parameters may need to be transferred from MAF to MEF in the "Usage in Centralized Key Distribution Server Handshake". This is FFS.

Bootstrap Credential Configuration: For this Security Bootstrap Framework, Enrolee and M2M Enrolment Function authenticate each other using a Public Key Certificate. The Bootstrap Credentials for the Enrolee and M2M Enrolment Function are pre-provisioned as described in clause 8.1.1.2.1 "Credential Configuration for Certificate-Based Security Frameworks".

NOTE 1:	The identities of the M2M Enrolment Function and M2M Authentication Function are assumed to have been configured prior to this phase.

Editor's Note: The specification may need more details regarding configuring the identities of the M2M Enrolment Function and M2M Authentication Function.

Bootstrap Instruction Configuration: The Enrolee and M2M Enrolment Function  are configured with the information needed for authorizing the remote provisioning:

The Enrolee is configured with (or otherwise obtains) the following arguments to initiate remote provisioning:

The URI of the M2M Enrolment Function which will facilitate the remote provisioning, for the purpose of routing the (D)TLS exchange.

The M2M Enrolment Function Certificate Name. This value is used by the Enrolee when verifying the M2M Enrolment Function’s Certificate in the Bootstrap Security Handshake.

The M2M Enrolment Function Root of Trust. This value is used by the Enrolee when verifying the M2M Enrolment Function’s Certificate in the Bootstrap Security Handshake.

The target M2M Authentication Function Identity (MAF-ID), with whom the Enrolee is to be provisioned using Security Bootstrap.

The Enrolee identity (Enrolee-ID): The Enrolee is to use this entity identity with the identified M2M Authentication Function.

The mechanisms for achieving this are discussed in clause 8.4.1.2.

The M2M Enrolment Function is configured with the following arguments describing Enrolee authorized to perform Security Handshake with M2M Enrolment Function:

The Enrolee Certificate Name. This value is used by the M2M Enrolment Function when verifying the Enrolee’s Certificate in the Bootstrap Security Handshake.

The Enrolee Root of Trust. This value is used by the M2M Enrolment Function when verifying the Enrolee’s Certificate in the Bootstrap Security Handshake.

The target M2M Authentication Function Identity (MAF-ID), with whom the Enrolee (authenticated using the above Enrolee Certificate Name and Enrolee Root of Trust) is to be provisioned using Security Bootstrap.

The Enrolee identity (Enrolee-ID). The M2M Enrolment Function is to provide this entity identity for the Enrolee with the Master Credential (Km) to the target M2M Authentication Function, when requested by the M2M Authentication Function.

The mechanisms for achieving this are discussed in clause 8.4.2.

Bootstrap Security Handshake: The Enrolee and M2M Enrolment Function perform a (D)TLS handshake as specified in TLS 1,2 RFC 5246 [16] and DTLS 1.2 RFC 6347 [17] specifications.to establish a secure session.

Each entity (Enrolee and M2M Enrolment Function) verifies the other entity's certificate as described in clause 8.1.1.2.2 "Certificate Verification".

The Enrolee and M2M Enrolment Function authenticate each other using the validated certificates as specified in TLS 1.2 RFC 5246 [16] and DTLS 1.2 RFC 6347 [17] specifications.

Mandatory and optional TLS cipher suites for this phase are specified in clause 9.2.

Enrolment Key Generation:

The Enrolment Key (Ke) is generated from the (D)TLS session secrets by the Enrolee and M2M Enrolment Function using TLS Key Export (RFC 5705) [18], as described in clause 9.3.

The Enrolment Key Identifier (KeId) is generated by the Enrolee and M2M Enrolment Function, as described in clause 9.1.

The Enrolee and M2M Enrolment store the Enrolment Key (Ke) and Enrolment Key Identifier (KeId).

NOTE 2:	The Enrolment Key Generation for the Pre-Provisioned Symmetric Enrolee Key Security Bootstrap Framework is identical to the Enrolment Key Generation for the Certificate-Based Security Bootstrap Framework.

Usage in Centralized Key Distribution Server Handshake: See "Overview of Security Frameworks" in clause 8.3.1.

### -----------------------End of change 1---------------------------------------------

# Comments

This editor's note has been moved here from It is unclear at this stage if anymore details are required, so we should leave the edtior's note in the text (in 83.1.2) as a reminder.