| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 (SEC) at TP#11 |
| Title:* | oneM2M Access Control Policy Specification |
| Source:* | CATT |
| Contact: | Wei Zhou, zhouwei@catt.cn Hui Xu, xuhui@catt.cn |
| Date:* | 2014-07-08 |
| Abstract:* | Proposing a sub-clause in the Security TS for release 1: “Access Control Policy Specification” |
| Agenda Item:* | TBD |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | oneM2M-TS-0003 Security Solutions |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

This contribution aims to propose a sub-clause in the Security TS for release 1: “Access Control Policy Specification”

2	Proposal

## x.x	Access Control Policy Specification

### x.x.1	Element <DecisionRequest>

The <DecisionRequest> element is used by a PEP for describing an resource access in an access control decision request that will be sent to a PDP for obtaining an access control decision.

<xs:element name="DecisionRequest" type="DecisionRequestType"/>

<xs:complexType name="DecisionRequestType">

<xs:sequence>

<xs:element ref="Resource"/>

<xs:element ref="Originator"/>

<xs:element ref="Operation"/>

<xs:element ref="Context" minOccurs="0"/>

</xs:sequence>

</xs:complexType>

The < DecisionRequest > element contains the following elements:

Resource [Required]

It provides the URI of the target resource that the Originator wants to access.

Originator [Required]

It provides the ID of the Originator with some optional attributes pertained to the Originator such as roles and/or groups.

Operation [Required]

It provides the operation that the Originator wants to perform on the target resource.

Context [Optional]

It provides some extra information related to the Originator such as location and/or IP address.

### x.x.1	Element <DecisionResponse>

The <DecisionResponse> element is used by a PDP for providing access control decision result in an access control decision response that will be sent to a PEP as a response to an access control decision request

<xs:element name="Response" type="ResponseType"/>

<xs:complexType name="ResponseType">

<xs:sequence>

<xs:element ref="Result"/>

</xs:sequence>

</xs:complexType>

The < DecisionResponse> element contains the following elements:

Result [Required]

It provides an access control decision result. See Section x.x.x.

### x.x.1	Element <Request>

The <Request> element is generated based on the content provided by the <DecisionRequest> element by the PDP. The PDP uses the content of <Request> element for evaluating access control policy set, access control policies or access control rules.

<xs:element name="Request" type="RequestType"/>

<xs:complexType name="RequestType">

<xs:sequence>

<xs:element ref="Originator"/>

<xs:element ref="Operation"/>

<xs:element ref="Context" minOccurs="0"/>

</xs:sequence>

</xs:complexType>

The < DecisionRequest > element contains the following elements:

Originator [Required]

It provides the ID of the Originator with some optional attributes pertained to the Originator such as roles and/or groups.

Operation [Required]

It provides the operation that the Originator wants to perform on the target resource.

Context [Optional]

It provides some extra information related to the Originator such as location and/or IP address.

### x.x.1	Element <Result>

The <Result> element represents a result of evaluating an access control policy set, access control policy or an access control policy rule.

<xs:element name="Result" type="ResultType"/>

<xs:complexType name="ResultType">

<xs:sequence>

<xs:element ref="Decision"/>

<xs:element ref="Status" minOccurs="0"/>

</xs:sequence>

</xs:complexType>

The < DecisionRequest > element contains the following elements:

Decision [Required]

It provides the evaluation result of a policy set, a policy or a rule. Its value can be: “Permit”, “Deny”, “Indeterminate” or “NotApplicable”.

Status [Optional]

It provides the information about the errors occurred during the evaluation of the decision request.

### x.x.1	Element <Decision>

The <Decision> element contains the result of access control policy set, access control policy or access control rule evaluation.

<xs:element name="Decision" type="DecisionType"/>

<xs:simpleType name="DecisionType">

<xs:restriction base="xs:string">

<xs:enumeration value="Permit"/>

<xs:enumeration value="Deny"/>

<xs:enumeration value="Indeterminate"/>

<xs:enumeration value="NotApplicable"/>

</xs:restriction>

</xs:simpleType>

The meanings of the values of the <Decision> element are described in Section x.x.x.

### x.x.1	Element <Status>

The <Status> element represents the status of the access control decision result.

<xs:element name="Status" type="StatusType"/>

<xs:complexType name="StatusType">

<xs:sequence>

<xs:element ref="StatusCode" minOccurs="0"/>

<xs:element ref="StatusMessage" minOccurs="0"/>

</xs:sequence>

</xs:complexType>

The < DecisionRequest > element contains the following elements:

StatusCode [Required]

It provides a status code of an access control decision result. See Section x.x.x.

StatusMessage [Optional]

It provides a status message describing the status code.

### x.x.1	Element <StatusCode>

The <StatusCode> element contains a status code value. The following status code values defined in this document are the same as defined in [i.7].

<xs:element name="StatusCode" type="StatusCodeType"/>

<xs:simpleType name="StatusCodeType">

<xs:restriction base="xs:string">

<xs:enumeration value="ok"/>

<xs:enumeration value="missing-attribute"/>

<xs:enumeration value="processing-error"/>

<xs:enumeration value="syntax-error"/>

</xs:restriction>

</xs:simpleType>

The values of the <StatusCode> element have the following meanings:

ok: This identifier indicates success.

missing-attribute: This identifier indicates that all the attributes necessary to make a policy decision were not available.

processing-error: This identifier indicates that an error occurred during policy evaluation. An example would be division by zero.

syntax-error: This identifier indicates that some attribute value contained a syntax error, such as a letter in a numeric field.

### x.x.1	Element <StatusMessage>

The <StatusMessage> element is a free-form description of the status code.

<xs:element name="StatusMessage" type="xs:string"/>

### x.x.1	Element <PolicySet>

The <PolicySet> element is the top-level element in the access control policy schema. <PolicySet> is an aggregation of policies that are applicable to a particular access control decision request. Access control policies may be included in an enclosing <PolicySet> element either directly using the <Policy> element or indirectly using the <PolicyIdReference> element.

The PAP finds all applicable access control policies that are applicable to an access control decision request and encapsulates them into a <PolicySet> element. The policies in a <PolicySet> element shall be combined with policy combining algorithm according to a predefined a configuration file. This predefined configuration file specifies how to combine the applicable access control policies for a particular access control decision request.

The PDP evaluates the access control policies contained in a <PolicySet> element, and combines the evaluation results of these policies in order to obtain one policy set evaluation result.

<xs:element name="PolicySet" type="PolicySetType"/>

<xs:complexType name="PolicySetType">

<xs:sequence>

<xs:choice minOccurs="0" maxOccurs="unbounded">

<xs:element ref="Policy"/>

<xs:element name="PolicyIdReference" type="xs:anyURI"/>

</xs:choice>

</xs:sequence>

<xs:attribute name="PolicySetId" type="xs:anyURI" use="required"/>

<xs:attribute name="PolicyCombiningAlgId" type="xs:anyURI" use="required"/>

</xs:complexType>

The <PolicySet> element contains the following attributes and elements:

PolicySetId [Required]

It provides the identifier of a policy set. It is the responsibility of the PAP to ensure that no two policy sets visible to the PDP have the same identifier.

PolicyCombiningAlgId [Required]

It provides the identifier of the policy-combining algorithm by which the policy evaluation results in the policy set shall be combined. For more information about policy-combining algorithm see Section x.x.x.

Policy [Any Number]

A policy that is included in this policy set.

PolicyIdReference [Any Number]

It provides a reference to a policy that MUST be included in this policy set.

### x.x.1	Element <Policy>

The <Policy> element is the smallest entity that shall be presented to the PDP for evaluation. <Policy> is an aggregation of rules that are applicable to the target resource. Rules included in the <Policy> element must be combined by the algorithm specified by the RuleCombiningAlgId attribute in order to obtain one policy evaluation result.

<xs:element name="Policy" type="PolicyType"/>

<xs:complexType name="PolicyType">

<xs:sequence>

<xs:choice maxOccurs="unbounded">

<xs:element ref="Rule"/>

</xs:choice>

</xs:sequence>

<xs:attribute name="PolicyId" type="xs:anyURI" use="required"/>

<xs:attribute name="RuleCombiningAlgId" type="xs:anyURI" use="required"/>

</xs:complexType>

The <Policy> element contains the following attributes and elements:

PolicyId [Required]

It provides the identifier of a policy. It is the responsibility of the PAP to ensure that no two policies visible to the PDP have the same identifier.

RuleCombiningAlgId [Required]

It provides the identifier of the rule-combining algorithm by which the rule evaluation results in the policy shall be combined. For more information about rule-combining algorithm see Section x.x.x.

Rule [Any Number]

A rule that is included in this policy.

### x.x.1	Element <Rule>

The <Rule> element shall define the individual rules in the policy.

<xs:element name="Rule" type="RuleType"/>

<xs:complexType name="RuleType">

<xs:sequence>

<xs:element ref="Originator"/>

<xs:element ref="Operations"/>

<xs:element ref="Contexts" minOccurs="0"/>

</xs:sequence>

</xs:complexType>

The <Rule> element contains the following attributes and elements:

Originator [Required]

It provides the identifier of a policy.

Operation [Required]

It provides the operation that the Originator can perform on the target resource.

Context [Optional]

It provides predicates that must be satisfied for the rule can be used for evaluating the access control decision request.

### x.x.1	Element <Originator>

The <Originator> element defines attributes pertaining to the Originator. The main components of this element are the <OriginatorID>, <Roles> and <Groups> elements.

The <Originator> element is used in access control decision requests, access control policy evaluation requests and access control rules for describing the Originator.

<xs:element name="Originator" type="OriginatorType"/>

<xs:complexType name="OriginatorType">

<xs:sequence>

<xs:element ref="OriginatorID"/>

<xs:element ref="Roles" minOccurs="0"/>

<xs:element ref="Groups" minOccurs="0"/>

</xs:sequence>

</xs:complexType>

The <Originator> element contains the following attributes and elements:

OriginatorID [Required]

It provides the ID of the Originator.

Operations [Optional]

It provides the roles that the Originator owns.

Contexts [Optional]

It provides the groups to which the Originator belongs.

### x.x.1	Element <OriginatorID>

The <OriginatorID> element provides the ID of the Originator.

<xs:element name="OriginatorID"  type="xs:string"/>

### x.x.1	Element <Roles>

The <Roles> element specifies a list of <Role> elements.

<xs:element name="Roles" type="RolesType"/>

<xs:complexType name="RolesType">

<xs:sequence>

<xs:choice maxOccurs="unbounded">

<xs:element ref="Role"/>

</xs:choice>

</xs:sequence>

</xs:complexType>

The <Roles> element contains the following attributes and elements:

Role [Any Number]

It provides an ID of a role.

### x.x.1	Element <Role>

The <Role> element provides the ID of the Role.

<xs:element name="Role"  type="xs:anyURI"/>

### x.x.1	Element <Groups>

The <Groups> element specifies a list of <Group> elements.

<xs:element name="Groups" type="GroupsType"/>

<xs:complexType name="GroupsType">

<xs:sequence>

<xs:choice maxOccurs="unbounded">

<xs:element ref="Group"/>

</xs:choice>

</xs:sequence>

</xs:complexType>

The <Groups> element contains the following attributes and elements:

Group [Any Number]

It provides an ID of a group.

### x.x.1	Element <Group>

The <Group> element provides the ID of the Group.

<xs:element name="Group"  type="xs:anyURI"/>

### x.x.1	Element <Resource>

The <Resource> element provides the URI of a Resource.

<xs:element name="Resource"  type="xs:anyURI"/>

### x.x.1	Element <Operations>

The <Operations> element specifies a list of <Operation> elements.

<xs:element name="Operations" type="OperationsType"/>

<xs:complexType name="OperationType">

<xs:sequence>

<xs:choice maxOccurs="unbounded">

<xs:element ref="Operation"/>

</xs:choice>

</xs:sequence>

</xs:complexType>

The <Operations> element contains the following attributes and elements:

Operation [Any Number]

It specifies an operation.

### x.x.1	Element <Operation>

The <Operation> element contains an operation that an Originator can perform on a resource.

<xs:element name="Operation" type="OperationType"/>

<xs:simpleType name="DecisionType">

<xs:restriction base="xs:string">

<xs:enumeration value="RETRIEVE"/>

<xs:enumeration value="CREATE"/>

<xs:enumeration value="UPDATE"/>

<xs:enumeration value="DELETE"/>

<xs:enumeration value="DISCOVER"/>

<xs:enumeration value="NOTIFY"/>

</xs:restriction>

</xs:simpleType>

The meanings of the values of the <Operation> element are described in Clause 9.6.2.3 in the oneM2M Functional Architecture [TS-0001].

### x.x.1	Element <Contexts>

The <Contexts> element specifies a list of <Context> elements.

<xs:element name="Contexts" type="ContextsType"/>

<xs:complexType name="ContextsType">

<xs:sequence>

<xs:choice maxOccurs="unbounded">

<xs:element ref="Context"/>

</xs:choice>

</xs:sequence>

</xs:complexType>

The <Contexts> element contains the following attributes and elements:

Context [Any Number]

It specifies a Context.

### x.x.1	Element <Context>

The <Context> element contains an operation that an Originator can perform on a resource.

<xs:element name="Context" type="ContextType"/>

<xs:complexType name="ContextType">

<xs:sequence>

<xs:element ref="TimeWindow" minOccurs="0"/>

<xs:element ref="LocationRegion" minOccurs="0"/>

<xs:element ref="IPAddress" minOccurs="0"/>

</xs:sequence>

</xs:complexType>

The meanings of the values of the elements of <TimeWindow>, <LocationRegion> and <IPAddress> are described in Clause 9.6.2.2 in the oneM2M Functional Architecture [TS-0001].

### x.x.1	Element <TimeWindow>

The <TimeWindow> element specifies a time window with a start time and an end time. The format for specifying a time window is defined in Clause 7.1.

<xs:element name="TimeWindow"  type="xs:string"/>

### x.x.1	Element <LocationRegion>

The <LocationRegion> element specifies a location region. The format for specifying a location region is defined in Clause 7.1.

<xs:element name="LocationRegion"  type="xs:string"/>

### x.x.1	Element <IPAddress>

The <IPAddress> element specifies an IP address. The format for specifying an IP address is defined in Clause 7.1.

The <IPAddress> element provides the ID of the Originator.

<xs:element name="IPAddress"  type="xs:string"/>