| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 (SEC) at TP#12 |
| Title:* | oneM2M Access Control Policy Structure and Evaluation |
| Source:* | CATT, CATR |
| Contact: | Wei Zhou, zhouwei@catt.cn Hui Xu, xuhui@catt.cn Song Luo, luosong@catr.cn |
| Date:* | 2014-07-28 |
| Abstract:* | Proposing a sub-clause in the Security TS for release 1: “Access Control Policy Structure and Evaluation” |
| Agenda Item:* | TBD |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | oneM2M-TS-0003 Security Solutions |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

This contribution aims to propose a sub-clause in Clause 7 in the Security TS for release 1.

2	Proposal

## 7.x	Access Control Policy Structure and Evaluation

### 7.x.1	Access Control Policy Structure

oneM2M access control policy comprises the following three components:

- Access Control Rule;

- Access Control Policy; and

- Access Control Policy set.

#### 7.x.1.1	Access Control Rule

A set of accces control rules is represented by the privileges and selfPrivileges in the <accessControlPolicy> resource. An access control rule is the basic elementary unit of policy. The main components of a rule are:

- an accessControlOriginators,

- an accessControlOperations, and

- an accessControlContexts.

An access control rule specifies that any entity defined in the component accessControlOriginators can perform any operation defined in the component accessControlOperations on the target resource. The component accessControlContexts defines a set of conditions that must evaluate to “True” for the rule to be applicable in an access control decision making process.

For more information about the access control rule see Clause 7.3 and Clause 7.5.

#### 7.x.1.2	Access Control Policy

An access control policy is the basic elementary unit assigned to a protected resource. It is also the smallest entity that shall be presented to a PDP for evaluation. An access control policy is comprised of a set of access control rules that are all applicable to the protected resource. The evaluation results of these access control rules shall be combined by a rule combining algorithm in order to render a finial evaluation result. This finial evaluation result shall be used as the access control policy evaluation result. Rule combining algorithms are described in Clause 7.x.3.

An access control policy may be shared by multiple resources, and an access to a resource may need to consider multiple access control policies. It is the responsibility of PRP to find all applicable access control policies through checking the target resource accessControlPolicyIDs attribute that lists all applicable access control policies’ IDs or URIs.

#### 7.x.1.3	Access Control Policy Set

An access control policy set is the basic elementary passed to a PDP by a PRP. An access control policy set is comprised of a set of access control policies that are all applicable to the protected resource. The evaluation results of these access control policies shall be combined by a policy combining algorithm in order to render a finial evaluation result. This finial evaluation result shall be used as the policy set evaluation result. Policy combining algorithms are described in Section 7.x.3.

It is the responsibility of PRP to find all applicable access control policies and organize these access control policies into an access control policy set. The policy combining algorithm is selected according to a predefined configuration file that specifies which policy combining algorithm shell be used for what access control decision requests or resources. However, the description about this configuration file is outside the scope of this specification.

### 7.x.2	Access Control Policy Evaluation Result

The evaluation result of an access control rule shall be either “Permit” or “Deny”. For more information about the access control rule evaluation procedure see Clause 7.5.1.

The evaluation result of an access control policy is the result of combining the evaluation results of the rules contained in this access control policy, and it shall be either “Permit” or “Deny”. For more information about the access control policy evaluation procedure see Clause 7.x.3.

The evaluation result of an access control policy set is the result of combining the evaluation results of the policies contained in this access control policy set, and it shall be either “Permit” or “Deny”. For more information about the access control policy set evaluation procedure see Clause 7.x.3.

### 7.x.3	Access Control Rule and Policy Combining Algorithms

An access control rule combining algorithm defines a procedure for arriving at an access control decision given the individual results of evaluation of a set of access control rules. Similarly, an access control policy combining algorithm defines a procedure for arriving at an access control decision given the individual results of evaluation of a set of access control policies. This specification adopts the “Permit-overrides” rule/policy combining algorithm that is defined in [i.7] with some simplification.

#### 7.x.3.1	Permit-Overrides

The “Permit-overrides” combining algorithm is intended for those cases where a permit decision should have priority over a deny decision. This algorithm has the following behaviour.

- If any decision is “Permit”, the result is “Permit”.

- Otherwise, the result is “Deny”.

### 7.x.4	Access Control Policy Evaluation

Access control policy evaluation consists of three phases:

- access control rule evaluation,

- access control policy evaluation, and

- access control policy set evaluation.

#### 7.x.4.1	Access Control Rule Evaluation

The evaluation result of an access control rule shall be calculated by evaluating its contents against an access control decision request. For more information about the access control rule evaluation procedure see Clause 7.5.1.

#### 7.x.4.2	Access Control Policy Evaluation

The evaluation result of an access control policy shall be determined by combining its rules’ evaluation results using the specified rule-combining algorithm. For more information about the access control policy evaluation procedure see Clause 7.x.3.

#### 7.x.4.3	Access Control Policy Set Evaluation

The evaluation result of an access control policy set shall be determined by combining its policies’ evaluation results using the specified policy-combining algorithm. For more information about the access control policy set evaluation procedure see Clause 7.x.3.