| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 (SEC) at TP#12 |
| Title:* | oneM2M Access Control Policy Specification |
| Source:* | CATT |
| Contact: | Wei Zhou, zhouwei@catt.cn Hui Xu, xuhui@catt.cn |
| Date:* | 2014-07-28 |
| Abstract:* | Proposing oneM2M Access Control Policy Specification in XSD format. |
| Agenda Item:* | TBD |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | oneM2M-TS-0003 Security Solutions |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

This contribution aims to propose oneM2M Access Control Policy Specification in XSD format for the Security TS Release 1.

2	Proposal

## x	Access Control Policy Specification

### x.1	Element <PolicySet>

The <PolicySet> element is the top-level element in the access control policy schema. <PolicySet> is an aggregation of policies that are applicable to an access control decision request. Access control policies may be included in an enclosing <PolicySet> element either directly using the <Policy> element or indirectly using the <PolicyReference> element.

The PRP is responsible for finding all applicable access control policies to an access control decision request and encapsulating them into a <PolicySet> element. The policies in a <PolicySet> element shall be combined with a policy combining algorithm according to a predefined configuration file. This configuration file specifies how to combine the applicable access control policies for a particular access control decision request.

The PDP evaluates the access control policies included in a <PolicySet> element, and combines the policy evaluation results by the algorithm specified by the PolicyCombiningAlgId attribute in order to obtain one policy set evaluation result.

<xs:element name="PolicySet" type="PolicySetType"/>

<xs:complexType name="PolicySetType">

<xs:sequence>

<xs:choice minOccurs="0" maxOccurs="unbounded">

<xs:element ref="Policy"/>

<xs:element ref="PolicyReference"/>

</xs:choice>

</xs:sequence>

<xs:attribute name="PolicySetId" type="xs:anyURI" use="required"/>

<xs:attribute name="PolicyCombiningAlgId" type="xs:anyURI" use="required"/>

</xs:complexType>

The <PolicySet> element contains the following attributes and elements:

PolicySetId [Required]

It provides the identifier of a policy set. It is the responsibility of the PRP to ensure that no two policy sets visible to the PDP have the same identifier.

PolicyCombiningAlgId [Required]

It provides the identifier of the policy-combining algorithm by which the policy evaluation results in the policy set shall be combined. For more information about policy-combining algorithm see Clause 7.x.3 in the oneM2M Security Solutions [TS-0003].

Policy [Any Number]

A policy that is included in this policy set.

PolicyReference [Any Number]

It provides a reference to a policy that must be included in this policy set.

### x.2	Element <Policy>

The <Policy> element is the smallest entity that shall be presented to the PDP for evaluation. <Policy> is an aggregation of rules that are applicable to the target resource. Rules included in the <Policy> element must be combined by the algorithm specified by the RuleCombiningAlgId attribute in order to obtain one policy evaluation result.

<xs:element name="Policy" type="PolicyType"/>

<xs:complexType name="PolicyType">

<xs:sequence>

<xs:element ref="Rule" maxOccurs="unbounded"/>

</xs:sequence>

<xs:attribute name="PolicyId" type="xs:anyURI" use="required"/>

<xs:attribute name="RuleCombiningAlgId" type="xs:anyURI" use="required"/>

</xs:complexType>

The <Policy> element contains the following attributes and elements:

PolicyId [Required]

It provides the identifier of a policy. It is shall be ensured that no two policies visible to the PDP have the same identifier.

RuleCombiningAlgId [Required]

It provides the identifier of the rule-combining algorithm by which the rule evaluation results in the policy shall be combined. For more information about rule-combining algorithm see Clause 7.x.3 in the oneM2M Security Solutions [TS-0003].

Rule [Any Number]

A rule that is included in this policy.

### x.3	Element <PolicyReference>

The <PolicyReference> element provides the URI of a Policy resource.

<xs:element name="PolicyReference" type="xs:anyURI"/>

### x.4	Element <Rule>

The <Rule> element shall define the individual rules in the policy.

<xs:element name="Rule" type="RuleType"/>

<xs:complexType name="RuleType">

<xs:sequence>

<xs:element ref="Subjects"/>

<xs:element ref="Operations"/>

<xs:element ref="Contexts" minOccurs="0"/>

</xs:sequence>

<xs:attribute name="RuleId" type="xs:string" use="required"/>

</xs:complexType>

The <Rule> element contains the following attributes and elements:

RuleId [Required]

A string identifying this rule.

Subjects [Required]

It provides the information about Originators that are permitted to perform specified operations on the target resources in the rule.

Operations [Required]

It provides a list of operations that the subjects can perform on the target resources in the rule.

Contexts [Optional]

It provides some conditions that must be satisfied for a rule being used for evaluating an access control decision request.

### x.5	Element <Subjects>

The <Subjects> element shall define the Originators that are permitted to perform specified operations on the target resources in a rule.

<xs:element name="Subjects" type="SubjectsType"/>

<xs:complexType name="SubjectsType">

<xs:sequence>

<xs:element ref="Originators"/>

</xs:sequence>

</xs:complexType>

The <Subjects> element contains the following elements:

Originators [Optional]

It provides a list of Originator IDs.

### x.6	Element <Originators>

The <Originators> element specifies a list of <Originator> elements.

<xs:element name="Originators" type="OriginatorsType"/>

<xs:complexType name="OriginatorsType">

<xs:sequence>

<xs:element ref="Originator" maxOccurs="unbounded"/>

</xs:sequence>

</xs:complexType>

The <Originators> element contains the following attributes and elements:

Originator [Required]

It specifies an Originator.

### x.7	Element <Originator>

The <Originator> element specifies an Originator.

<xs:element name="Originator" type="OriginatorType"/>

<xs:complexType name="OriginatorType">

<xs:sequence>

<xs:element name="Originator" type="xs:string"/>

</xs:sequence>

<xs:attribute name="Node" type="NodeType" use="required"/>

</xs:complexType>

The <Originator> element contains the following attributes and elements:

Originator [Required]

It provides the ID of the Originator.

NodeType [Required]

It provides the node type of the Originator.

### x.8	Simple Type NodeType

The NodeType simple type defines the values allowed for the Node attribute of the <Originator> element.

<xs:simpleType name="NodeType">

<xs:restriction base="xs:string">

<xs:enumeration value="AE"/>

<xs:enumeration value="CSE"/>

</xs:restriction>

</xs:simpleType>

### x.14	Element <Operations>

The <Operations> element specifies a list of <Operation> elements.

<xs:element name="Operations" type="OperationsType"/>

<xs:complexType name="OperationsType">

<xs:sequence>

<xs:element ref="Operation" maxOccurs="unbounded"/>

</xs:sequence>

</xs:complexType>

The <Operations> element contains the following attributes and elements:

Operation [Any Number]

It specifies an operation.

### x.15	Element <Operation>

The <Operation> element contains an operation that an Originator can perform on a resource.

<xs:element name="Operation" type="OperationType"/>

<xs:simpleType name="OperationType">

<xs:restriction base="xs:string">

<xs:enumeration value="RETRIEVE"/>

<xs:enumeration value="CREATE"/>

<xs:enumeration value="UPDATE"/>

<xs:enumeration value="DELETE"/>

<xs:enumeration value="DISCOVER"/>

<xs:enumeration value="NOTIFY"/>

</xs:restriction>

</xs:simpleType>

The meanings of the values of the <Operation> element are described in Clause 9.6.2.3 in the oneM2M Functional Architecture [TS-0001].

### x.16	Element <Contexts>

The <Contexts> element specifies conditions that must be satisfied for a rule being used for evaluating an access control decision request.

<xs:element name="Contexts" type="ContextsType"/>

<xs:complexType name="ContextsType">

<xs:sequence>

<xs:element ref="TimeWindows" minOccurs="0"/>

<xs:element ref="LocationRegions" minOccurs="0"/>

<xs:element ref="IPAddresses" minOccurs="0"/>

</xs:sequence>

</xs:complexType>

The <Contexts> element contains the following attributes and elements:

TimeWindows [Optional]

It specifies a list of time windows. The meaning of the time window is described in Clause 9.6.2.2 in the oneM2M Functional Architecture [TS-0001].

LocationRegions [Optional]

It specifies a list of location regions. The meaning of the location region is described in Clause 9.6.2.2 in the oneM2M Functional Architecture [TS-0001].

IPAddresses [Optional]

It specifies a list of IP addresses. The meaning of the IP address is described in Clause 9.6.2.2 in the oneM2M Functional Architecture [TS-0001].

### x.17	Element <TimeWindows>

The <TimeWindows> element specifies a list of <TimeWindow> elements.

<xs:element name="TimeWindows" type="TimeWindowsType"/>

<xs:complexType name="TimeWindowsType">

<xs:sequence>

<xs:element ref="TimeWindow" maxOccurs="unbounded"/>

</xs:sequence>

</xs:complexType>

The <TimeWindows> element contains the following attributes and elements:

TimeWindow [Any Number]

It specifies a TimeWindow.

### x.18	Element <TimeWindow>

The <TimeWindow> element specifies a time window. The format for specifying a time window is defined in Clause 7.1.

<xs:element name="TimeWindow" type="TimeWindowType"/>

<xs:complexType name="TimeWindowType">

<xs:sequence>

<xs:element name="StartTime" type="xs:string"/>

<xs:element name="EndTime" type="xs:string"/>

</xs:sequence>

</xs:complexType>

### x.19	Element <LocationRegions>

The <LocationRegions> element specifies a list of <LocationRegion> elements.

<xs:element name="LocationRegions" type="LocationRegionsType"/>

<xs:complexType name="LocationRegionsType">

<xs:sequence>

<xs:element ref="LocationRegion" maxOccurs="unbounded"/>

</xs:sequence>

</xs:complexType>

The <LocationRegions> element contains the following attributes and elements:

LocationRegion [Any Number]

It specifies a LocationRegion.

### x.20	Element <LocationRegion>

The <LocationRegion> element specifies a location region. The format for specifying a location region is defined in Clause 7.1.

<xs:element name="LocationRegion"  type="xs:string"/>

### x.21	Element <IPAddresses>

The <IPAddressess> element specifies a list of <IPAddresses> elements.

<xs:element name="IPAddresses" type="IPAddressesType"/>

<xs:complexType name="IPAddressesType">

<xs:sequence>

<xs:element ref="IPAddress" maxOccurs="unbounded"/>

</xs:sequence>

</xs:complexType>

The <IPAddresses> element contains the following attributes and elements:

IPAddress [Any Number]

It speifies a IPAddress.

### x.22	Element <IPAddress>

The <IPAddress> element specifies an IP address. The format for specifying an IP address is defined in Clause 7.1.

<xs:element name="IPAddress" type="IPAddressType"/>

<xs:complexType name="IPAddressType">

<xs:sequence>

<xs:element name="IPAddress" type="xs:string"/>

</xs:sequence>

<xs:attribute name="IPVersion" type="IPVersionType" use="required"/>

</xs:complexType>

### x.23	Simple Type IPVersionType

The IPVersionType simple type defines the values allowed for the IPVersion attribute of the <IPAddress> element.

<xs:simpleType name="IPVersionType">

<xs:restriction base="xs:string">

<xs:enumeration value="IPv4"/>

<xs:enumeration value="IPv6"/>

</xs:restriction>

</xs:simpleType>

### x.24	Element <Response>

The <Response> element is used by a PDP for providing an access control decision response that will be sent to a PEP as a response to an access control decision request.

<xs:element name="Response" type="ResponseType"/>

<xs:complexType name="ResponseType">

<xs:sequence>

<xs:element ref="Result"/>

</xs:sequence>

</xs:complexType>

The <Response> element contains the following attributes and elements:

Result [Required]

It provides an access control decision result.

### x.25	Element <Result>

The <Result> element represents a result of evaluating an access control policy set, access control policy or an access control policy rule.

<xs:element name="Result" type="ResultType"/>

<xs:complexType name="ResultType">

<xs:sequence>

<xs:element ref="Decision"/>

<xs:element ref="Status" minOccurs="0"/>

</xs:sequence>

</xs:complexType>

The <Resquest> element contains the following attributes and elements:

Decision [Required]

It provides the evaluation result of an access control policy set, access control policy or access control rule. Its value can be: “Permit” or “Deny”.

Status [Optional]

It provides extra information about the access control decision, for example information about an error occurring during the policy evaluation process.

### x.26	Element <Decision>

The <Decision> element contains the result of evaluating an access control policy set, access control policy or access control rule.

<xs:element name="Decision" type="xacml:DecisionType"/>

<xs:simpleType name="DecisionType">

<xs:restriction base="xs:string">

<xs:enumeration value="Permit"/>

<xs:enumeration value="Deny"/>

</xs:restriction>

</xs:simpleType>

The meanings of the <Decision> values are described in Clause 7.x.2.

### x.27	Element <Status>

The <Status> element represents the status of the access control decision result.

<xs:element name="Status" type="StatusType"/>

<xs:complexType name="StatusType">

<xs:sequence>

<xs:element ref="StatusCode" minOccurs="0"/>

<xs:element ref="StatusMessage" minOccurs="0"/>

</xs:sequence>

</xs:complexType>

The <DecisionRequest> element contains the following attributes and elements:

StatusCode [Required]

It provides a status code of an access control decision result.

StatusMessage [Optional]

It provides a status message describing the status code.

### x.28	Element <StatusCode>

The <StatusCode> element contains a status code value. The following status code values defined for this specification are the same as defined in [i.7].

<xs:element name="StatusCode" type="xacml:StatusCodeType"/>

<xs:simpleType name="StatusCodeType">

<xs:restriction base="xs:string">

<xs:enumeration value="ok"/>

<xs:enumeration value="missing-attribute"/>

<xs:enumeration value="processing-error"/>

<xs:enumeration value="syntax-error"/>

</xs:restriction>

</xs:simpleType>

The values of the <StatusCode> element have the following meanings:

ok: This identifier indicates success.

missing-attribute: This identifier indicates that all the attributes necessary to make a policy decision were not available.

processing-error: This identifier indicates that an error occurred during policy evaluation. An example would be division by zero.

syntax-error: This identifier indicates that some attribute value contained a syntax error, such as a letter in a numeric field.

### x.29	Element <StatusMessage>

The <StatusMessage> element is a free-form description of the status code.

<xs:element name="StatusMessage" type="xs:string"/>