| CHANGE REQUEST |
| --- |
| Group Name:* | SEC 12 |
| Source:* | Francois Ennesser, Gemalto (ETSI) |
| Format:* | Face-to-Face |
| Date:* | 2014-07-20 |
| Contact:* | francois.ennesser@gemalto.com |
| Reason for Change/s:* | Though a clause explaining the positioning of security procedures in the M2M sequence of events was contributed to TS_0001 (WG2), TS-0003 still lacks information on the topic. It is confusing for readers if the Security TS lacks information on how security procedures integrate with what is specified in other oneM2M TSs. |
| CR against: Release* | 1 |
| CR against: TS/TR* | TS-0003 v0.6.0 |
| Clauses/Sub Clauses* | 3.1, new clause X |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR provides information on the positioning of security procedures in the oneM2M sequence of events..

### -----------------------Start of change 1 (Definitions)----------------------------------------

# 3	Definitions and abbreviations

## 3.1	Definitions

[…]

enrolment phase: The step in the lifecycle of an M2M equipment where it becomes provisioned for operation with a specific M2M Service Provider.

operational phase: The period in the lifecycle of an M2M equipment where it is actually used for providing M2M services.

### -----------------------End of change1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

# X 	Security Integration in oneM2M flow of events

This clause specifies the integration of security process and procedures during deplotyment and operation of a oneM2M solution.

### X.1 	Interactions between layers

Before any M2M Common Services layer procedure can take place, connectivity has to be established in the underlying Network Services Layer, which may involve independent provisioning and service registration procedures specified by the underlying network.

The Service Layer Security provisioning (security pre-provisioning or security bootstrapping) and Security Association Establishment procedures specified in the present document are assumed to take place independently (and generally consecutively) to any required Network Service Layer connectivity establishment procedures.

In turn, M2M Application Service Providers may have their own security provisioning and security association establishment requirements.

### X.2 	High level sequence of events

### X.2.1 	Enrolment phase

### M2M equipments typically require provisioning and configuration phases before being put in actual operation. This may be performed by a pre-provisioning that can be integrated in the manufacturing or product deployment phase, or by means of a security bootstrapping procedure (i.e. remote security provisioning) that takes place before the equipment starts actual operation.

### At the service layer level, such provisioning and configuration is tied with selection of the stakeholders that will provide services through the equipment, especially the M2M Service Provider. This Enrolmernt phase requires contractual agreements between the stakeholders that can place constraints on deployment and operation.

### Enrolment phase may occur several times during the lifecycle of an M2M equipment, and is mainly repeated when a change in the Service Provider affects the provisioning or configuration of the equipment.

The security provisioning phase for the different layers can advantageously be combined using a common method of  security pre-provisioning or security bootstrapping.

### X.2.2 	Operational phase

#### X.2.2.1	M2M Service Access

#### AEs and CSEs seeking access to M2M services need to be mutually identified and authenticated with the M2M Service Infrastructure, in order to provide protection from unauthorized access and Denial of Service attacks. This mutual authentication enables to additionally provide integrity and confidentiality to communication between the corresponding entities.

#### This is the purpose of the Security Association Establishment procedure, which shall take place before execution of the service related procedures specified in TS-0001 for the corresponding reference point.

#### On the Mcc reference point, security association establishment between field domain CSE and IN-CSE is mandatory.

#### On the Mca reference point, security association establishment between AE and local CSE is strongly recommended.

#### The security association establishment phase of the M2M Service Layer and M2M Application Layer are generally independent from similar procedures that may be required by the Network Layer, though they may rely on the security services provided by the Network Layer.

#### X.2.2.2	Authorization to access M2M resources

### Once an AE or CSE has been granted access to M2M services, the Access Control procedure specified in Clause 7 of the present document shall be executed before accessing an M2M resource, as specified in oneM2M TS-0001 [1].

### -----------------------End of change 2---------------------------------------------