| CHANGE REQUEST |
| --- |
| Group Name:* | SEC |
| Source:* | Dragan Vujcic, Oberthur Technologies |
| Subject:* | Configuration of Protection levels |
| Date:* | 2014-07-21 |
| Contact:* | v.dragan@oberthur.com |
| Reason for Change/s:* | This CR includes the table of protection levels configuration fom TR0008 to TS0003 |
| CR against: | TS-0003 v0.6.0 |
| Clauses/Sub Clauses Affected* | 6.2.1 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To include the proposed changes to TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

### This  CR includes the the table of configuration of protection levels fom TR0008 to TS0003

### -----------------------Start of change 1-------------------------------------------

### 6.2.1	Secure Environment

The Secure Environment component is a logical entity that provides Sensitive Functions operating on Sensitive Data, Secure Storage and other resources/functions.

There is no assumption made on the particular implementation of the Secure Environment. A SE may be implemented as an independent HW Security Element or as an integrated SW function. Each Secure Environment shall be associated with one certain Security Level depending on the particular implementation of the SE. Different Secure Environments may provide different Security Levels.

The Security Levels are associated to the minimum protection level indicating desired quality of protection against attacks as in Table X.

| Protection Level | Security Level | Description |
| --- | --- | --- |
| 0 | None | No protection. The data are exposed even without active attacks. |
| 1 | Low | Low protection, data are protected from passive observers but could be exposed by active attacks, be they local or remote. E.g. software solutions exist that rely on general purpose processing hardware of the supporting equipment. |
| 2 | Medium | Medium protection, protection of the data from remote attacks is addressed, but local attacks, especially physical attacks, remain possible, ie. Medium protection provides countermeasures against software attacks only E.g. Software solutions to protect data and sensitive functions rely on specific processing providing enforced isolation and enables sensitive code and data to be kept away from an unprotected operating environment, software and memory. The code running in the protected environment is cryptographically verified for integrity assurance. |
| 3 | High | High protection, addressing both remote and local attacks to access the data, including attacks involving physical access. This includes strong counter measures against software and hardware attacks, such as detection of abnormal operating conditions and scrambling plus hardware masking of the memory and side channel analysis of operations involving sensitive data. |

Table X: Configuration of Protection levels associated to different Security lecvels

There shall be at least one Secure Environment within or accessible via the Security API, however there may be multiple.

### -----------------------End of Changes -------------