| CHANGE REQUEST |
| --- |
| Group Name:* | SEC#12 |
| Source:* | LG Electronics |
| Title | Security considerations on Application Entity |
| Date:* | 2014-07-21 |
| Contact:* | seongyoon.kim@lge.com |
| Reason for Change/s:* | Please find SEC-2014-0361 for the rationale. |
| CR against: | TS-0003 |
| Clauses/Sub Clauses Affected* | Clause 8 and sub-clauses |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree on changes to current baseline. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

Please find SEC-2014-0361 for the rationale.

R01: Remove AE Registration

R02: change clause

### -----------------------Start of change 1-------------------------------------------

# 7.X AE Impersonation Prevention

Since several AEs can behave maliciously and pretend to be another AE with their ID changed, Receiver CSE needs prevention mechanism for AE impersonation. This mechanism works at Registrar CSE since Registrar CSE is an entry point of M2M system.

When Receiver CSE receives a request, Receiver CSE shall perform as follows.

- Security association establishment is performed

- AE sends a request to Registrar CSE.

- Receiver CSE checks whether Receiver CSE is Registrar CSE (Registrar CSE finds ID associated in security association and find any <AE> resource which contains that ID in AE-ID attribute).

- If Receiver CSE is Registrar CSE, Receiver CSE checks the value in fr parameter is the same as the found ID in step 2. If the request is AE registration and fr parameter is empty string, this procedure is terminated.

- If the value is not the same, Receiver CSE sends response with impersonation error response code.

- Receiver CSE performs procedures specified in clause 8.2 [1].

### -----------------------Start of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

## 3.1	Definitions

security association establishment: sequential processing of credential configuration, association configuration and association security handshake between two entities. Credential configuration and/or association configuration can not be performed if those steps have already been executed before.

### -----------------------End of change 2---------------------------------------------