| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG4 (SEC) at TP#12 |
| Title:* | oneM2M Access Control Decision Request for Annex |
| Source:* | CATT |
| Contact: | Wei Zhou, zhouwei@catt.cn Hui Xu, xuhui@catt.cn |
| Date:* | 2014-07-28 |
| Abstract:* | Proposing a sub-clause in the Annex for describing Access Control Decision Request. |
| Agenda Item:* | TBD |
| Work item(s): | SEC WI-0007 |
| Document(s) Impacted* | oneM2M-TS-0003 Security Solutions |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0003. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

This contribution aims to propose a sub-clause in the Annex for describing Access Control Decision Request in the Security TS for release 1.

This contribution is provided according to the comments given in the SEC_11-4.

2	Proposal

Annex x (informative):
Access Control Decision Request

An access control decision request is generated by a PEP according to an Originator’s access request and extra information provided by the hosting CSE using the format specified by the PDP. The PEP can send the access control decision request to a PDP for an access control decision.

The PDP asks the PRP to retrieve all applicable access control policies according to the access control decision request, and then uses the access control decision request to evaluate the retrieved access control policies for an access control decision. An access control decision request from PEP to PDP can contain the following information:

- An Originator: It represents the ID of the Originator that sends an access request to the target resource.

- A Resource: It represents the URI of the target resource which the Originator wants to access.

- An Operation: It represents the operation which the Originator wants to perform on the target resource.

- An AccessTime: It represents the time of access.

- A LocationRegion: It represents the location of the Originator.

- An IPAddress: It represents the IP Address of the Originator.

The URI of the target resource is used to locate the target resource and then find the associated access control policies.

The ID of Originator is used to compare with the rule component subjects in order to check if a rule is applicable to the access control decision request.

The operation is used to compare with the rule component operations in order to check if the operation is permitted by the rule.

The AccessTime, LocationRegion and/or LocationRegion are used to check the rule component contexts in order to ensure some extra conditions are satisfied to using the rule for making an access control decision.