| CHANGE REQUEST |
| --- |
| Group Name:* | SEC#12 |
| Source:* | Qualcomm Inc. (TIA) |
| Format:* | Plenary |
| Date:* | 2014-07-30 |
| Contact:* | Philip Hawkes, Qualcomm, phawkes@qti.qualcomm.com, Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Reason for Change/s:* | Updates 10 .2 “TLS and DTLS Details” describing the supported versions and ciphersuites for TLS and DTLS. |
| CR against: | TS-0003 and 0.7.0 DRAFT |
| Clauses/Sub Clauses Affected* | 10.2 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Include the proposed changes in TS-0003 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Do not conflict with the content of an already approved text, by modification, deletion or the addition of an editor’s note.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

### -----------------------Start of change 1-------------------------------------------

## 10.2 TLS and DTLS Details

### 10.2.1 TLS and DTLS Versions

Where TCP payloads are to be secured, TLS v1.2 (RFC 5246 [16]) shall be used.

Where UDP payloads are to be secured, DTLS v1.2 (RFC 6347 [17]) shall be used, noting that the DTLS v1.2 ciphersuites are identical to the TLS v1.2 ciphersuites.

Implementations shall support the Server Name Indication (SNI) to indicate their authority in the SNI HostName field as defined in Section 3 of RFC 6066 [RFC6066]. This is needed so that when a host that acts as a virtual server for multiple Authorities receives a new TLS or DTLS connection, it knows which keys to use for the TLS or DTLS session.

### 10.2.2	TLS and DTLS Ciphersuites for TLS-PSK-Based Security Frameworks

The following Security Association Establishment Frameworks:

- Pre-Provisioned Symmetric Key Security Association Establishment Framework;

- MAF-Based Security Association Establishment Framework;

- GBA-Based Security Association Establishment Framework;

- Pre-Shared Key Remote Security Provisioning Framework;

- GBA-Based Remote Security Provisioning Framework;

shall use one of the key exchange algorithms defined in [15].

TLS Implementations supporting these security frameworks shall implement at least the following ciphersuites:

- TLS_PSK_WITH_AES_128_CBC_SHA256 [RFC5487].

DTLS Implementations supporting these security frameworks shall implement at least the following ciphersuites:

- TLS_PSK_WITH_AES_128_CCM_8 [31].

- The security considerations of Section 7 of RFC4279 [15] apply. In particular, applications should carefully weigh whether or not they need Perfect Forward Secrecy (PFS) and select an appropriate ciphersuite (Section 7.1 of RFC4279 [15]).

### 10.2.3	TLS and DTLS Ciphersuites for Certificate-Based Security Frameworks

The following Security Frameworks:

- Certificate-Based Security Association Establishment Framework

- Certificate-Based Security Bootstrap Framework

shall use the standard TLS v1.2 handshake (RFC 5246 [16]) with the ECDHE_ECDSA Key Exchange (RFC4492 [RFC4492]).

TLS Implementations supporting these security frameworks shall implement at least the following ciphersuite:

- TLS_ECDHE_ECDSA_WITH_AES_128_CBC_SHA256, [RFC5289].

DTLS Implementations supporting these security frameworks shall implement at least the following ciphersuite:

- TLS_ECDHE_ECDSA_WITH_AES_128_CCM, [RFC7251].

Implementations supporting these security frameworks shall support authenticating other entities using all available public key certificate flavours (see clause 8.1.1.2.1 “Public Key Certificate Flavours”)

- Raw public key certificate: using the mechanism specified in RFC 7250 [RFC7250], Implementation shall support receiving and processing raw public keys compliant with Section 9.1.3.2 “Raw Public Key Certificates” in RFC 7252 [RFC7252].

- All other certificates: X.509 certificates including device hardware identifier. Implementation shall support receiving and processing raw public keys compliant with Section 9.1.3.3 “X.509 Certificates” in RFC 7252 [RFC7252].

### ----------------------End of change 1---------------------------------------------

### -----------------------Start of Changes to References Section -------------

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

[RFC4492]			 IETF RFC 4492 “Elliptic Curve Cryptography (ECC) Cipher Suites for Transport Layer Security (TLS)”

[RFC5487]	IETF RFC 5487 “Pre-Shared Key Cipher Suites for TLS with SHA-256/384 and AES Galois Counter Mode”

[RFC7250]	 IETF RFC 7250 “Using Raw Public Keys in Transport Layer Security (TLS) and Datagram Transport Layer Security (DTLS)”

[RFC7251]	 IETF RFC 7251  “AES-CCM Elliptic Curve Cryptography (ECC) Cipher Suites for Transport Layer Security (TLS)”

[RFC7252]	 IETF RFC 7252 “The Constrained Application Protocol (CoAP)”

## 2.2	Informative references

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

### -----------------------End of Changes to References  -------------

### -Start of changes to Definitions Symbols Abbreviations Acronyms -

# 3	Definitions, symbols, abbreviations  and acronyms

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in [i.2] and the following apply:

## 3.2	Abbreviations

For the purposes of the present document, the abbreviations given in [i.2] and the following abbreviations apply:

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Does this change request avoid conflict with the content of an already approved text, by modification, deletion or the addition of an editor’s note?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change  include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

IF we do not support GBA SAEF, then delete this line