| CHANGE REQUEST |
| --- |
| Group Name:* | SEC#12 |
| Source:* | Qualcomm Inc. (TIA) |
| Format:* | Plenary |
| Date:* | 2014-07-21 |
| Contact:* | Philip Hawkes, Qualcomm, phawkes@qti.qualcomm.com, Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Reason for Change/s:* | Adds clause 10.3 listing Security Framework parameters and their descriptions. |
| CR against: | TS-0003 and 0.6.0 |
| Clauses/Sub Clauses Affected* | 10.3 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Include the proposed changes in TS-0003 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Do not conflict with the content of an already approved text, by modification, deletion or the addition of an editor’s note.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

### -----------------------Start of change 1-------------------------------------------

### 10.3 Security Framework Parameter Descriptions

| Parameter | Abbreviation (if any) | Description | Type of value |
| --- | --- | --- | --- |
| Assigned Identifier | assignedId | CSE-ID/AE-ID that the Security Association End-Point is to use with the Target End-Point | CSE-ID/AE-ID |
| Association Configuration Expiry | aCE | See clause 3.1 “Definitions” | Absolute Time (e.g. xs:time) |
| authorization frequency | authFreq | See clause 3.1 “Definitions” | Time duration (e.g. xs:duration) |
| bootstrapping transaction identifier | B-TID | See clause 3.1 “Definitions” | NAI [RFC4282]. |
| BSF Trust Anchor Certificates |  | One or more Trust Anchor Certificates to which the BSF’s certificate chains. See 3GPP 33.220 [13]. | One or more self-signed X.509 certificates |
| Enrolee Certificate and Chain |  | Enrolee’s Certificate and Certificate Chain to the Enrolee Trust Anchor Certificate. | X.509 certificate chain |
| Enrolee Certificate Information |  | Information enabling MEF to authenticate the Enrolee. Contents depend on the flavour of the Enrolee Certificate | Raw public key certificate | Enrolee Public key identifier | See relevant parameters |
|  |  |  | Device certificate | Enrolee hardware identifier and Enrolee Trust Anchor Certificate |  |
| Enrolee Identifier | Enrolee-ID | See clause 3.1 “Definitions” | CSE-ID/AE-ID |
| Enrolee Private Key |  | Enrolee’s private signing key. May be the same Certificate as used for Certificate-Based Security Association Establishment Framework, or may be a distinct certificate | ECDSA private signing key compliant with clause 10.4.1.1 |
| Enrolee Raw Public Key Certificate |  |  | Raw public key certificate compliant with clause 10.4.1.2 |
| Enrolee Trust Anchor Certificate. |  | One or more Trust Anchor Certificate for the Enrolee’s Certificate | One or more self-signed X.509 certificates |
| Enrolment Key | Ke | See clause 3.1 “Definitions” | 256-bit secret |
| Enrolment Key Identifier | KeId | See clause 3.1 “Definitions” | NAI [RFC4282] |
| Pre-Provisioned Symmetric Enrolee Key | Kpm | See clause 3.1 “Definitions” | 256-bit secret |
| Pre-Provisioned Symmetric Enrolee Key Identifier | KpmId | See clause 3.1 “Definitions” | Any value that can be used as a TLS psk_identifier [15] |
| Pre-Provisioned M2M Secure Connection Key | Kpsa | See clause 3.1 “Definitions” | 256-bit secret |
| Pre-Provisioned M2M Secure Connection Key Identifier | KpsaId | See clause 3.1 “Definitions” | Any value that can be used as a TLS psk_identifier [15] |
| MAF Certificate and Chain |  | M2M Authentication Function’s Certificate and Certificate Chain to the M2M Authentication Function’s Trust Anchor Certificate | Sequence of X.509 certificates |
| M2M Authentication Function Identifier | MAF-ID | See clause 3.2 “Abbreviations | URI |
| MAF Private Key |  | M2M Authentication Function’s Private Key | ECDSA private signing key compliant with clause 10.4.1.1 |
| MAF Trust Anchor Certificates |  | One or more Trust Anchor Certificates for M2M Authentication Function’s Certificate | X.509 certificate chain |
| Master Credential | Km | See clause 3.1 “Definitions” | 256-bit secret |
| master credential Identifier | KmId | See clause 3.1 “Definitions” | NAI [RFC4282] |
| master credential expiry | KmExpiry | See clause 3.1 “Definitions” | time (e.g. xs:time) |
| MEF Certificate and Chain |  | M2M Enrolment Function’s Certificate and Certificate Chain to the M2M Enrolment Function’s Trust Anchor Certificate | X.509 certificate chain |
| MEF Private Key |  | M2M Enrolment Function’s Private Key | ECDSA private signing key compliant with clause 10.4.1.1 |
| MEF Trust Anchor Certificates |  | One or more Trust Anchor Certificate for M2M Enrolment Function’s Certificate | One or more self-signed X.509 certificates |
| M2M Enrolment Function’s URI | MEF URI |  | URI |
| NAF Private Key |  | NAF’s Private Key. May be the same Private Key as used for Certificate-Based Security Association Establishment Framework, or may be a distinct certificate. See 3GPP 33.220 [13]. | ECDSA private signing key compliant with clause 10.4.1.1 |
| NAF Certificate and Chain |  | NAF’s Certificate and Certificate Chain to the NAF’s Trust Anchor Certificate. NAF’s Certificate shall contain NAF’s FQDN. May be the same Certificate as used for Certificate-Based Security Association Establishment Framework, or may be a distinct certificate. See 3GPP 33.220 [13]. | X.509 certificate chain |
| NAF Trust Anchor Certificates |  | One or more Trust Anchor Certificate for the NAF’s Certificate | One or more self-signed X.509 certificates |
| Relative Enrolment Key Identifier | RelativeKeId | See clause 3.1 “Definitions” | Base64 encoding of a 128-bit value |
| Target End-Point Identifier |  | CSE-ID/AE-ID of the other Security Association End-Point that a Security Association End-Point is to establish a Security Association with | CSE-ID/AE-ID |
| Target End-Point Public Key Identifier |  | An Public Key identifier that matches the public key the Target End-Point’s raw public certificate | Public Key Identifier [RFC6920] compliant with clause 10.4.2 |
| Target End-Point hardware identifier |  | An device identifier that matches a unique value in a subjectAltName field of the Target End-Point’s Certificate | FFS |
| Target End-Point Trust Anchor Certificates |  | One or more Trust Anchor Certificates to which the Target End-Point’s Certificate chains | One or more self-signed X.509 certificates |
| thisEntityRaw Public Key Certificate |  | Raw Public Key Certificate for which the Security Association End-Point possesses the private signing key |  |
| thisEntityCertificate and Chain |  | Certificate and Certificate Chain for which the Security Association End-Point possesses the private signing key | Sequence of X.509 certificates |
| thisEntityIdentifier |  | CSE-ID/AE-ID that the Security Association End-Point or Enrolee is to use with other Security Association End-Points . | CSE-ID/AE-ID |
| thisEntityPrivateKey |  | Private Key of a Security Association End-Point or Enrolee | ECDSA private signing key |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of Changes to References Section -------------

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

[RFC4282] IETC RFC 4282 “The Network Access Identifier”

## 2.2	Informative references

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

### -----------------------End of Changes to References  -------------

### -Start of changes to Definitions Symbols Abbreviations Acronyms -

# 3	Definitions, symbols, abbreviations  and acronyms

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in [i.2] and the following apply:

Network Address Identifier: the purpose of the NAI is to identify the user as well as to assist in the routing of the authentication request [RFC4282]

## 3.2	Abbreviations

For the purposes of the present document, the abbreviations given in [i.2] and the following abbreviations apply:

NAI: Network Address Identifier

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Does this change request avoid conflict with the content of an already approved text, by modification, deletion or the addition of an editor’s note?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change  include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?